## Slide 1: Flight Operations
Eric Christian
Notes: introduction

## Slide 2: Outline
Initial commissioning
Nominal operations
Instrument command loads
Instrument autonomy requirements
Flight operations staffing
Off-nominal operations

## Slide 3: Initial Commissioning
ISIS EPI-Lo and EPI-Hi Statistics Gathering and Threshold Scans
  After initial checkout it is important that ISIS instrument gather as much data as possible (especially raw event data)
  Allows instruments to populate composition tracks so that TOF vs E flux boxes (EPI-Lo) and De vs Eprime boxes (EPI-Hi) can be adjusted before perihelion
  Threshold scans to determine optimal threshold values
  6 weeks need for these activities
  EPI-Lo does not need to be on continuously
ISIS EPI-Lo and EPI-Hi Table Loads and/or Software Updates
  Table updates expected (adjustment of flux box bins) 3 weeks into statistic gathering period
  Software updates as needed
Based on STEREO experience EPI-HI will require 10-20 opportunities (on separate days) to send commands in the first two months
  Necessary to obtain/analyze at least a few hours of new data in between command opportunities to test whether the commands worked
  Therefore, need to collect data between commanding opportunities

## Slide 4: Nominal Operations
EPI-Hi and EPI-Lo operate the same whenever powered-on except for the volume/content of the data sent to the S/C inside/outside 0.25 AU
Spacecraft- Sun Distance R<0.25 AU (Normal Science Mode)
  Full nominal power
  High data collection rate
  Burst mode (EPI-Lo)
Spacecraft- Sun Distance: 0.25 AU < R (Low-rate Science Mode)
  Full power whenever possible
  Reduced data collection rate (fits within ISIS telemetry allocation)
  Commanding window should be scheduled late in the series of telemetry passes, although it may not be used every orbit
  Minimize power cycling the HV supplies
Expecting some tool to plan and coordinate operations

## Slide 5: Instrument Command Loads
Commanding of EPI-Hi and EPI-Lo
  “Flatsat” at UNH used to test command loads
    SwRI engineer will be responsible for using the native design products during Phase C to create a “behavioral model” of EPI-Hi and EPI-Lo
    Constraint Checking Modules
  Standard Commanding performed via GSEOS at UNH SOC
  Commissioning and Contingency response, commanding may optionally be done by EPI-Hi and EPI-Lo via GSEOS directly through MOC
Planning for instrument operations
  Planning software
    Automated routines & Templates for initial planning
    Interactions with ISIS SOC interfaces for finalization of planning
  Develop rough plans three orbits ahead
    Test command load
  Develop definitive plans one orbit ahead
    Final testing
    Upload

## Slide 6: Autonomy
Instrument Autonomy requirements considerably more than in initial SPP proposal and more than EPI-HI has experienced in previous missions
Main additional requirement is the ability to record the instrument state and return to that state autonomously after instrument power cycling, due to either s/c telemetry time periods or anomalous safing of instrument.
ISIS will implement operational mode changes via instrument autonomy logic supplemented by a macro capability

## Slide 7: Flight Operations Staffing
FLEXIBLE
  variability of telemetry and commanding requires flexible staffing
Priorities (in order)
  Analysis of health and safety housekeeping
  Analysis of quicklook science data to determine interesting time periods and science optimization
  Full analysis of science data and generation of data products

## Slide 8: Off-nominal Operations
Plan to avoid them
If they do occur, do whatever is necessary
  Pull in whomever is needed, when they are needed