## Slide 1: ISIS Power
David Do
Notes: introduction

## Slide 2: Outline
EPI-Lo and EPI-Hi LVPS
  Power requirements
  Block diagrams
  Circuit topologies and descriptions
  Circuit margins
  Packaging
  Thermal management
Plans for testing including bench checkout equipment
Maturity of the design (BB testing, design, analysis completed)
Preliminary parts lists and any special testing required
Summary and follow-up from peer review held prior to the instrument PDR

## Slide 3: Block Diagram
Need Update

## Slide 4: EPI-Hi Block Diagram
Need Update

## Slide 5: Environment
Operating Temp: -30°C to +60°C
Radiation: 100Krad, 82MeV

## Slide 6: Input Power Requirement
  Input voltage: 24V- 35V, 28V nominal
  1Mohm isolation minimum
  EMI/EMC
  Inrush Current
CE01& CE03 Limit
In-Rush Current Limit

## Slide 7: Power Topology
Main converter is forward with resonant reset operating at 200kHz. Efficiency is >80%.
Digital voltages are linear regulated
Bulk high voltage is set at 3.5kV
High voltages of up to 3.4kV are controlled through Optocouplers

## Slide 8: EPI-Lo Output Requirement
 | Outputs Regulation | Min Load (mA) | Nom Load (mA) | Max Load (mA)
+1.5V | ±3% | 45 | 80 | 200
+3.3V | ±3% | 150 | 200 | 460
+5V | ±5% | 115 | 135 | 160
+13V | ±5% | 10 | 63 | 90

## Slide 9: Sensor Voltages
MCP
Anode/Preamp
MCP
+3200V
HVPS Out +3400V
+ 900V
MCP Return is a ground reference at HVPS (allows MCP current measurement across resistor)
SSD
900V (total diode drop)
200V
+3400V
1000V
Grounded Foils
Collimators
MCP return
Tecan Grid
100V

## Slide 10: EPI-Lo HVPS
 | Max Output Voltage (V) | Min Load (uA) | Max Load (uA)
Bias | 200 | 0 | 20
Bulk | 3500 | 0 | 200
HVPS | 3400 | 0 | 40
Grid | 1000 | 0 | 1
MCP | 900 | 0 | 40

## Slide 11: EPI-Hi Output Requirements
 | Output Regulation | Min Load (mA) | Nom Load (mA) | Max Load (mA)
+1.5V | ±2.5% | 50 | 100 | 150
+1.8V | ±2.5% | 20 | 40 | 60
+3.3V | ±2.5% | 145 | 287 | 430
+6V | ±5% | 79 | 338 | 500
+12V | ±7% | 8 | 16 | 64
-6V | ±7% | 6 | 12.6 | 19

## Slide 12: Thermal Analysis

## Slide 13: LVDS Fault Mitigation
Transformer: primary and 3.3V winding is well isolated
+3.3V is linear regulated from +3.5V
+3.5V is monitored on housekeeping

## Slide 14: Packaging

## Slide 15: Peer Reviews
EPI-Hi LVPS: May 2013
EPI-Lo Power: Aug 2013
Major Action Items:
  EPI-Hi:
    Shielding over switching circuits
    Output Loads
    Output Regulations
  EPI-Lo:
    MCP voltage accuracy
    LVDS fault mitigation
    Bias Voltage Zener diode protection

## Slide 16: Breadboard Testings

## Slide 17: Analysis
Preliminary EMI completed
Worst Case analysis for digital voltages completed

## Slide 18: EPI-Lo EMI Analysis
Primary Current in Discrete Time
Primary Current in CFFT
CE03 Limit
EMI Filter Attenuation