## Slide 1: EMI / EMC
Reid Gurnee
Notes: introduction

## Slide 2: Outline
EMI/EMC requirements and specifications as well as descriptions of design mitigations to meet these requirements
Include the deep dielectric discharge mitigation approach
Testing to be performed to verify compliance and when the testing will take place

## Slide 3: EMC Design Considerations
Power supplies crystal controlled to a frequency window centered at n*50 kHz with n>=3 and 500 ppm wide over all operating conditions and time.
Place any transformers or big inductors as far from Box walls as possible.
Stable currents to minimize changes in Magnetic Emissions
Control all current paths inside your box to minimize loop area. Cannot use a solid return plane if a trace is the source. Any circuit over 100 milliamps AC or 1 amp DC must be analyzed
All Cables outside the metal box must be twisted shielded with 360 shields terminated to the Box with less than 20 mOhms.
EMI Backshells not required by EME but shield must cover connector fully
Connector shell to Box resistance before mated < 5 mOhms
Any cable outside the spacecraft body attached to a device must have either 13 mils shielding or DDD first circuit protection
All use of Magnetic Materials (Nickel, 400 Series CRSS, etc) must be identified and approved by the project. High Phosphor Nickel coating is allowed because it is not magnetic.
I will add to these slides to show how we plan to meet these

## Slide 4: EMC Grounding
Primary power supplies isolated by >1 MΩ from everything
Secondary power supply returns tied to chassis with <2.5 mΩ in only the Box using the power. (RIO’s excepted)
Grounding Diagrams will show all chassis grounds, primary and secondary power feeds and returns, shields, and signals with returns
ID all connector pins with first circuits
Connectors unused in flight shall have a conductive cover with less that 10 mW from cover to Box chassis
“Conductive” Box exterior
Box design must be at least tongue and groove. EMI gaskets on flat joints is acceptable.
I will add to these slides to show how we plan to meet these

## Slide 5: EMC Testing
Early Testing (Breadboard, Card level, Engineering Model (EM)) can identify a problem when it can still be fixed without major schedule slip.
Doing conducted emissions (CE) can find most issues.
EM Testing can be used to reduce testing on the FM if the EM passed and is close to flight like. A list of all differences must be supplied prior to approval of FM test procedure. CE and Mag testing required on every unit.
The conducted emissions of the EM and the FM must be the same. If not, FM testing may be required.
Required Tests: Bonding & Isolation
Conducted Emissions: CE-01, CE-02, CE-07
Conducted Susceptibility: CS-01, CS-02, CS-06
Radiated Emissions: RE-01, RE-02, Mag Sniff
Radiated Susceptibility: RS-03, ESD
I will add to these slides to show how we plan to meet these