## Slide 1: ISIS Thermal
Gregory J Dirks
Notes: introduction

## Slide 2: Outline
Driving Instrument Thermal Requirements
Thermal Design and Implementation
  Thermal Management
  Heaters and Sensors
  MLI Design
  Materials and Finishes
Predicted Performance and Margins
  Thermal Model Details
  Design Cases
  Optical Properties
  Predictions and Margins
Plans for Thermal Verification

## Slide 3: Requirements
Design Temperature Limits
EPI-Hi EPI-Lo
Margin Guidelines – Includes Test and Model Uncertainty
  Hot Limits 10 C and Cold Limits 5 C (Heater Controlled)
Component | Hot Op. (°C) | Cold Op. (°C) | Cold Surv. (°C)
EPI-HI HET | 40 | -25 | -40
EPI-Hi LET1 | 40 | -25 | -40
EPI-Hi LET2 | 40 | -25 | -40
EPI-Hi DPU | 40 | -25 | -40
EPI-Hi Bias | 40 | -25 | -40
EPI-Hi LVPS | 40 | -25 | -40
EPI-Hi HET Tel | 30 | -25 | -40
EPI-Hi LET 1 Tel | 30 | -25 | -40
EPI-Hi LET 2 Tel | 30 | -25 | -40
Component | Hot Op. (°C) | Cold Op. (°C) | Cold Surv. (°C)
Detector | 35 | -30 | -45
Anode Board | 55 | -30 | -45
Event Board | 55 | -30 | -45
Power Board | 55 | -30 | -45
Dome | 35 | -30 | -45

## Slide 4: Requirements
Interface Temperatures
  Operational: -25 / +65 C
  Non-Operational: -30 / +70 C
Heaters
  75% Maximum Duty Cycle
  Resistance Determined at 26 V

## Slide 5: Design
EPI-Hi
  E-box Radiator to Dissipate Internally Generated Heat
  Telescopes Conductively Isolated from E-box
  Operational Heaters on Telescopes
  Survival Heaters on Telescopes and E-box
  MLI on Surfaces Except Apertures and Radiators
E-Box
Circuit Boards
Telescopes
Radiator Surface

## Slide 6: Design
EPI-Lo
  Wedge Radiators (8) to Dissipate Internally Generated Heat
  Eight Survival Heaters (One on Each Wedge)
  MLI on Surfaces Except Apertures and Radiators

## Slide 7: Design
ISIS
  EPI-Hi and EPI-Lo are Thermally Isolated from the Bracket
  Bracket is Thermally Isolated from the S/C

## Slide 8: Heaters and Sensors
EPI-Hi Heater Operations
  One S/C Thermistor on Each Telescope and Two S/C Thermistors on E-box (Primary and Redundant)
  Operational Heaters on Each Telescope are on One S/C Service, but Controlled by E-box
  Survival Heaters on Each Telescope and the E-Box are on One S/C Service and Controlled by S/C with Sense Location Currently Baselined as the E-box
  Survival Heaters Also Used to Warm Instrument to Cold Operational Temperature for Cold Turn On by using Different Set Points

## Slide 9: Heaters and Sensors
EPI-Lo Heater Operations
  Two (Primary and Redundant) S/C Thermistors on Dome for Heater Control and One More (To Be Positioned)
  Survival Heaters on One S/C Service (Separate from EPI-Hi) Controlled by S/C with Sense Location Currently Baselined as One of the Wedges
  Survival Heaters are Used to Warm Instrument to Cold Operational Temperature for Cold Turn On by Using Different Set Points
  Survival Heaters are Also Used to Maintain Minimum Cold Operating Temperature During Low Power Operating Conditions
Summary
  One S/C Operational Heater Service (EPI-Hi)
  Two S/C Survival Heater Services
  Eight total (5 EPI-Hi and 3 EPI-Lo) S/C Thermistors

## Slide 10: MLI
Coverage
  Entire Instrument (Including Underneath) Other than Apertures and Radiators
Specifications
  Each Separate Blanket Grounded with Wire to S/C
  Vented Using Edge Mesh Screens Directed away from Apertures
  Edges and Seams Sealed using GBK Tape
  Blankets Secured using G-10 Buttons and SS Snap Rings

## Slide 11: Materials and Finishes
Radiators
  Z-93Z55 Conductive White Coating
MLI
  Germanium Black Kapton (GBK)
Apertures
  EPI-Hi: TBD
  EPI-Lo: TBD
Thermal Isolators
  G-10 Fiberglass

## Slide 12: Thermal Model
EPI-Hi Modeled by Vertex Aerospace
  Rommel Zara and Santino Rosanova
EPI-Lo Modeled by APL
  Shawn Begley
Bracket Modeled by Vertex Aerospace
ISIS Model Integrated by Vertex Aerospace
All Models Created using Thermal Desktop Software
Pre-PDR Model Delivered to S/C in June
Good Correlation between Instrument and S/C Results

## Slide 13: Design Cases
Hot Operational
  0.TBD AU with +65 C I/F Temperature
  EOL Power and Optical Properties
  Low MLI e* = 0.03
Cold Operational
  0.TBD AU with -25 C I/F Temperature
  BOL Power and Optical Properties
  High MLI e* = 0.05
Cold Non-Operational
  0.TBD AU with -30 I/F Temperature
  BOL Optical Properties and e* = 0.05
Hot Non-Operational
  0.TBD AU with +70 I/F Temperature
  EOL Optical Properties and e* = 0.03

## Slide 14: Optical Properties
Radiator: Z-93Z55 White Coating
  BOL: a = 0.20, e = 0.90
  EOL: a = 0.45, e = 0.90
MLI Exterior: GBK
  BOL: a = 0.49, e = 0.81
  EOL: a = 0.55, e = 0.78

## Slide 15: Predictions
Component | Limit (°C) | Predict (°C) | Margin (°C)
EPI-HI HET | 40 | 29.2 | 10.8
EPI-Hi LET1 | 40 | 29.3 | 10.7
EPI-Hi LET2 | 40 | 27.9 | 12.0
EPI-Hi DPU | 40 | 28.4 | 11.6
EPI-Hi Bias | 40 | 28.4 | 11.6
EPI-Hi LVPS | 40 | 29.9 | 10.0
EPI-Hi HET Tel | 30 | 3.5 | 26.5
EPI-Hi LET 1 Tel | 30 | -15.3 | 45.3
EPI-Hi LET 2 Tel | 30 | -1.2 | 31.2
EPI-Hi Hot Operational

## Slide 16: Predictions
EPI-Hi Cold Operational
Component | Limit (°C) | Predict (°C) | Margin (°C)
EPI-HI HET | -25 | -6.76 | 18.24
EPI-Hi LET1 | -25 | -6.73 | 18.27
EPI-Hi LET2 | -25 | -8.58 | 16.42
EPI-Hi DPU | -25 | -7.99 | 17.01
EPI-Hi Bias | -25 | -7.32 | 17.68
EPI-Hi LVPS | -25 | -6.55 | 18.45
EPI-Hi HET Tel | -25 | -20 | 5
EPI-Hi LET 1 Tel | -25 | -20 | 5
EPI-Hi LET 2 Tel | -25 | -20 | 5
Heater Location | Heater Power(W)
EPI-Hi HET TEL | 0
EPI-Hi LET1 TEL | 0.35
EPI-Hi LET2TEL | 0.13
TOTAL | 0.48

## Slide 17: Predictions
EPI-Hi Cold Non-Operational
Heater Location | Heater Power (W)
EPI-Hi EBOX | 2.78
LET 1 Telescope | 0.47
LET 2 Telescope | 0.35
HET Telescope | 0.21
TOTAL | 3.81

## Slide 18: Predictions
EPI-Hi Cold Non-Operational Temperatures

## Slide 19: Predictions
EPI-Hi Hot Non Operational

## Slide 20: Predictions
EPI-Lo Hot Operational
Component | Limit (°C) | Predict (°C) | Margin (°C)
Detector | 35 | 24.62 | 10.4
Electronics | 55 | 33.01 | 21.99

## Slide 21: Predictions
EPI-Lo Cold Operational
Component | Limit (°C) | Predict (°C) | Margin (°C)
Detector | -30 | -20.65 | 9.35
Electronics | -30 | -13.39 | 16.61

## Slide 22: Predictions
EPI-Lo Cold Non Operational
Component | Limit (°C) | Predict (°C) | Margin (°C)
Detector | -45 | -40.24 | 4.76
Anode Board | -45 | -41.28 | 3.72
Event Board | -45 | -41.17 | 3.83
Power Board | -45 | -41.27 | 3.73
Dome | -45 | -40 | 5
 | Heater Power (W)
EPI-Lo Surv Heater | 2.45

## Slide 23: Predictions
EPI-Lo Hot Non Operational