## Slide 1: ISIS Power
David Do
Notes: introduction

## Slide 2: EPI-Hi Electronics Overview

## Slide 3: EPI-Lo Electronics Overview
Event Board
Power Board
Anode Boards (x4)
Energy Boards (x8)

## Slide 4: EPI-Hi Block Diagram

## Slide 5: EPI-Lo Block Diagram

## Slide 6: Environment Requirements
Thermal
  Survival is -55°C to +85°C
  Operational is -35°C to +65°C
Radiation
  25 krad (includes RDM=2 from FASTrad analysis)
  LET > 80 MeV*cm2/mg

## Slide 7: LVPS Major Input Requirements
Requirements from Solar Probe Bus
Input Specification
  Operate over bus voltage of 22 to 35V
  Survive any standing or fluctuating voltage from 0 to 40V
  Meet EMI/EMC
  Transformer and power inductor far away from wall
  Power supplies crystal controlled to a frequency window centered at n*50 kHz with n>=3 and 500 ppm wide over all operating conditions and time.
  Inrush current limit
  Primary Secondary isolation >1MOhm
  Overall efficiency > 70%

## Slide 8: Input Power Requirement
  EMI/EMC
  Inrush Current
CE01& CE03 Limit
In-Rush Current Limit

## Slide 9: Interface
EPI-Hi
  Input connector: MWDM2L-9SCBRR2-.110-429
  Output connector: 891-008-51PSBRT1T-429TH
EPI-Lo
  Input connector: MWDM_L-9SSMR
  Inter board connector: 891-008-51PSBRT1T-429
  Safing connector: 803-005-07M5-3EN
  Bias voltage connector: 09-9001-1
  High voltage: Pig tails

## Slide 10: Power Topology
Common for EPI-Hi and EPI-Lo:
  Main converter is forward with resonant reset operating at 200kHz. Efficiency is >80%.
  Digital voltages are linear regulated
EPI-Lo HVPS:
  Bulk high voltage is set at 3.4kV
  High voltages of up to 3.3kV are controlled through Opto-couplers
  Bias voltage is up to 200V

## Slide 11: Output Requirements
EPI-Hi:
  Generate low voltages: +12V, +6V, +3.3V, +1.8V, +1.5V & -6V
  Primary input current telemetry
  Temp sensor
  Provide path for Op-heater voltage
EPI-Lo:
  Generate low voltages: +13V, +5V, +3.3V and +1.5V
  House keeping through ADC for primary input current, temperature, output currents and output voltages
  Generate high voltages and bias voltages to sensors
  Hard and soft high voltage safing

## Slide 12: EPI-Hi Output Requirements
 | Output Regulation | Min Load (mA) | Nom Load (mA) | Max Load (mA)
+1.53V | ±2.5% | 50 | 100 | 150
+1.82V | ±2.5% | 20 | 40 | 60
+3.41V | ±2.5% | 145 | 287 | 430
+6V | ±7% | 79 | 338 | 500
+12V | ±7% | 8 | 16 | 64
-6V | ±5% | 6 | 12.6 | 19

## Slide 13: EPI-Lo Output Requirement
 | Outputs Regulation | Min Load (mA) | Nom Load (mA) | Max Load (mA)
+1.5V | ±3% | 45 | 80 | 200
+3.3V | ±3% | 150 | 200 | 460
+5V | ±5% | 115 | 135 | 160
+13V | ±5% | 10 | 63 | 90

## Slide 14: Sensor Voltages
MCP
Anode/Preamp
MCP
+2900V
HVPS Out +3300V Max
+ 900V
MCP Return is a ground reference at HVPS (allows MCP current measurement across resistor)
SSD
900V (total diode drop)
100V
+3000V
1000V
Grounded Foils
Collimators
MCP return
Tecan Grid
100V

## Slide 15: EPI-Lo HVPS Requirements
 | Max Output Voltage (V) | Min Load (uA) | Max Load (uA)
Bias | 200 | 0 | 20
Bulk | 3400 | 0 | 250
HVPS | 3300 | 0 | 50
Grid | 1000 | 0 | 1
MCP | 900 | 0 | 50

## Slide 16: HVPS Current Limit
Control range: 0uA to 200uA
Control granularity: <1uA
Response time: <1ms
LVPS sends over-current signal to event board
Event board turns off high voltage output and resets DAC

## Slide 17: LVDS Fault Mitigation
Transformer: primary and +3.3V winding is well isolated by +13V and +6V windings
+3.3V is linear regulated from +3.6V
Linear pass transistor is rated for 100V
Worse case fault LVPS goes to full duty cycle which results in +7.5V output on +3.6V
Preliminary thermal analysis shows 33°C rise in linear regulator
DC/DC
Linear
+3.6V
+3.3V

## Slide 18: Worst Case Thermal Analysis
6oz Cu in PWB
Thermal contours plot shown with 8W total power dissipation
Actual power dissipation <2.5W
TO-254 temps for 6oz
  Junction = 32.8°C
  Case = 13.2°C

## Slide 19: EPI-Hi Package
Top Shields
LVPS Board
Bottom Shields
Chassis

## Slide 20: EPI-Lo Packaging
Packaged in octagon frame
2 daughter boards for high voltages
Stiffener goes across the board
Power dissipation is estimated <2.5W
Safing
Interconnect
Input

## Slide 21: EPI-Hi Board Layout
Input
Output
Secondary Shield
Primary
Shield
XFORMER

## Slide 22: EPI-Lo Board Placement
LVPS
HVPS
XFORMER

## Slide 23: Nominal Output Regulation and Efficiency
 | Load(A) | Regulation(V) | Power(W)
+1.53V | 0.14 | 1.505 | 0.2107
+3.41V | 0.287 | 3.69* | 0.9758
+6V | 0.338 | 5.97 | 2.01786
+12V | 0.016 | 11.98 | 0.19168
-6V | 0.012 | 5.95 | 0.0714
input | 0.159 | 28 | 4.452
 |  |  | 78%
*+3.41V shown pre-regulated. Efficiency is calculated using +3.4V.
+3.41V and +1.82V linear regulator have same design as +1.53V.

## Slide 24: Analysis
Preliminary EMI completed
WCA for digital voltages regulation = ±2.3%

## Slide 25: Voltage Regulation WCA Method and Assumptions
WCA Method
  Extreme Value Analysis in Mathcad
Temperature Range
  -35C to +65C operational
Resistors Variation
  K resistors are 100 ppm (0.8%) + 1% initial tolerance + 2% Aging ≈ 4%
  E resistors are 25 ppm (0.2%) + 0.1% initial tolerance + 1% Aging ≈ 1.3%
  Z resistor are 5ppm(0.04%)+ 0.01% initial tolerance 0.16% Aging ≈ 0.2%
RH1078
  100Krad data from datasheet
PWM5302S
  100Krad data from datasheet

## Slide 26: EPI-Lo EMI Analysis
Primary Current in Discrete Time
Primary Current in CFFT
CE03 Limit
EMI Filter Attenuation

## Slide 27: Parts
All parts are rad-hard to >100krad
Parts submitted to PCB. No issues expected.
Part Number | Description | Manufacture
PWM3052S | PWM IC | Aeroflex
ADC128S102QML | 12 Bit-ADC | TI
RH1009MW | 2.5V Reference | Linear Tech
RH1078MW | Low power Opamp | Linear Tech
M49470X01335KBB | Stacked 3.3uF Ceramic | Presidio
IRHNM57110 | 100V N Channel FET | IR
JANSR1N5811US | 100V Schottky Diode | Microsemi
JANSR2N2222AUB | NPN transistor | Microsemi
JANSR2N3501UB | NPN transistor | Microsemi
66353 | High voltage opto | Micropac
ADCMP600 | Comparator | Analog Devices

## Slide 28: Plans for Testing
Follows APL Manufacturing Flow, these are significant highlights
  Populate Passive Components with Automatic Measurement.
  Populate Actives and Install Known Tailors or Tailor Flags
  Install into Flight Frame
  Execute Test Procedure to Test and Tailor Entire Board
  ESS Testing
  Execute Functional Test Procedure
  Photograph and Conformal Coat
  Execute Test Procedure to Calibrate and Characterize Board (over temperature)
  Release to Next Assembly

## Slide 29: Status Summary
EPI-Hi
  EM PWB is being fabricated
EPI-Lo
  EM is in placement & layout phase

## Slide 30: Plan Forward
EPI-Hi
  Complete testing EM
  Fabricate flight
EPI-Lo
  Fabricate and complete testing EM
  Fabricate flight
Finalize all documentation and procedures for flight build
Build, tailor, calibrate, and qualify flight units

## Slide 31: Peer Reviews
EPI-Hi LVPS: May 2013, 27AI all closed SRI-13-026
EPI-Lo Power: Aug 2013, 5 AI all closed SRI-13-029
Major Action Items:
  EPI-Hi:
    Shielding over switching circuits
    Output loads
    Output regulations
  EPI-Lo:
    MCP voltage accuracy
    LVDS fault mitigation
    Bias Voltage Zener diode protection