## Slide 1: ISIS Overview
Scott Weidner
ISIS PM (SwRI)
This document contains technical data that may be controlled by the International Traffic in Arms Regulations (22 CFR 120-130) and may not be provided, disclosed or transferred in any manner to any person, whether in the U.S. or abroad, who is not 1) a citizen of the United States, 2) a lawful permanent resident of the United States, or 3) a protected individual as defined by 8 USC 1324b(a)(3), without the written permission of the United States Department of State.
Notes: introduction

## Slide 2: Outline
ISIS Organization Chart
ISIS Suite
Spacecraft Accommodation
Changes since MDR
Development Status
Summary

## Slide 3: ISIS Team

## Slide 4: ISIS Suite
ISIS Energetic Particle Suite
  Measures energetic particles, including electrons, protons, and heavy ions
Two instruments for wide energy coverage
  EPI-Hi (Caltech, JPL, & GSFC)
  EPI-Lo (JHU/APL)
ISIS Allocations
  Mass: 9.383 kg
  Power: 11.768 W
  Telemetry: 12 Gbit/orbit
EPI-Lo
EPI-Hi
ISIS
Bracket

## Slide 5: ISIS EPI-Hi
Three Telescopes
  HET – High energy
  LET1 – Low energy
  LET2 – Low energy, single-ended
Energy Range
  Ions:
    1 MeV/nucleon – 50 MeV/nucleon
  Electrons:
    0.5 MeV – 3 MeV
FOV: ≥π/2 sr in sunward and anti-sunward hemispheres (incl. 10°from S/C-Sun line)
Electronics
Box
LET2
LET1
HET

## Slide 6: ISIS EPI-Lo
8 Wedges configured in 4 independent quadrants
Energy Range
  Ions:
    50 keV/nucleon –
    15,000 keV Total E
  Electrons:
    50 – 500 keV
Nearly 2-π FOV
Sensor
Wedges
Electronics
Housing

## Slide 7: Spacecraft Accommodation

## Slide 8: Late-Breaking Trade with the S/C
New Solar Limb sensor appeared in S/C model near ISIS
Analysis of the effect on our FOV is on-going
No “show stoppers” expected but analysis and accommodation needs to be completed
Working the process-issues with the Spacecraft team

## Slide 9: Changes Since MDR
No changes to Science
EPI-Lo electronics box reduced in diameter and fits inside the ISIS bracket
Updated design for EPI-Hi electronics box
ISIS bracket modified to accommodate the Ebox changes
Mass increased as part of risk-reduction process run by the SPP spacecraft when the nominal orbit was modified
Power and telemetry have held steady with some reductions in uncertainty
Two small additions
  EPI-Hi added a background pixel
  EPI-Lo added an anti-coincidence detector
  Both of these use spare resources of existing electronics and provide large payoff for dynamic range

## Slide 10: Development Status
Successfully completed TRL6 Technology Developments
Developed requirements flow-down with SPP Spacecraft
ICDs with the Spacecraft are signed-off
Preliminary analyses completed
Prototypes of new circuits have been built and tested
Completed preliminary designs
  In most areas we are right on track
  In some areas we are beyond a PDR-level and EM fabrication is underway
Five different ASICs within ISIS
  All have completed EM build or FM build
We’ve brought in coast-to-coast teams to help Peer Review details of each subsystem

## Slide 11: Summary
In Phase B, the ISIS team has completed definition, preliminary design, and analysis work for the suite
The presentations ahead will be taking you through all of the details
We look forward to your feedback on our plans and preliminary designs