## Slide 1: EPI-Lo Software
John Hayes
EPI-Lo FSW Lead (JHU/APL)
This document contains technical data that may be controlled by the International Traffic in Arms Regulations (22 CFR 120-130) and may not be provided, disclosed or transferred in any manner to any person, whether in the U.S. or abroad, who is not 1) a citizen of the United States, 2) a lawful permanent resident of the United States, or 3) a protected individual as defined by 8 USC 1324b(a)(3), without the written permission of the United States Department of State.

## Slide 2: Outline
Common Software
SPP Host Software
EPI-Lo Application Software
EPI-Lo Boot Software
Software Development Environment
Summary

## Slide 3: Common Software
Packet telemetry
Command handling
Macros (stored command sequences)
Memory management
Monitoring and alarm generation
Status reporting

## Slide 4: Common Software Reuse
Common software reuse estimates for EPI-Lo
  ~50% of application
  >90% of boot
Common software currently (or soon to be) in flight:
  MESSENGER: EPPS, GRS, MAG, MASCS, MDIS, NS, and XRS
  MRO: CRISM
  New Horizons: LORRI and PEPSSI
  Pucks: Juno/JEDI, RBSP/RBSPICE, MMS/EIS (2014)
  BepiColombo/Strofio (2015)
  Solar Orbiter/SIS (2017)
Automated regression test for common software (and for boot software)

## Slide 5: SPP Spacecraft Interface Software
Command and telemetry use 115200 baud UART protocol, 8 data bits plus odd parity
Virtual 1PPS, i.e. falling edge of start bit of first byte in command ITF
Redundant interface, side A vs. side B
  Command arrival determines active side; telemetry sent only to that side
  Dynamic side switching supported
Interrupt driven: per-byte interrupt for command and telemetry, and side A and B 1PPS interrupts

## Slide 6: SPP Host S/W – EPI-Lo to S/C
Telemetry ITF
  Variable length up to 8196 bytes (EPI-Lo limits to 2060 bytes)
  Multiple telemetry ITFs can be sent but cannot straddle 1PPS (EPI-Lo sends one per second)
  Frame header includes sync pattern, length, etc.; checksum at end of frame
  Frame transmission synchronized to 1PPS
CCSDS telemetry packets
  Variable length, up to 4096 bytes (including headers)
  Zero to many packets per frame
  Packets can straddle frames
  64 APIDs available
  Critical housekeeping packet

## Slide 7: SPP Host S/W – Critical Housekeeping
Critical housekeeping packet sent once per second
  May optionally be sent to the SSR
  If so, it counts against telemetry volume allocation
Contains 32 bits of TBD data to share with other instruments
Contains 8 bytes of housekeeping data
  Data is included in spacecraft-generated combined instrument critical housekeeping packet
  Data is NOT monitored by spacecraft autonomy
Contains bits to request power off or power cycle, set via EPI-Lo command:
  EPILO_SAF_OFF: Request power off
  EPILO_SAF_CYCLE: Request power cycle

## Slide 8: SPP Host S/W – S/C to EPI-Lo
Command ITF
  Variable length up to 512 bytes
  S/C sends one command ITF per second
  Frame header includes sync pattern, length, etc.; checksum at end of frame
  Frame transmission synchronized to 1PPS
CCSDS telecommand packets
  Variable length, up to 362 (TBD) bytes (including headers)
  One to many packets per frame
    S/C time and status (telemetry) packet sent every second, always first
    Zero or more command packets
  Packets cannot straddle frames
  Secondary header is optional (EPI-Lo does not use)
  64 APIDs available (EPI-Lo uses one)
If command ITF is not received for a commandable number of seconds, EPI-Lo runs its safing macro

## Slide 9: SPP Host S/W – Time Keeping
Time is set by spacecraft
  32-bit MET (seconds)
  Time arrives every second (as part of time and status)
  Virtual 1PPS from S/C generates interrupt; interrupt routine sets time, converted to milliseconds
Time is updated by EPI-Lo
  1000 Hz interrupt routine updates time
  Common software telemetry and command processes run at 1PPS, use coarse (1 s. resolution) time tags
  Science can be tagged with TBD finer resolution

## Slide 10: EPI-Lo Application Software
Subsystems
  MCP HV
  SSD bias
  Time-of-flight and angle/position measurement (in backup)
  Energy measurement (in backup)
  Event analysis (in backup)
Data Collection
  Science products
  Ancillary products
  Integration control
Miscellaneous
  DACs and ADCs (in backup)
  Autonomous operation

## Slide 11: EPI-Lo Application S/W – MCP HV
EPI-Lo software controls MCPs’ High Voltage (HV) common supply (bulk) and four individual HVs (opto-isolator controlled)
EPI-Lo software slowly ramps voltages to commanded levels
At least two commands are required to turn on HV
There are also commands to control current monitors implemented in hardware
Commands:
  EPILO_HV_COM_LEVEL: Set Common High Voltage Supply Level
  EPILO_HV_COM_LIMIT: Set Common High Voltage Supply Limit
  EPILO_HV_MCP_LEVEL: Set MCP High Voltage Supply Level
  EPILO_HV_MCP_LIMIT: Set MCP High Voltage Supply Limit
  EPILO_HV_MCP_STEP: Step MCP High Voltage Supply Level
  EPILO_HV_CUR_ENB: Enable/Disable MCP HV Current Monitoring
  EPILO_HV_CUR_LIMIT: Set MCP HV Current Monitoring Limit

## Slide 12: EPI-Lo Application S/W – SSD Bias
EPI-Lo software controls SSDs’ Bias Voltage (BV) supply
EPI-Lo software slowly ramps the supply voltage to commanded level
At least two commands are required to turn on bias supply
Commands:
  EPILO_BV_LEVEL: Set SSD Bias Supply Level
  EPILO_BV_LIMIT: Set SSD Bias Supply Limit
  EPILO_BV_STEP: Step SSD Bias Supply Level

## Slide 13: EPI-Lo Application S/W – Science Products
Ions are collected with different energy resolution, angular (position) resolution, and cadence
  Ions - Fast: 8 angles, 8 energies
  Ions - Slow: 80 angles, 69 energies (29 H, 12 He, 14 Heavy group 1, and 14 Heavy group 2)
Electrons are collected with different resolution and cadence
  Electrons - Fast: 8 angles, 6 energies
  Electrons - Slow - Regular: 8 angles, 32 energies
  Electrons - Slow - Hi-Angle: 80 angles, 16 energies

## Slide 14: EPI-Lo Application S/W – Ancillary Products
Basic rates (i.e. singles) are collected
  Hardware counters, e.g. SSD, Start1, Start2, Stop, Events queued, etc.,
    24-bit hardware counters accumulated in 32-bit software counters
    Collected per-quadrant or octant
  Software counters, e.g. Events processed
Single events
  Software reads events from hardware FIFO
  A commandable number collected in raw event product

## Slide 15: EPI-Lo Application S/W - Integration Control
EPI-Lo software defines data products as fast or slow
The time to integrate fast and slow data is commandable
Each data product can be individually enabled or disabled
Commands
  EPILO_DAT_COLLECT - Set Data Collection Pattern
  EPILO_DAT_ENB - Enable/Disable Data Products
  EPILO_DAT_RAW - Control Amount of Raw Event Data
  EPILO_DAT_TIME - Control Data Integration Time

## Slide 16: EPI-Lo Application S/W – Autonomous Operations
Common-code macro capability support definition, execution, and save/restore of command sequences
  Macros can pause until a given MET or delay a given number of seconds
  Macros can contain do-loops, calls and “forks” to other macros
Time and status from spacecraft includes
  Startup Mode: selects manual vs. autonomous operation
  Solar Distance: current distance to the Sun and in vs. outbound
If autonomous operation is selected, EPI-Lo software will:
  Automatically load macros from MRAM
  Run startup macro; this ramps up HVs, etc.
  Monitor solar distance against a set of commandable thresholds
    Different threshold crossings trigger different macros to run
    Macros configure science collection, e.g. integration times, etc.
If autonomous operation is not selected, EPI-Lo software will wait for commands

## Slide 17: EPI-Lo Boot S/W
Commands: memory load, copy, execute, dump, check, plus boot from MRAM
Telemetry: status/housekeeping, memory dump, etc.
High (>95%) code reuse:
  SPP I/F from application
  Common software (subset)
  Boot software (boot programs from MRAM)
New: wrapper, startup, etc.
  If autonomous operation is selected, EPI-Lo boot software will automatically try to boot a series of programs from MRAM
  If autonomous operation is not selected, EPI-Lo boot software will wait for commands

## Slide 18: Software Development Environment
Flight software and development tools are on Space Department’s Unix system
  /project/spp-instr
  Backed up nightly
  Tools are C-based and have been used on Sun OS, Linux, & Mac OS X
  Only single developer can modify software
Software versions
  Numbered with integers, i.e. 1, 2, 3, etc.
  Each version is in a subdirectory; name of subdirectory includes version number
  Version number reported in telemetry
  Each delivered version includes snapshot of libraries
  Archived in Product Lifecycle Management (PLM) system
Testing
  Unit and integration testing done on Xilinx prototype board (no sensor); concocted events are in RAM
  Further testing on EM with pulsers simulating events
  Acceptance testing is done as part of Instrument Test Procedure

## Slide 19: Summary
EPI-Lo application software
  EPI-Lo-specific software - new code
  Common software - reused code, ~50% of application
  SPP spacecraft interface software - new code, but derived from RBSP interface code
EPI-Lo boot software, >95% reused code

## Slide 20: Backup

## Slide 21: Common S/W - Packet Telemetry
Provides standard API to application
  Delivers variable-length packets
  Numeric ID identifies packet type/contents
  Time tag of data collection time
API also used within common code to deliver standard products:
  Memory dump, memory checksum, etc.
  Command echo
  Alarm
  Status/housekeeping

## Slide 22: Common S/W - Commands
Standard API for “clients” to register commands:
  Numeric “opcode” and expected number of arguments
  Pointer to code that implements command
API also used within common code to register standard commands:
  EPILO_CMD_NULL: do nothing; tests uplink and downlink paths
  EPILO_STAT_CLR: reset counters
Command process executes commands
  Echoes opcode, up to ten argument bytes, and a result code
  Also executes stored command sequences, macros …

## Slide 23: Common S/W – Macros (1/2)
Macros are stored sequences of commands
256 different macros can be defined
64 Kbyte of RAM is available for macro storage
Macros can nest 16 deep; up to 64 macros can execute concurrently
Real-time uplink commands take precedence over macro commands
Commands from a macro are echoed; the echo includes a flag indicating that the command is from a macro

## Slide 24: Common S/W - Macros (2/2)
Macros are “learned” by the instrument
  EPILO_MAC_DEF starts a macro definition; any command uplinked with its “macro” arg set will be appended to the macro
  EPILO_MAC_ENDDEF ends the definition
  While a macro is being compiled, any real-time command, i.e., one without a set “macro” arg will be executed.
  There is no need for macro compiler or macro memory management by ground software
Other macro commands:
  EPILO_MAC_DELAY and EPILO_MAC_PAUSE delay by a give number of seconds or until a given time, respectively
  EPILO_MAC_NEST and EPILO_MAC_RUN nest a macro and starts a concurrently executing macro, respectively
  EPILO_MAC_LOOP_BEGIN and EPILO_MAC_LOOP_END delimit a definite loop
  EPILO_MAC_HALT kills a running macro

## Slide 25: Common S/W - Memory Management
Commands:
  EPILO_MEM_LOAD: loads RAM
  EPILO_MEM_COPY: copy memory; source and/or destination can be RAM or non-volatile MRAM
  EPILO_MEM_READ: produce memory dump packets
  EPILO_MEM_READ_ABRT: stop memory dump
  EPILO_MEM_CHECK: produce a checksum packet summarizing given region
  EPILO_MEM_RUN: jump to program at given address
Note: these commands are the core of the boot software

## Slide 26: Common S/W - Monitoring and Alarms
Alarm packet is generated in response to a software problem or to a monitored value going out of limits
Alarms from monitors can be transient or persistent
  If a monitored value is out-of-limits just once, a transient alarm is reported
  If a monitored value is consecutively out-of-limits twice, a persistent alarm is reported and the software may take corrective action
  If a monitored value is consecutively out-of-limits more than twice, either corrective action is taken again, the shutdown macro is run, or nothing is done, depending on the thing being monitored
Commands:
  EPILO_MON_CNTRL enables or disables corrective action

## Slide 27: Common S/W - Monitoring Algorithm
High response (low response is similar):
high once: issue transient high alarm high twice: issue persistent high alarm if enabled (via EPILO_MON_CNTRL command) execute high response macro for this alarm high more than twice: case of monitor class current/voltage: if enabled (via EPILO_MON_CNTRL command) run shutdown macro temperature: nop count rate: if enabled (via EPILO_MON_CNTRL command) re-execute high response macro

## Slide 28: Common S/W - Status Reporting
Status packet
  Command and macro execution counters
  Analogs: voltages, currents, and temperatures
  Commanded instrument state
Commands:
  EPILO_STAT_INT: how often should status be reported

## Slide 29: EPI-Lo Application S/W – Time-Of-Flight Subsystem
Measures particle time-of-flight (TOF), angle (i.e. position) on the sensor, and pulse height
EPI-Lo software controls discriminator thresholds
Commands:
  EPILO_TOF_CFD: Set TOF Constant Fraction Discriminator Threshold
  EPILO_TOF_THRESH: Set TOF Pulse Height Discriminator Threshold

## Slide 30: EPI-Lo Application S/W – Energy Subsystem
Measures particle energy
EPI-Lo software time-multiplexes hardware between electron and ion detectors
EPI-Lo software controls thresholds, one set per detector
Commands:
  EPILO_EGY_THRESH: Set Energy Discriminator Threshold
  EPILO_EGY_ANTI: Set Energy Anti-Coincidence Threshold

## Slide 31: EPI-Lo Application S/W – Event Subsystem
Analyzes data from TOF and energy subsystems to identify an “event”
EPI-Lo software configures hardware to define a valid event
Commands:
  EPILO_EVT_MULTI: Enable/Disable Multiple Hit Reject
  EPILO_EVT_WINDOW: Set Event Coincidence Window

## Slide 32: EPI-Lo Application S/W – DACs and ADCs
1 Hz activity schedule
Control QuadDACs over I2C bus
  Set power supply levels, e.g. MCP HV
  Set thresholds, e.g. MCP HV current
Read ADCs over SPI bus
  Read analogs (read three times and use median value)
  Save in housekeeping
  Monitor and report/respond to out-of-limit conditions

## Slide 33: EPI-Lo Application S/W – Test Support
EPI-Lo software provides commands to control an on-board pulser
EPI-Lo software provides commands to select internal test points to bring out on the test port
Commands:
  EPILO_TST_PUL_CFG: Configure Pulser
  EPILO_TST_PUL_ENB: Enable/Disable Pulser
  EPILO_TST_POINT: Select Test Point Signals

## Slide 34: Reference Documents
7434-9066, “Solar Probe Plus (SPP) General Instrument (GI) ICD”
16105-ISIS-IRD-01, “PRELIMINARY INSTRUMENT REQUIREMENTS DOCUMENT SOLAR PROBE PLUS PROJECT ISIS INSTRUMENT”
7464-9005, “EPI-Lo Flight Software Specification”
7464-9003, “EPI-Lo Software Development Plan”