## Slide 1: ISIS Thermal
Gregory J. Dirks
ISIS Thermal Lead (SwRI)
This document contains technical data that may be controlled by the International Traffic in Arms Regulations (22 CFR 120-130) and may not be provided, disclosed or transferred in any manner to any person, whether in the U.S. or abroad, who is not 1) a citizen of the United States, 2) a lawful permanent resident of the United States, or 3) a protected individual as defined by 8 USC 1324b(a)(3), without the written permission of the United States Department of State.
Notes: introduction

## Slide 2: Outline
Driving Instrument Thermal Requirements
Thermal Design and Implementation
  Thermal Management
  Heaters and Sensors
  MLI Design
  Materials and Finishes
Predicted Performance and Margins
  Thermal Model Details
  Design Cases
  Optical Properties and Power Dissipation
  Predictions and Margins
Plans for Thermal Verification
Summary

## Slide 3: Requirements (1/2)
Design Temperature Limits
EPI-Hi EPI-Lo
Margin Guidelines – Includes Test and Model Uncertainty
  Hot Limits 10 C and Cold Limits 5 C (Heater Controlled)
Component | Hot Op. (°C) | Cold Op. (°C) | Cold Surv. (°C)
EPI-HI HET | 40 | -25 | -40
EPI-Hi LET1 | 40 | -25 | -40
EPI-Hi LET2 | 40 | -25 | -40
EPI-Hi DPU | 40 | -25 | -40
EPI-Hi Bias | 40 | -25 | -40
EPI-Hi LVPS | 40 | -25 | -40
EPI-Hi HET Tel | 30 | -25 | -40
EPI-Hi LET 1 Tel | 30 | -25 | -40
EPI-Hi LET 2 Tel | 30 | -25 | -40
Component | Hot Op. (°C) | Cold Op. (°C) | Cold Surv. (°C)
Detector | 35 | -30 | -45
Anode Board | 55 | -30 | -45
Event Board | 55 | -30 | -45
Power Board | 55 | -30 | -45
Dome | 35 | -30 | -45

## Slide 4: Requirements (2/2)
Interface Temperatures
  Operational: -25 / +65 C
  Non-Operational: -30 / +70 C
Heaters
  75% Maximum Duty Cycle
  Resistance Determined at 26 V

## Slide 5: Design (1/3)
EPI-Hi
  E-box Radiator to Dissipate Internally Generated Heat
  Telescopes Conductively Isolated from E-box
  Operational Heaters on Telescopes
  Survival Heaters on Telescopes and E-box
  MLI on Surfaces Except Apertures, Radiator, and Bottom (S/C Facing)
E-Box
Circuit Boards
Telescopes
Radiator Surface

## Slide 6: Design (2/3)
EPI-Lo
  Wedge Radiators (8) to Dissipate Internally Generated Heat
  Eight Survival Heaters (One on Each Wedge)
  MLI on Surfaces Except Apertures and Radiators

## Slide 7: Design (3/3)
ISIS
  EPI-Hi and EPI-Lo are Thermally Isolated from the Bracket
  Bracket is Thermally Isolated from the S/C

## Slide 8: Heaters and Sensors (1/2)
EPI-Hi Heater Operations
  One S/C Thermistor on Each Telescope and Two S/C Thermistors on E-box (Primary and Redundant)
  Operational Heaters on Telescopes are All on One S/C Service, but Controlled by E-box
  Survival Heaters on Telescopes and the E-Box are All on One S/C Service and Controlled by S/C with Sense Location Currently Baselined as the E-box
  Survival Heaters Also Used to Warm Instrument to Cold Operational Temperature for Cold Turn On by using Different Set Points

## Slide 9: Heaters and Sensors (2/2)
EPI-Lo Heater Operations
  Two (Primary and Redundant) S/C Thermistors on Dome for Heater Control and One More (To Be Positioned)
  All Survival Heaters are on One S/C Service (Separate from EPI-Hi) Controlled by S/C with Sense Location Currently Baselined as One of the Wedges
  Survival Heaters are Used to Warm Instrument to Cold Operational Temperature for Cold Turn On by Using Different Set Points
  Survival Heaters are Also Used to Maintain Minimum Cold Operating Temperature During Low Power Operating Conditions

## Slide 10: MLI
Coverage
  Entire Instrument Other than Apertures, Radiators, and Under EPI-Hi Electronics
Specifications/Construction
  Each Separate Blanket Grounded with Wire to S/C
  Vented Using Edge Mesh Screens Directed away from Apertures
  Edges and Seams Sealed using GBK Tape
  Blankets Secured using G-10 Buttons and SS Snap Rings

## Slide 11: Materials and Finishes
Radiators
  Z-93 Conductive White Coating
MLI
  Germanium Black Kapton (GBK)
Apertures
  EPI-Hi: Metalized Polyimide
  EPI-Lo: Z-93
Thermal Isolators
  G-10 Fiberglass

## Slide 12: Thermal Model
EPI-Hi Modeled by Vertex Aerospace
  Rommel Zara and Santino Rosanova
EPI-Lo Modeled by APL
  Shawn Begley
Bracket Modeled by Vertex Aerospace
ISIS Model Integrated by Vertex Aerospace
All Models Created using Thermal Desktop Software
Pre-PDR Model Delivered to S/C in June
Good Correlation between Instrument and S/C Results

## Slide 13: Design Cases
Hot Operational
  +65 C I/F Temperature
  EOL Power and BOL Optical Properties
  Low MLI e* = 0.03
Cold Operational
  -25 C I/F Temperature
  BOL Power and BOL Optical Properties
  High MLI e* = 0.05
Cold Non-Operational
  -30 I/F Temperature
  BOL Optical Properties and e* = 0.05
Hot Non-Operational
  1.02 AU with +70 I/F Temperature
  EOL Optical Properties and e* = 0.03

## Slide 14: Optical Properties
Radiator: Z-93 White Coating
  BOL: a = 0.15, e = 0.91
  EOL: a = 0.45, e = 0.91
MLI Exterior: GBK
  BOL: a = 0.49, e = 0.81
  EOL: a = 0.55, e = 0.78
EPI-Hi Apertures
  HET BOL: a = 0.31, e = 0.46
  LET BOL: a = 0.35, e = 0.35

## Slide 15: Power Dissipation
ISIS Power Distribution
  Cold Case uses CBE, Hot Case uses CBE+Cont.

## Slide 16: Predictions (1/9)
Component | Limit (°C) | Predict (°C) | Margin (°C)
EPI-HI HET | 40 | 29.4 | 10.6
EPI-Hi LET1 | 40 | 29.5 | 10.5
EPI-Hi LET2 | 40 | 27.3 | 12.7
EPI-Hi DPU | 40 | 28.2 | 11.8
EPI-Hi Bias | 40 | 28.6 | 11.4
EPI-Hi LVPS | 40 | 29.6 | 10.4
EPI-Hi HET Tel | 30 | 3.5 | 26.5
EPI-Hi LET 1 Tel | 30 | -15.0 | 45.0
EPI-Hi LET 2 Tel | 30 | -0.5 | 30.5
EPI-Hi Hot Operational

## Slide 17: Predictions (2/9)
EPI-Hi Cold Operational
Component | Limit (°C) | Predict (°C) | Margin (°C)
EPI-HI HET | -25 | -2.9 | 22.1
EPI-Hi LET1 | -25 | -2.9 | 22.1
EPI-Hi LET2 | -25 | -4.8 | 20.2
EPI-Hi DPU | -25 | -4.1 | 20.9
EPI-Hi Bias | -25 | -3.8 | 21.2
EPI-Hi LVPS | -25 | -2.6 | 22.4
EPI-Hi HET Tel | -25 | -20 | 5
EPI-Hi LET 1 Tel | -25 | -20 | 5
EPI-Hi LET 2 Tel | -25 | -20 | 5
Heater Location | Heater Power(W)
EPI-Hi HET TEL | 0.05
EPI-Hi LET1 TEL | 0.08
EPI-Hi LET2TEL | 0.32
TOTAL | 0.45

## Slide 18: Predictions (3/9)
EPI-Lo Hot Operational
Component | Limit (°C) | Predict (°C) | Margin (°C)
Detector | 35 | 24.8 | 10.2
Event | 55 | 27.2 | 27.8
Pwr. Supply | 55 | 28.9 | 26.1
MCP | 55 | 25.2 | 29.8
Anode | 55 | 23.8 | 31.2

## Slide 19: Predictions (4/9)
EPI-Lo Cold Operational
Component | Limit (°C) | Predict (°C) | Margin (°C)
Detector | -30 | -10.0 | 20.0
Event | -30 | -8.4 | 21.6
Pwr. Supply | -30 | -7.0 | 23.0
MCP | -30 | -8.8 | 21.2
Anode | -30 | -11.1 | 18.9

## Slide 20: Predictions (5/9)
ISIS Heater Sizing
EPI-Lo Operational CBE Power of 4.17 W is Duty Cycled at 75% for a Heater Instantaneous Power of 5.56 W (26 V).
  Temperature Setpoints of -25°C/-22°C (Operational)
  Temperature Setpoints of -40°C/-37°C (Non-Operational)
EPI-Hi Operational CBE Power of 5.81 W is Duty Cycled at 75% for a Heater Instantaneous Power of 7.74 W (26 V).
  HET TEL: 0.3 W
  LET1 TEL: 0.8 W
  LET 2 TEL: 0.5 W
  EBOX: 6.15 W
  Temperature Setpoints of -20°C/-17°C (Operational)
  Temperature Setpoints of -35°C/-32°C (Non-Operational)

## Slide 21: Predictions (6/9)
ISIS Cold Non-Operational Temperatures
Component | Avg.Heater Power, W | 
EPI LO | 2.30 (2.82 Allocation) | 
EPI HI Ebox | 3.09 | 3.90 (4.38)
EPI HI HET 1 | 0.25 | 
EPI HI LET 1 | 0.15 | 
EPI HI LET 2 | 0.40 | 

## Slide 22: Predictions (7/9)
ISIS Warm Up Temperatures
Component | Avg. Heater Power, W | 
EPI LO | 3.40 | 
EPI HI Ebox | 4.26 | 5.37
EPI HI HET 1 | 0.35 | 
EPI HI LET 1 | 0.21 | 
EPI HI LET 2 | 0.55 | 

## Slide 23: Predictions (8/9)
ISIS Hot Non-Operational Temperature Plot

## Slide 24: Predictions (9/9)
ISIS Hot Non-Operational Temperature Table
Component | Hot Surv Predict, °C | Hot Surv Limit, °C | Margin, °C
IS_ISIS_TEL_HET | 7.0 | 55.0 | 48.0
IS_ISIS_TEL_LET1 | 26.8 | 55.0 | 28.2
IS_ISIS_TEL_LET2 | 30.8 | 55.0 | 24.2
IS_ISIS_EPI_HI_BIAS | 8.9 | 55.0 | 46.1
IS_ISIS_EPI_HI_DPU | 9.1 | 55.0 | 45.9
IS_ISIS_EPI_HI_HET | 8.9 | 55.0 | 46.1
IS_ISIS_EPI_HI_LET1 | 8.9 | 55.0 | 46.1
IS_ISIS_EPI_HI_LET2 | 9.1 | 55.0 | 45.9
IS_ISIS_EPI_HI_LVPS | 9.2 | 55.0 | 45.8
Component | Hot Surv Predict, °C | Hot Surv Limit, °C | Margin, °C
IS_ISIS_EPI_LO_DETECTOR | 42.5 | 55.0 | 12.5
IS_ISIS_EPI_LO_EVENT | 42.2 | 55.0 | 12.8
IS_ISIS_EPI_LO_PWR_SUPPLY | 42.1 | 55.0 | 12.9
IS_ISIS_EPI_LO_MCP | 42.3 | 55.0 | 12.7
IS_ISIS_EPI_LO_ANODE | 42.2 | 55.0 | 12.8
IS_ISIS_EPI_LO_DOME | 42.7 | 55.0 | 12.3

## Slide 25: Verification (1/2)
ISIS Thermal Vacuum Profile
  Six Operational Cycles
  One Survival Cycle

## Slide 26: Verification (2/2)
ISIS Thermal Balance
  Three Cases: Hot Operational, Cold Operational, and Cold Survival
  Temperature Controlled Baseplate to S/C I/F Temperature Limits
  Radiators with View to LN2 Cooled Chamber Shroud
  Verify Heater Duty Cycle
  Verify Interface Conductances
  Correlate Thermal Model

## Slide 27: Summary
Instrument Requirements (Temperature Limits) are Defined
Thermal Environments and Interfaces are Defined
Resources (Heater Power) have been Iterated and Baselined
The Thermal Design Presented and Analyzed Meets all Requirements in the Specified Environments within the Allocated Resources