## Slide 1: Assembly, Integration, and Test
John Dickinson
ISIS SE (SwRI)
This document contains technical data that may be controlled by the International Traffic in Arms Regulations (22 CFR 120-130) and may not be provided, disclosed or transferred in any manner to any person, whether in the U.S. or abroad, who is not 1) a citizen of the United States, 2) a lawful permanent resident of the United States, or 3) a protected individual as defined by 8 USC 1324b(a)(3), without the written permission of the United States Department of State.
Notes: introduction

## Slide 2: Outline
EPI-Hi Assembly, Integration, and Test Flow
EPI-Lo Assembly, Integration, and Test Flow
EDTRD Test Levels:
  Acoustic
  Vibration
  Thermal-Vacuum profile
  Observatory Environmental Testing
Summary
Typical Test Flow for Components and Instruments (EDTRD)
Not Performed on ISIS

## Slide 3: EM EPI-Hi Assembly, Integration, & Test

## Slide 4: FM EPI-Hi Assembly, Integration, & Test
Performance Tests performed between Qualification Tests

## Slide 5: EM EPI-Lo Assembly, Integration, & Test

## Slide 6: FM EPI-Lo Assembly, Integration, & Test
Performance Tests performed between Qualification Tests

## Slide 7: Normal Vibration Levels
Frequency (Hz) | Qualification (G2/Hz) | Protoflight (G2/Hz) | Acceptance (G2/Hz)
20 | 0.01 | 0.01 | 0.01
60 | 1.25 | 1.25 | 0.63
200 | 1.25 | 1.25 | 0.63
350 | 0.04 | 0.04 | 0.04
500 | 0.04 | 0.04 | 0.04
2000 | 0.01 | 0.01 | 0.01
Overall Grms | 16.4 | 16.4 | 12.6
Duration (mins) | 2 | 1 | 1
Side Panels Mounted Components & Subsystems Normal To Panel
Normal
Lateral
Lateral

## Slide 8: Lateral Vibration Levels
Normal
Lateral
Lateral
Frequency (Hz) | Qualification (G2/Hz) | Protoflight (G2/Hz) | Acceptance (G2/Hz)
20 | 0.01 | 0.01 | 0.01
35 | 0.04 | 0.04 | 0.04
500 | 0.04 | 0.04 | 0.04
2000 | 0.01 | 0.01 | 0.01
Overall Grms | 6.8 | 6.8 | 6.8
Duration (mins) | 2 | 1 | 1
Side Panels Mounted Components & Subsystems Lateral To Panel

## Slide 9: Acoustics Levels
1/3 Oct Center Freq (Hz) | MEFL (dB) |  | 1/3 Oct Center Freq (Hz) | MEFL (dB)
32 | 123.0 |  | 630 | 120.5
40 | 124.8 |  | 800 | 119.1
50 | 126.2 |  | 1000 | 117.8
63 | 127.5 |  | 1250 | 116.4
80 | 128.3 |  | 1600 | 115.0
100 | 128.8 |  | 2000 | 113.6
125 | 129.0 |  | 2500 | 112.3
160 | 128.7 |  | 3150 | 110.9
200 | 127.5 |  | 4000 | 109.5
250 | 126.0 |  | 5000 | 108.1
315 | 124.3 |  | 6300 | 106.8
400 | 123.3 |  | 8000 | 105.4
500 | 121.9 |  | 10000 | 104.0
 |  |  | OASPL | 138.1
Table 7‑2. Acoustic Flight Levels

## Slide 10: Thermal Vacuum Test Cycles
CPT
CPT
CPT
CPT

## Slide 11: Observatory Environmental Testing
(N/A for ISIS)

## Slide 12: Summary
EM is used as a pathfinder for FM integration and test
Selected EM environmental testing provide risk reduction
FM unit undergoes instrument level environmental testing to EDTRD levels
EM is used for command and procedure testing after FM delivery to spacecraft and to support commanding activities after launch