## Slide 1: Flight Operations
Eric Christian
ISIS Deputy PI (GSFC)
This document contains technical data that may be controlled by the International Traffic in Arms Regulations (22 CFR 120-130) and may not be provided, disclosed or transferred in any manner to any person, whether in the U.S. or abroad, who is not 1) a citizen of the United States, 2) a lawful permanent resident of the United States, or 3) a protected individual as defined by 8 USC 1324b(a)(3), without the written permission of the United States Department of State.
Notes: introduction

## Slide 2: Outline
Initial commissioning
Nominal operations
Instrument command loads
Instrument autonomy requirements
Flight operations staffing
Off-nominal operations
Summary

## Slide 3: Initial Commissioning
EPI-Hi turns on first (EPI-Lo needs two week out-gassing period)
ISIS Statistics Gathering and Threshold Scans
  Analysis parameters will be tuned with pre-flight calibrations, but it is likely that some fine-tuning will be required
  After initial instrument turn on and checkout it is important that the ISIS instruments gather as much data as possible (especially raw event data)
  Threshold scans will be required to determine optimal threshold values
  EPI-Lo does not need to be on continuously
ISIS EPI-Lo and EPI-Hi Table Loads and/or Software Updates
  Table updates expected (adjustment of flux box bins) 3 weeks into statistic gathering period
  Software updates might be needed
  Based on STEREO experience, EPI-HI will require ~10 opportunities (on separate days) to send commands in the first two months
  Necessary to obtain/analyze at least a few hours of new data in between command opportunities to test whether the commands worked
  Therefore, need to collect data between commanding opportunities

## Slide 4: Nominal Operations
EPI-Hi and EPI-Lo operate the same whenever powered-on except for the volume/content of the data sent to the S/C inside/outside 0.25 AU
Spacecraft- Sun Distance R<0.25 AU (Normal Science Mode)
  Full nominal power
  High data collection rate
  Burst data (EPI-Lo)
Spacecraft- Sun Distance: 0.25 AU < R (Low-rate Science Mode)
  Full power whenever possible
  Reduced data collection rate (fits within ISIS telemetry allocation)
  Commanding window should be scheduled late in the series of telemetry passes, although it may not be used every orbit
  Minimize power cycling the HV supplies

## Slide 5: Instrument Command Loads
Commanding of EPI-Hi and EPI-Lo
  “Flat-Sat” at UNH used to test command loads
    Development of Flat-Sat will be Phase D work
    Constraint Checking Modules
  Standard Commanding performed via GSEOS at UNH SOC
  Commissioning and Contingency response, commanding may optionally be done by EPI-Hi and EPI-Lo via GSEOS directly through MOC
Planning for instrument operations
  Planning software
    Automated routines and templates for initial planning
    Interactions with ISIS SOC interfaces for finalization of planning
  Develop rough plans three orbits ahead
    Test command load
  Develop definitive plans one orbit ahead
    Final testing
    Upload

## Slide 6: Autonomy
Instrument Autonomy requirements considerably more than in initial SPP proposal and more than EPI-Hi has experienced in previous missions
Main additional requirement is the ability to record the instrument state and return to that state autonomously after instrument power cycling, due to either s/c telemetry time periods or anomalous safing of instrument
ISIS will implement operational mode changes via instrument autonomy logic supplemented by a macro capability

## Slide 7: Flight Operations Staffing
FLEXIBLE
  variability of telemetry and commanding requires flexible staffing
Priorities (in order)
  Analysis of health and safety housekeeping
  Analysis of snapshot science data to determine interesting time periods (relayed to other SPP instruments) and science optimization
  Full analysis of science data and generation of data products

## Slide 8: Off-nominal Operations
Plan to avoid them
Small amounts of critical housekeeping will give team a heads-up
Instruments designed to dump diagnostic data when possible
“Deep bench” of scientists and engineers with many years of experience to draw from
ISIS will work with the SPP operations team to do what is necessary to prudently diagnose issues and bring instruments back to nominal operations

## Slide 9: Summary
ISIS Instrument operation modes designed to reduce complexity
Autonomous instrument operations simplify SPP spacecraft operations
ISIS team will develop all of the processes necessary to verify commanding and provide safe and efficient instrument operations