## Slide 1: EPI-Lo Electronics
Reid Gurnee
Notes: introduction

## Slide 2: Outline
Electronics Overview
Block Diagrams
Driving Requirements
Event Board
  Functionality, Interfaces, prototyping, FPGA, layout
Anode Board
  Functionality, Interfaces, prototyping, layout
Energy Board
  Functionality, Interfaces, prototyping, layout
Packaging and thermal considerations
Radiation analysis
Plans for testing
Preliminary parts list and special screening considerations
Status Summary
Plan Forward
Summary and follow-up from peer reviews
Headings in Outline don’t match
all the slide titles

## Slide 3: EPI-Lo – Electronics Overview
Event Board
Power Board
Anode Boards (x4)
Energy Boards (x8)

## Slide 4: EPI-Lo Block Diagram

## Slide 5: Block Diagram

## Slide 6: Electronics Driving Requirements
Analog Performance
  Timing resolution < 400pS FWHM
  Energy resolution < 15KeV (typically sensor / pre-amp dominated)
MCP timing system dynamic range of 500k to 25M electrons
Energy system dynamic range of 30keV to 15MeV
  Higher energies (>1MeV) use pulse width mode

## Slide 7: Event Board Functionality
Instrument processor
  Embedded processor in RTAX2000
    Execute Flight Code, Accumulating and Formatting Telemetry, Commanding, and Alarm Detection and Action
  Spacecraft communication
  Core code in PROM, classification tables and application code in MRAM
  Accumulate data into classification tables
Event Processing
  Communicate and handle timing with ADCs, TOFs
  Pre-process and accumulate event data
  Accumulate Rates
HVPS control
  Control four opto-coupler generated HVPS outputs
  Provide high speed safing of HVPS in response to over current

## Slide 8: Event Board Functionality
Time-of-flight based on APL TOD-D and CFD-D ASICs
  New ASICs developed for future programs
  Improved size and performance from previous ASICs
  12 CFDs and 4 TDCs for timing system
Solid State Detector Energy Measurements
  8 Peak detect and A/D converters for energy system
  Peak detect chips are APL ASICs flown on previous missions (PEPSSI, Jedi, RBSPICE)
MCP pulse height comparators
  Two comparators for each MCP monitor MCP gain
Pulsers
  Independent pulsers for start and stop signals on each anode board
  Two pulsers for Energy system
  All pulsers have programmable amplitude
TOD-D or TOF-D ?
Used TOFD and CFDD
in presentation 07
not TOF-D and CFD-D.
Make slides consistent.

## Slide 9: Event Board Interfaces
Solid State Detector Interface
  8, 9-pin ndsub connectors to energy boards
  ~10 mV to over 1 V unipolar-shaped pulses
  Control, pulser, and power lines
Anode Board Interface
  12 Time-of-Flight Coax connectors to anode
    ~10 mV to over 1 V fast-shaped pulses
  12 power and pulser Coax connectors
Test Port Connector
  1 Test Input (to aid in end-to-end timing tests)
  5 Test-point outputs
Spacecraft data connector
  Redundant LVDS interface

## Slide 10: Energy System Updates
Energy system re-designed from previous instruments
  8 ADC121s read out the 8 peak detect chips
  Prior designs used MUX and one fast ADC
  New design allows de-coupling of quadrants – each quadrant had completely independent readout electronics and can be operated as an individual instrument
  Event logic will be identical for each quadrant and then the data will be combined
  New approach significantly simplifies event logic design and increases data processing rates

## Slide 11: Energy System Prototype
SSD pre-amplfiers
Digital readout
ADC121 (EM)
Peak Detect SIP
Test interface of peak – detect chip to ADC

## Slide 12: Energy System Prototype Performance
Energy resolution of test setup far exceeds requirement
No glitches observed on signal when ADC transitions into track mode after the peak detect SIP captures an event
DB atten | KeV |  | Codes | Std Dev | FWHM | FWHM (KeV)
0 | 1820.00 |  | 3945 | 5.15 | 12.1025 | 9.92405
-6 | 912.161 |  | 3000 | 4.56 | 10.716 | 8.78712
-7 | 812.964 |  | 2910 | 3.25 | 7.6375 | 6.26275
-8 | 724.555 |  | 2830 | 3.16 | 7.426 | 6.08932
-9 | 645.760 |  | 2761 | 3.02 | 7.097 | 5.81954
-10 | 575.535 |  | 2696 | 2.9 | 6.815 | 5.5883
-15 | 323.647 |  | 2478 | 2.55 | 5.9925 | 4.91385
-20 | 182.000 |  | 2339 | 2.41 | 5.6635 | 4.64407
-25 | 102.346 |  | 2255 | 2.34 | 5.499 | 4.50918
-30 | 57.553 |  | 2203 | 2.23 | 5.2405 | 4.29721
-35 | 32.365 |  | 2174 | 2.15 | 5.0525 | 4.14305
-40 | 18.200 |  | 2157 | 2.36 | 5.546 | 4.54772

## Slide 13: FPGA
FPGA contains all event logic and event processing
  SCIP: 16-bit 10 MIPS processor (reused custom embedded processor based on Harris RTX2010 and APL’s FRISC)
  Processor memory interface to PROM, MRAM, SRAM
  Support I/O
    Provide voltage supply clocks, read safing status, set thresholds, monitor housekeeping, etc.
    LVDS spacecraft communication interface
    Processor test port interface
  Event Logic
    Count sensor basic rates and diagnostic rates
    Provide pulser stimulus
    Collect and process TOF values to generate start direction and particle time-of-flight
    Select appropriate SSD channel and record energy deposited
    Detect anti-coincidence (electron only) and pulse-height over-threshold (start and stop)
    Send selected valid events based on commanded event criteria to processor event buffer
    Event logic test port for ground testing

## Slide 14: FPGA
Actel RTAX2000SL -1 speed CCGA-624 (common buy part)
  Estimate ~40% resource utilization based on RBSPICE design
  Internal RAM for event FIFO only
    No minimize size required and soft memory is fine
  # user I/O of 418 user I/O total
    # spares to power board + 6 spares through Schmitt triggers to test connector + # true spares = # spares
    Note: At the FPGA requirement review, moderate reuse designs are green for at least 17 uncommitted I/O pins
  1.5V Core Voltage, 3.3V I/O Supply Voltage
    +/-5% voltage tolerance
    Supplies can be powered up or powered down in any sequence as long as some app note details are considered
    I/O are tri-stated during power-up
  Lower standby current part but still significant power contribution at hot temperatures

## Slide 15: FPGA
Part prototyping
  Reprogrammable Aldec/Actel system for EM
  Board layout also accommodates commercial socket if needed
  RTAX2000SL -1 speed CCGA-624 for flight (participating in common buy)
Design prototyping/reuse
  SCIP is identical to RBSPICE
  Similar approach to RBSPICE for many interfaces: S/C communication, power supplies, QDACs, test port, memories, peak detects, pulsers
  New interfaces prototyped prior to EM: TOF-D rather than TOF-C, new ADC for HK and peak detect
  Significant previous experience with all design tools: VHDL (with tcl scripts, pdc files etc.), Synplify Pro, Actel Libero, ModelSim
No expected areas of concern
  No timing closure challenges expected (most of design at 10MHz, some at 40MHz)
  Primarily synchronous design techniques with standard clock domain crossing techniques and no gated clocks
  Straightforward reset filtering and routing network
  Sufficient clock nets available for clocks and reset

## Slide 16: Event Board Layout
Sensitive analog is separated from digital
  FPGA, S/C communication, SRAM, PROM, MRAM, and oscillator on top of board
  TOF electronics on left and right of board
  Peak detect and ADC electronics on bottom of board
  All critical routing isolated by ground planes from digital routing
X layers, X ground and power planes
Actel located with SRAM directly adjacent
  Reduce track-length to SRAM to reduce noise
  Actel on Primary side, to allow the Development Tool access to the program pins

## Slide 17: Event Board Layout
CFDs
TOFs
RAM
ADCs
Peak Detect SIPs
FPGA
MRAM, PROM
LVDS, Test Port
TOFs
CFDs

## Slide 18: Anode Board Description
Functionality
  3 fast discrete amplifiers
    Stop anode and each end of the start delay line
    50 ohm impedance matched, designed to drive 50 ohms
  Anode is at 3kV, PCB embedded capacitors isolate HV from LV
  1 start pulser and 1 stop pulser
    Start pulser location in imaginary anode between sensor wedges
Interfaces
  6 coax SSMB connectors
  Power, 3 outputs, 2 pulsers
Show output waveform with X #
of input electrons

## Slide 19: Anode Board Prototyping
Initial prototype board fabricated, assembled, and tested
  First implementation of embedded capacitors for HV anode
  Verified quadrant design
EM anode board fabricated, assembled, and tested
  Electrical and mechanical interfaces well defined
  Position mapping on prototype verified simulations for start pad locations
  Kapton layer provides dielectric strengh of ~20kV for embedded capacitors
    Passed 10 day, 2x HV standoff test (recommended by Steve Battel)
  APL packaged transistor array

## Slide 20: Anode Board Layout
HV Filters
Pre-Amps
Delay line elements

## Slide 21: Energy Board
Functionality
  SSD Pre-amplifier and shaper
  Energy ASIC supports 3 pre-amplifiers and MUX
    Ion channel, electron channel, anti-coincidence channel
    Select between Ion channel, or electron and anti-coincidence channels
  Thermistor for temperature measurements
Interfaces
  9pin ndsub connector for power, signals, pulser, and temperature monitor
  Bias voltage from separate HV wire (<250V)
EM energy board fabricated and tested
Will have photo of fabricated board in 3 weeks

## Slide 22: Energy Board Layout
SSD inputs for ion, electron, and anit-coiincidence detectors
Bias supply input
HV (bulk) connection to SSDs
Ground (front) connection to SSDs
Test connector
Interface to event board
Energy ASIC Die

## Slide 23: Event Board Packaging
Packaged in octagon frame “slice”
  Board is loaded from the bottom and has six center mounting supports and full contact around the perimeter
  FPGA is supported on four corners
Large number of thermal vias under the higher power parts
  Actel, RAM, and MRAM to dissipate power into the board planes and out to the frame.
  Total board power is ~1 watt. No thermal issues expected.

## Slide 24: Anode and Energy Board Packaging
Anode Board
  Anode board is mounted to instrument main support structure by X #X mounting hardware
  Total board power is 90mW, no thermal concerns
Energy board is mounted directly behind SSD
  Total board power is 25mW, no thermal concerns
Add images from model
showing board mounting

## Slide 25: Radiation Analysis
FASTRad analysis performed on instrument in S/C model to predict doses seen at electronics
RESULTS:
Working on updated fast-rad analysis

## Slide 26: Plans for testing
Follows APL Manufacturing Flow, these are significant highlights
  Populate Passive Components
  Execute Test Procedure to Verify Passive Components
  Populate First-level Active Components
    Voltage References, Power-on Reset, Oscillator, applicable Tailor Flags
  Execute Test Procedure to Tailor and Verify First-level Active Components
  Populate Actives and Install Known Tailors or Tailor Flags
  Install into Flight Frame
  Execute Test Procedure to Test and Tailor Entire Board
  ESS Testing
  Execute Functional Test Procedure
  Photograph and Conformal Coat
  Execute Test Procedure to Calibrate and Characterize Board (over temperature)
  Release to Next Assembly

## Slide 27: Parts
All parts are rad-hard to 100krad
No parts concerns
Add table of parts

## Slide 28: Status Summary
Event board
  EM parts placement complete
  Routing in process
  EM PCB expected in early December
Anode Board
  EM anode board fabricated, assembled and tested
Energy Board
  EM Board fabricated, assembled, and tested

## Slide 29: Plan Forward
Anode Board
  Complete testing on Anode board
  Fabricate flight anode board
Energy Board
  Complete testing on energy board
  Fabricate flight energy board
Event Board
  Fabricate EM board
  Complete testing on EM board
  Fabricate flight Event board
Finalize all documentation and procedures for flight build
Build, tailor, calibrate, and qualify flight units

## Slide 30: Peer Review Status
Event Board Peer Review
  August 21, 2013. Summarized with action items in memo TBD
  action items were generated
  6 action items generated / 6 action items closed
Anode Board Peer Review
  TBD
Energy Board Peer Review
  August 26, 2013. Summarized with action items in memo TBD
  action items were generated
  4 action items generated
  TBD action items are closed
Parts Stress Analysis
  No issues expected
WCA
  No issues expected

## Slide 31: Outline
Driving requirements
Block Diagram
Electronics Design Overview
  Anode Board
  Energy Board
  Event Board
  Power Board
Detailed description of the measurement electronics and signal processing flow
Detailed description of the control electronics and its associated support circuitry
Interfaces to the spacecraft
Packaging and thermal considerations
Plans for testing
ASICs
Maturity of the design (BB testing, design, analysis completed)
Preliminary parts list and special screening considerations
Summary and follow-up from peer reviews
Original Outline