## Slide 1: Epi-Hi Flight Software
Management of Data Flow from
EPI-Hi DPU to Spacecraft
Solid State Recorders (SSRs)
Andrew Davis
October 31, 2014

## Slide 2: Description of Task
From Flight Software Requirements Doc:
During encounters, the DPU MISC FSW shall manage the volume of EPI-Hi instrument data telemetered to the Spacecraft as a function of time, based on the Solid-State-Recorder “fill-level” information in the Spacecraft status message, and the time-length of the current encounter. The algorithm to be used by the DPU to perform this management function shall be described in the Data Format Document (Ref. 8)
Context: The volume of data written by EPI-Hi to the spacecraft as a function of time must be managed so that we do not run out of SSR space before the end of the encounter.
Rationale/Flowdown: Self-imposed.
ID: L5-INSTSW-134

## Slide 3: Available Inputs (1)
From Spacecraft Time/Status Message, updated every second:
Mission Elapsed Time (MET). Seconds since Jan 1 2010 (drifts).
Solar Distance (km).
Solar Distance Valid. 0=Not valid. 1=Valid.
Solar Distance Inflection. 0=Decreasing. 1=Increasing.
EPI-Hi SSR Allocation Status: SSR%FULL: 0-255. 255 = 100%
  Note: S/C will stop recording new EPI-Hi data to the SSR when this parameter reaches 255 (100% full)
Encounter Flag? I don’t see one in the latest GI-ICD.

## Slide 4: Available Inputs (2)
Input set via ground command to DPU, prior to each Encounter
We can define whatever parameters we need, but here is a minimal suggested set:
Total SSR Allocation (bytes): SSR_ALLOC. Equals number of bytes written to SSR when SSR allocation Status from spacecraft = 255 (100%).
  This could be the same for every encounter, but may change…
  Needed for DPU to meter the data flow to SSR.
Encounter Start time (MET seconds): ESTART (or Encounter Start Solar Distance?)
Predicted Encounter time length (seconds): ELENGTH
  Needed for DPU to meter the data flow to SSR.
Amount of SSR allocation to reserve for use after end of encounter (bytes): SSR_RESERVE
  EPI-Hi will (hopefully) be powered-up and delivering low-rate data to the SSR after the end of each encounter. The SSR allocation status from the spacecraft will be adjusted downwards (or reset to 0%) at some point after the end of the encounter, but the timing is TBD.

## Slide 5: Constraints
The DPU has no significant data storage capacity (128kwords SRAM, much of which is used by code and data buffers)…we can’t “save up” some data and telemeter it some time in the future.
Event prioritization is implemented in the telescope MISCS, and events flow to the DPU from each of the telescopes at a rate up to the bandwidth capacity of the telescope-DPU serial link.
The DPU knows which telescope an events comes from but does not know anything about the “importance” of any individual event.
There are no commanding opportunities during encounters.

## Slide 6: Proposed Data Metering Algorithm (Simplest possible, I think)
WHILE (Encounter==TRUE)
Each Hour (or whatever time unit we agree upon)
#HOURS_LEFT = (ESTART + ELENGTH – MET)/3600
#BYTES_LEFT = (SSR_ALLOC * SSR%FULL) – SSR_RESERVE
IF (#BYTES_LEFT > 0)
#BYTESPERHOUR = #BYTES_LEFT/#HOURS_LEFT
ELSE
#BYTESPERHOUR = 0
ENDIF ENDWHILE
Nominally, the #BYTESPERHOUR value is enough to send 1 hour of “IN_ENCOUNTER” EPI-Hi rates and HK data, plus some events, to the SSR.
If solar activity is low early in an encounter, we won’t collect enough events in an hour to use up the full #BYTESPERHOUR. Thus, #BYTESPERHOUR may grow in size later in the encounter.
It is TBD what the DPU should do if we have a situation where we have to start an encounter and #BYTESPERHOUR < rates+HK
Comments/Improvements welcome…