## Slide 1: EPI-Lo Mechanical
Scott Cooper
Steve Layman
Shaughn London
Notes: introduction

## Slide 2: Outline
Development Status
Mechanical Design Requirements
Instrument Accommodation
Notable Design Changes Since PDR
Instrument Overview
Epi-Lo Drawing Tree
Sensor Design Details
Instrument Assembly Process
Prototype Hardware
Acoustic Test
Development Path Forward
Structural Analysis

## Slide 3: Development Status
Assembled 2 EM MCPs
  Performance test at HV
Assembled 1 EM wedge
  Performance test at HV over op temp range
Assembled 2 prototype wedges
  Acoustic test
Fabricated prototype spider frame
Integrated Event and Power PWAs with prototype board frames
Updated EM part fabrication in process
Awaiting mounting bracket to conduct vibe test
Structural analysis coupled with updated mounting bracket in work

## Slide 4: Mechanical Design Requirements
7434-9039, SPP Environmental Design and Test Requirements Document
  Subsystem to have min frequency > 80 Hz
  PWAs to have min frequency > 150 Hz
  Quasi-static load factor: 40g (Figure 4-11 & Table 4-19)
  Factors of safety: Table 4-5, Unpressurized Factors of Safety
  Random vibration levels: Table 4-8 and Table 4-9
Interface Documentation
  7434-9058, ISIS to S/C ICD
  7434-9066, SPP General Instrument to S/C ICD
  7464-0008 EPI-Lo-S/C Mechanical ICD
  161051001, ISIS Suite MICD
  161051002, ISIS Bracket to Instrument MICD
7434-9040, ElectroMagnetic Environment Control Plan
7434-9553, SPP Purge Plan
7434-9555, SPP Alignment Plan
7464-9007, Epi-Lo Contamination Control Plan

## Slide 5: Instrument Accommodation
ISIS INSTRUMENT SUITE
EPI-HI INSTRUMENT
ISIS MOUNTING BRACKET
ISIS INSTRUMENT SUITE ON SPP
MODELS SHOWN ARE NOTIONAL AND MAY BE OUTDATED
SOLAR PROBE S/C

## Slide 6: Epi-Lo on ISIS Mounting Bracket
ISIS MOUNTING BRACKET, SWRI
G-10 ISOLATORS,
4 PLCS
SUFFICIENT CLEARANCE AT INSTRUMENT CONNECTOR PANEL

## Slide 7: Notable Design Changes Since PDR
Added vents to all blind holes in sensor assembly
Replaced individual collimator bosses on wedge cover with continuous surfaces
Added interlocking feature between SSD holder and SSD insulator to improve stop foil/MCP compression plate insulation
Added ground strap attach points to spider
Incorporated side closeout with wedge cover into single piece*
Added purge fitting boss to wedge side wall
Changed to heritage MDM safing connector*
Added HV wiring conduit outside of board frames
Modified openings in wedge acceleration grid, MCP grid, and MCP mask to improve sensor performance*
Added bolts to constrain center of electronics bulkhead to power board frame*
Added stiffening ribs to bottom cover*
Removed wedge torlon screws and made wedge insulator the common joining feature*
Added various internal restraining features for wiring*
* Fabrication of updated design in work
Note: Changes in black text are highlighted on subsequent charts

## Slide 8: Instrument Overview
WEDGE ASSEMBLY
8 places
SPIDER FRAME
TOP CLOSEOUT
WEDGE CLOSEOUT,
8 PLACES
EPI-Lo Instrument Isometric View
Replaced individual collimator bosses on wedge cover with continuous surfaces
Added ground strap attach points to spider
Incorporated side closeout with wedge cover into single piece

## Slide 9: Instrument Overview
INSTRUMENT CONNECTOR PANEL
POWER BOARD SLICE
EVENT BOARD SLICE
MOUNTING INTERFACE, 4 PLACES
SPIDER
CLOSEOUTS,
8 PLACES
EPI-Lo Instrument Side Isometric View
Changed to heritage MDM safing connector

## Slide 10: Epi-Lo Drawing Tree

## Slide 11: Wedge Design
EPI-Lo Sensor Wedge Assembly
SIDE WALLS AT 1kV ALUMINUM 6061-T651
SENSOR COVER AT GROUND ALUMINUM 6061-T651
SSD INSULATOR
ULTEM 2300
COMPRESSION PLATE AT 1kV
STAINLESS 303
MCP ASSEMBLY IN A ULTEM 2300 HOUSING
WEDGE INSULATOR
ULTEM 2300
Removed wedge torlon screws and made wedge insulator the common joining feature

## Slide 12: Wedge Design
Added purge fitting boss to wedge side wall

## Slide 13: Wedge Design
EPI-Lo Sensor Wedge Assembly Cross-Section View
MCP COMPRESSION PLATE, 1kV
TOP MCP, 900V
BOTTOM MCP 2.9kV
SENSOR WEDGE COVER, GROUND
WEDGE INSULATOR ULTEM 2300
SCREWS, TORLON
3 PLCS
COLLIMATORS, AT GROUND
8 PLCS
APERTURE START FOIL GRID, GROUND
10 PLCS
MCP GRID, 1kV
(TOP OF ANODE PWB NOT SHOWN, 3kV)
WEDGE GRID, 1kV

## Slide 14: MCP Assembly Design
MCP Assembly
TOP VIEW
BOTTOM VIEW
COMPRESSION PLATE
900V LUG
1KV LUG
2.9KV LUG

## Slide 15: SSD Assembly Design
SSD Assembly Exploded View
SSD ASSY
SSD STOP GRID-FOIL, GROUND
GROUNDING SCREW
SSD ASSY HOUSING, ULTEM 1000
ENERGY PWB ASSY

## Slide 16: MCP Assembly Process
MCP Assembly Exploded View
900V ELECTRODE
INSULATED SHIM, ULTEM 1000
COMPRESSION PLATE
GUARD WASHER
900 V LUG ASSY
SLIDE-SPACER ELECTRODE
LINEAR EXPANDERS, 3 PLACES
2.9 kV ELECTRODE
1kV LUG ASSY
WASHER
2.9kV LUG ASSY
SLIDES FOR EXPANDERS, 2 PLACES
MCP
SCREW
MASK, .002
MCP
SCREW
NUT
MCP HOUSING

## Slide 17: Wedge Assembly Process
EPI-Lo Sensor Wedge Assembly Exploded View
APERTURE START FOILS
WEDGE COVER
WEDGE INSULATOR,
ULTEM 2300
WEDGE GRID
(SIDE WALL REMOVED FOR CLARITY)
COLLIMATORS
MCP GRID
SSD WEDGE GRID, 1kV
SSD INSULATOR, ULTEM 2300
SIDE WALL, 1kV
SCREWS, TORLON
3 PLCS
Added interlocking feature between SSD holder and SSD insulator to improve stop foil/MCP compression plate insulation

## Slide 18: Spider and Electronics Integration
BOTTOM COVER
SPIDER FRAME
EPI-Lo Electronics Frames Exploded View
EVENT BOARD PWA
ELECTRONICS BULKHEAD
POWER BOARD PWA
ANODE BOARD,
4 PLACES
Added bolts to constrain center of electronics bulkhead to power board frame
Added stiffening ribs to bottom cover

## Slide 19: External High Voltage Wiring Conduit
EPI-Lo Isometric View
Added HV wiring conduit outside of board frames

## Slide 20: Wedge Integration and Cable Routing
EPI-Lo Cross-Section Isometric View
ANODE BOARD CONNECTORS
(SEE NEXT SLIDE)
EVENT BOARD CONNECTORS
SSD ASSEMBLY
HARNESS CONNECTORS
INTER-BOARD HARNESS
WITH CLAMP
CABLE PASS THRU
CABLES TO ANODE BOARD

## Slide 21: Anode Board Cable Connections
Anode PWB Assembly,
Bottom Side Shown
Mounted To Spider Frame
2.9KV LUG
900V LUG
1KV LUG
3.7 mm MIN SPACE BETWEEN LUG AND WALL
ANODE BOARD HV CONNECTORS
ANODE BOARD SIGNAL CONNECTORS

## Slide 22: Instrument Closeout Installation
EPI-Lo Cross-Section Isometric View
SPIDER CLOSEOUT
WEDGE CLOSEOUT
TOP CLOSEOUT

## Slide 23: Prototype Subassemblies
EM SSD in Holder
EM SSD Assembly
EM MCP Assembly, Top
EM MCP Assembly, Bottom

## Slide 24: Acoustic Test
Conducted at NRL in reverberant chamber
  October 1, 2014
Acceptance test at EDTRD’s MEFL
  135.9 OASPL
  1 minute duration
Protoflight test
  MEFL +3dB
  1 minute duration
Post-test inspection revealed no damage
HUNG FROM CHAMBER CRANE
EPI-Lo Prototype Acoustic Test Unit

## Slide 25: Acoustic Test Unit
Custom test fixture to mimic a single spider quadrant
Anode PWB
2 Prototype Sensor Wedge Assemblies
  EM MCP Assemblies
    Mechanical MCPs
  EM SSD Assemblies
    Energy PWB
  EM Upper Wedge Assemblies
    Included outdated Torlon screw design
  Flight-like grids and foils in all locations
    Most recent grid spacing not included
EPI-Lo Partial Acoustic Test Unit

## Slide 26: Collimator Foil Inspection
No collimator foil damage was noted after the acoustic test
Collimator Foil Inspection (S/N 01, Look Direction #1 Shown)
PRIOR TO ACOUSTIC TEST
AFTER ACOUSTIC TEST

## Slide 27: Start Foil Inspection
No start foil damage was noted after the acoustic test
Start Foil Inspection (S/N 01, Look Direction #4 Shown)
PRIOR TO ACOUSTIC TEST
AFTER ACOUSTIC TEST

## Slide 28: Development Path Forward
Complete purge system design
Complete fabrication of updated designs
Update and complete GSE designs and fabrication
Assemble 2 EM wedges with updated parts
Conduct wedge thermal “stress” test
Conduct wedge blow-down test
Conduct force limited vibration test on ISIS bracket
Complete wire routing and tie down designs
Release EM drawings

## Slide 29: Vibration Test Set-Up
ISIS BRACKET
LOAD CELLS, 8 PLCS
EPI-HI MASS SIMULATOR, SWRI
EM EPI-LO UNIT WITH 2 WEDGES
WEDGE MASS SIMULATORS, 6 PLCS