## Slide 1: 7464-0000 EPI-Lo EDR Structural Analysis
Shaughn London
Packaging Engineer
2014/10/31

## Slide 2: Executive Summary
SPP EPI-Lo instrument analyzed
  Created from EPI-Lo CAD model as of 8/14/2014
  New wedge closeout cover design added to model (10/14/2014)
  Instrument mass modeled as 3.26 kg (7.19 lbm)
Structural model analyzed based on 7434-9039 SPP EDTRD Rev B
  Modal frequencies of assembly, Section 4.4.7.1
  Quasi-static design limit load, Section 4.4.2.1
  Random vibration analysis, Section 4.4.3, NOT done at this time, results dependent on SwRI bracket design
Structural analysis results summary
  All metallic and composite subassemblies have positive margins of safety under Quasi-static loading
This presentation is a preliminary analysis of the baseline EPI-Lo instrument design, complete analysis will be performed pre-CDR

## Slide 3: Background and Methodology
Instrument level structural model created using CAD Model from Designer
  CAD model of instrument dated 8/14/2014
  Wedge assembly updated to latest CAD design as of 10/14/2014
Environmental Structural Requirements (Section 4.4)
  7434-9039 Rev B, SPP Environmental Design and Test Requirements Document
  Subsystem to have min frequency > 80 Hz
  Quasi-static load factor: 32g (Figure 4-11)
  Factors of safety: Table 4-5. Unpressurized Factors of Safety
  Random vibration: not done at this time frame due to dependence on SwRI bracket
Interested in assembly response
  Fundamental frequencies and Interaction of board and chassis
  Chassis response to MAC quasi-static load
  Chassis & PWA dynamic response to random vibration input from 0-2,000 Hz, will be done fore CDR
FEA software
  Pre/Post-processing: Femap V.11
  Solver (static, modal, sine, random: ASD): MSC.Nastran V.2008
  Solver (random: rms/peak): MAYA Structural Analysis Toolkit Pro V5.0.1

## Slide 4: EPI-Lo Overview
EPI-Lo Instrument mounts to SwRI bracket at four mounting posts on Event PWA chassis, offset by four G-10 spacers (for thermal isolation)
EPI-Lo mounting interface NOT parallel to S/C deck, mounting face tilted and rotated about all three axes
SwRI bracket mounts to S/C deck, mounting interface parallel to S/C panel
S/C Interface
SwRI Bracket

## Slide 5: Finite Element Model Overview Instrument Level
Modeling Strategy
  Plate elements where applicable: PWAs, frames, covers
  Solid elements where necessary: frame bosses, bookbolt bosses, small aspect ratios
  PWA: plate elements with EEE part mass smeared over total board area
  Rigid elements (RBE2s): bookbolts, mounting hardware, Connectors
Model size: nodes = 88,811, elements = 70,269
LVPS Cover
Closeout Covers (8x)
LVPS ASSY
Event ASSY
Anode Cover (4x)
Wedges (8x)
Spider ASSY

## Slide 6: Finite Element Model Overview Wedge Assembly
EPI-Lo has 8 identical wedges
Top cover: plate elements, Al-6061 & collimator mass smear
Wedge Frame Insulator: plate and solid elements, Ultem1000
Side cover: beam and solid elements, Al-6061
MCP Cover: plate elements, SS 304
MCP: mass element & RBE3 to MCP cover and baseplate
MCP Baseplate: plate and solid elements, Ultem1000
SSD Assembly: plate elements, Ultem1000
Wedge assembly connected using RBE2s at all bolted interfaces
Front View
Bottom View
Top Cover
MCP Cover
Side View
Top View
MCP Baseplate
Wedge Frame Insulator
Side Cover
Anode ASSY
MCP

## Slide 7: Finite Element Model Overview Wedge Assembly Exploded View

## Slide 8: Finite Element Model Overview Spider & Anode PWAs
Spider frame modeled in detail using plate and solid elements with Al 6061 material properties
Anode PWAs (4x) modeled using plate elements and PWA material properties with estimated board mass smeared across PWA
PWAs connected to Spider frame at mounting hardware bosses using RBE2 elements
Anode PWA (4x)
Top Side
Back Side

## Slide 9: Finite Element Model Overview Event Slice Assembly
Event housing: plate and solid elements, Al 6061 material properties
Event housing thickness .040” at minimum, thicker at bosses
Event PWA: plate elements, PWA material properties and EEE part mass smeared across board
PWA: diameter = 7.5”, thickness = 0.093”
Right-angle MDM connectors modeled with RBE2s from frame to board
PWA connected to housing with RBE2s at mounting bosses
MDM Connectors
Top Side
Back Side

## Slide 10: Finite Element Model Overview LVPS Slice Assembly
LVPS housing: plate and solid elements, Al 6061 material properties
LVPS housing thickness .040” at minimum, thicker at bosses
LVPS PWA: plate elements, PWA material properties and EEE part mass smeared across board
PWA: diameter = 7.5”, thickness = 0.093”
Right-angle MDM connector modeled with RBE2 from frame to board
PWA connected to housing with RBE2s at mounting bosses
MDM Connector
Top Side
Back Side

## Slide 11: Finite Element Model Overview LVPS Covers
EMI & Bottom cover: plate elements, Al 6061 material properties
  EMI cover design is 0.042” thick sheet with center attachment to LVPS frame
  Bottom cover design is 0.062” thick sheet, rib stiffener pattern not included in this analysis iteration (will be for CDR)
EMI Cover
Bottom Cover
EMI Cover
Bottom Cover

## Slide 12: Finite Element Model Overview Wedge & Spider Closeout Covers
Wedge & Spider closeout covers: plate elements, Al 6061 material properties
Wedge closeout covers
  Spoke covers (8x) modeled as .060” thick
  Spoke center cover modeled as .055” thick
  Connected to wedges and spider with RBE2 elements
Spider closeout covers
  Modeled as 0.040” thick
  Connected to spider with RBE2 elements
Spoke Center
Spokes (8x)
Spider Cover (4x)

## Slide 13: Finite Element Model Overview Boundary Conditions
Environmental loading conditions specified in EDTRD reference the S/C panels
  Both in-plane (parallel) and out-of-plane (perpendicular) loading conditions
  SwRI mounting bracket attached to S/C panel
  EPI-Lo mounting interface on bracket not parallel to S/C panels
Bracket not modeled at this time, will be for CDR
For EDR, EPI-Lo FEM “spidered” (RBE2) to origin node, assume hard-mounted configuration with instrument parallel and perpendicular to S/C C.S.
Z
Y
X
B.C. Node

## Slide 14: Mass and Material Properties
Mass breakdown table shown on next slide, reflects CBE (2014/10/07)
FEM mass tailored to match estimated EPI-Lo configuration plus approximately 3% margin for unaccounted for items
FEM board mass approximately 3% greater than CBE PWA mass
  Unaccounted for mechanical, staking, conformal coat, etc.
  More conservative approach, yields lower PWA frequency and larger displacement
EEE component mass smeared on PWAs, does not take into account local stiffening and mass of large EEE parts on PWA dynamic effects
Not modeled discretely: internal harnesses, bookbolt mass and connector mass
Model material property table shown below
Properties allocated as noted in previous slides
Material | E (Msi) | Yts (ksi) | Uts (ksi) | ρ (lbm/in3) | ν
PWA | 3.5 | N/A | 35 | N/A | 0.30
Al 6061 | 9.9 | 35 | 42 | 0.098 | 0.33
SS 304 | 30.0 | 45 | 80 | 0.289 | 0.29
Ultem 1000 | 0.4 | 16 | 16.5 | 0.046 | 0.30

## Slide 15
Item Desc (Sub-ASSY) | Part # | Material | Est. Mass (Ea.) |  | FEM Mass (lb) | Qty (ea) | Est Mass (Total) |  | FEM Mass (total) |  | % Diff.
 |  |  | (lb) | (g) |  |  | (lb) | (g) | (lb) | (g) | 
Sensor Head ASSY | 7464-1000 |  | 0.377 | 184.7 | 0.390 | 8 | 3.018 | 1370.4 | 3.117 | 1415.0 | 3%
Wedge Top Cover | 7464-1206 | Al 6061 | 0.103 | 46.8 | 0.139 | 8 | 0.825 | 374.7 | 1.115 | 506.3 | 35%
Collimators (per wedge) |  | Al 6061 | 0.020 | 9.3 |  | 8 | 0.164 | 74.3 |  |  | 
Wedge Frame Insulator | 7464-1202 | Ultem 1000 | 0.012 | 5.5 | 0.014 | 8 | 0.098 | 44.4 | 0.110 | 50.1 | 13%
Wedge Side Cover (L) | 7464-1201-09 | Al 6061 | 0.018 | 8.3 | 0.018 | 8 | 0.146 | 66.1 | 0.142 | 64.3 | -3%
Wedge Side Cover (R) | 7464-1201-10 | Al 6061 | 0.017 | 7.7 | 0.017 | 8 | 0.136 | 61.8 | 0.132 | 59.9 | -3%
MCP Housing | 7464-1101 | Ultem 1000 | 0.037 | 17.0 | 0.043 | 8 | 0.299 | 135.7 | 0.346 | 156.9 | 16%
MCP (2x) | 7464-1110 |  | 0.050 | 22.7 | 0.050 | 8 | 0.400 | 181.8 | 0.400 | 181.6 | 0%
MCP Cover | 7464-1105 | SS - 304 | 0.071 | 32.4 | 0.075 | 8 | 0.570 | 258.8 | 0.600 | 272.2 | 5%
SSD Assembly | 7464-1300 |  | 0.030 | 13.4 | 0.034 | 8 | 0.237 | 107.5 | 0.272 | 123.7 | 15%
SSD Housing | 7464-1303 | Ultem 1000 | 0.005 | 2.5 |  | 8 | N/A | N/A | N/A | N/A | 
SSD Cover | 7464-1203 | SS - 304 | 0.014 | 6.4 |  | 8 | N/A | N/A | N/A | N/A | 
SDD PWB | 7464-1354 | PWB | 0.003 | 1.4 |  | 8 | N/A | N/A | N/A | N/A | 
Connectors (SSD) | N/A |  | 0.007 | 3.2 |  | 8 | N/A | N/A | N/A | N/A | 
Wedge Hardware + Misc. | N/A |  | 0.018 | 8.2 |  |  |  |  |  |  | 
Anode PWB | 7464-5302 | PWB | 0.176 | 79.8 | 0.182 | 4 | 0.703 | 319.2 | 0.726 | 329.8 | 3%
Spider Frame | 7464-0100 | Al 6061 | 0.704 | 319.5 | 0.724 | 1 | 0.704 | 319.5 | 0.724 | 328.7 | 3%
Spider Cover | 7464-0102-01 | Al 6061 | 0.049 | 22.4 | 0.050 | 3 | 0.148 | 67.3 | 0.149 | 67.6 | 0%
Spider Cover | 7464-0102-03 | Al 6061 | 0.050 | 22.8 | 0.050 | 1 | 0.050 | 22.8 | 0.050 | 22.9 | 0%
Event PWA Housing | 7464-4005 | Al 6061 | 0.346 | 156.9 | 0.370 | 1 | 0.346 | 156.9 | 0.370 | 168.1 | 7%
Event PWA | 7464-4004 | PWB | 0.540 | 245.2 | 0.555 | 1 | 0.540 | 245.2 | 0.555 | 251.7 | 3%
LVPS PWA Housing | 7464-3005 | Al 6061 | 0.291 | 132.1 | 0.334 | 1 | 0.291 | 132.1 | 0.334 | 151.5 | 15%
LVPS PWA | 7464-3004 | PWB | 0.496 | 225.2 | 0.513 | 1 | 0.496 | 225.2 | 0.513 | 232.8 | 3%
Bottom Closeout Cover | 7464-0101 | Al 6061 | 0.272 | 123.6 | 0.266 | 1 | 0.272 | 123.6 | 0.266 | 120.7 | -2%
EMI Cover | 7464-0104 | Al 6061 | 0.202 | 91.5 | 0.185 | 1 | 0.202 | 91.5 | 0.185 | 84.2 | -8%
Harness Cover | 7464-0108 | Al 6061 | 0.010 | 4.4 |  | 1 | 0.010 | 4.4 |  |  | 
closeout Cover (Spoke) | 7464-0021 | Al 6061 | 0.022 | 10.1 | 0.022 | 8 | 0.178 | 80.8 | 0.174 | 78.8 | -2%
closeout Cover (Hub) | 7464-0022 | Al 6061 | 0.027 | 12.0 | 0.028 | 1 | 0.027 | 12.0 | 0.028 | 12.7 | 5%
Ti Bookbolts |  | Ti | 0.010 | 4.4 |  | 4 | 0.039 | 17.8 |  |  | 
Misc Hardware |  |  | 0.001 | 0.4 |  | 32 | 0.025 | 11.5 |  |  | 
 |  |  | Instrument Totals |  |  |  | 7.048 | 3,200 | 7.191 | 3,265 | 3%

## Slide 16: Model Checkout and Modal Analysis
Model checkouts were performed
  1g check, ensures model grounded and force sum matches model mass
  Grid point singularity table check for proper autospc
  Modal free check for rigid body motion, modes 1-6 & mass participation = 100%
Modal analysis of flight config. performed to find fundamental frequencies of system
Instrument oriented in hard-mounted configuration
EDTRD: instrument min freq must be greaten than 80 Hz
Desire min PWA freq > 150 Hz
Try to avoid modal coupling of subassemblies & chassis
  Causes large displacements/stresses
  Ideally design for octave rule (2x) separation of PWAs and chassis
Modal summary results on next slide
  Event PWA mode #1 = 388 Hz (out-of-plane)
  LVPS PWA mode #1= 406 Hz (out-of-plane)
  First Instrument mode at 502 Hz (out-of-plane, and rotation about base)
  PWA & instrument freqs. well separated in directional responses

## Slide 17: Modal Analysis Results Summary Modal Effective Mass Fraction
Desc. | Mode# | Freq (Hz) | Tx | Ty | Tz | Rx | Ry | Rz
Bottom Cover, Mode #1 | 1 | 321.6 | 0.0% | 0.0% | 3.6% | 1.7% | 0.0% | 0.0%
Event PWA, Mode #1 | 2 | 388.5 | 0.0% | 0.1% | 12.4% | 4.3% | 0.1% | 0.0%
LVPS PWA, Mode #1 | 3 | 406.6 | 0.0% | 0.0% | 5.3% | 4.4% | 0.0% | 0.0%
LVPS PWA, Mode #2 | 4 | 441.3 | 0.0% | 0.3% | 2.3% | 0.1% | 0.2% | 0.0%
Event PWA, Mode #2 | 5 | 482.5 | 2.7% | 3.9% | 0.0% | 8.6% | 16.0% | 0.9%
LVPS PWA, Mode #3 | 6 | 491.6 | 4.0% | 1.3% | 0.1% | 3.3% | 15.3% | 2.3%
Instrument, Mode #1 | 7 | 502.1 | 6.9% | 15.5% | 0.5% | 18.1% | 18.9% | 4.4%
Instrument, Mode #2 | 8 | 507.8 | 11.6% | 7.5% | 3.5% | 1.5% | 26.0% | 5.0%
Event PWA, Mode #3 | 9 | 528.6 | 4.4% | 0.0% | 5.7% | 5.0% | 7.9% | 1.9%
Instrument, Mode #3 | 10 | 559.9 | 0.0% | 1.0% | 43.6% | 32.4% | 1.5% | 0.1%
EMI Cover, Mode #1 | 15 | 664.2 | 0.0% | 0.0% | 0.3% | 0.2% | 0.0% | 0.0%
Anode PWAs, Mode#1 | 70 | 1,147.0 | 0.0% | 0.0% | 4.9% | 2.7% | 0.1% | 0.0%
Anode Cover, Mode#1 | 98 | 1,402.2 | 0.1% | 0.6% | 0.0% | 0.0% | 0.0% | 0.2%
Sum Total | 244 | 2,000 | 86% | 90% | 87% | 89% | 86% | 89%
*Ti = translation in i-direction, Ri = rotation about i-axis

## Slide 18: Mode Shapes for Various Components
Mode #2, 389 Hz, Event PWA
Mode #3, 407 Hz, LVPS PWA
Mode #7, 502 Hz, Instrument
Mode #1, 321 Hz, Bottom Cover
Mode #8, 508 Hz, Instrument
Mode #10, 560 Hz, Instrument

## Slide 19: Quasi-Static Analysis von Mises Stress
Model analyzed for von Mises stress under quasi-static loading
Model simulated in hard-mounted condition, bracket not included
Interested mainly in chassis and PWA stress
Fastener analysis not done at this time
Factors of safety (FoS) taken from 7434-9039 SPP EDTRD rev B, table 4-5.
  Metallic structures: FoSu = 1.4, FoSy = 1.25
  Composite (PWA + Ultem1000): FoSu = 1.5, FoSy = N/A
Margins of safety (MoS) calculations performed,
  MoS formula ->
  MoS table on the following slide
All margin of safety results are positive under 32g quasi-static load in hard-mounted condition

## Slide 20: Quasi-Static Analysis MoS Table
Description | Strength (ksi) |  | Factor of Safety |  | Margin of Safety (Yield) |  |  | Margin of Safety (Ult) |  | 
 | Yield | Ultimate | Yield | Ultimate | Z-Axis | X-Axis | Y-Axis | Z-Axis | X-Axis | Y-Axis
Wedge Top Cover | 35 | 42 | 1.25 | 1.4 | 15.08 | 12.34 | 12.54 | 16.65 | 13.63 | 13.85
Wedge Frame Insulator | N/A | 16.5 | N/A | 1.5 | N/A | N/A | N/A | 47.25 | 66.48 | 67.75
Wedge Side Cover | 35 | 42 | 1.25 | 1.4 | 12.27 | 10.94 | 11.10 | 13.56 | 12.10 | 12.28
MCP Housing | N/A | 16.5 | N/A | 1.5 | N/A | N/A | N/A | 3.45 | 8.17 | 4.26
MCP Cover | 31 | 71 | 1.25 | 1.4 | 10.46 | 15.74 | 15.86 | 17.63 | 26.21 | 26.41
SSD Assembly | N/A | 16.5 | N/A | 1.5 | N/A | N/A | N/A | 353.84 | 353.84 | 477.26
Anode PWB | N/A | 35 | N/A | 1.5 | N/A | N/A | N/A | 66.63 | 61.39 | 62.58
Spider Frame | 35 | 42 | 1.25 | 1.4 | 7.90 | 8.94 | 9.72 | 8.77 | 9.91 | 10.76
Spider Cover | N/A | 16.5 | N/A | 1.5 | 43.75 | 35.26 | 35.07 | 48.10 | 38.79 | 38.58
Event PWA Housing | 35 | 42 | 1.25 | 1.4 | 3.99 | 6.77 | 6.93 | 4.48 | 7.53 | 7.70
Event PWA | N/A | 35 | N/A | 1.5 | N/A | N/A | N/A | 27.08 | 51.79 | 55.22
LVPS PWA Housing | 35 | 42 | 1.25 | 1.4 | 17.56 | 45.58 | 32.80 | 19.37 | 50.11 | 36.08
LVPS PWA | N/A | 35 | N/A | 1.5 | N/A | N/A | N/A | 26.61 | 310.11 | 249.90
LVPS PWA Housing Cover | 35 | 42 | 1.25 | 1.4 | 16.63 | 104.17 | 92.64 | 18.34 | 114.38 | 101.74
EMI Cover | 35 | 42 | 2.53 | 2.68 | 20.79 | 46.89 | 41.79 | 22.90 | 51.54 | 45.95
closeout Cover (Spoke) | 35 | 42 | 1.25 | 1.4 | 44.05 | 63.64 | 65.69 | 48.42 | 69.92 | 72.17

## Slide 21: Quasi-Static Analysis PWA von Mises Stress
PWA von Mises results for the Event and LVPS assemblies: highest stress under out-of-plane loading (Z-axis)
Occur at PWA/housing mounting locations
Event PWA MoSu: 27 (Z-axis), 52 (X-axis), 55 (Y-axis)
LVPS PWA MoSu: 27 (Z-axis), 310 (X-axis), 250 (Y-axis)
psi
Event PWA (Out-of-Plane Loading)
psi
LVPS PWA (Out-of-Plane Loading)

## Slide 22: Quasi-Static Analysis Frame von Mises Stress
Frame results for the Spider, Event and LVPS assemblies: highest stress under out-of-plane loading (Z-axis)
Spider Frame MoS (min): 7.9 (Z-axis), 8.9 (X-axis), 9.7 (Y-axis)
Event Frame MoS (min): 4.0 (Z-axis), 6.8 (X-axis), 6.9 (Y-axis)
LVPS Frame MoS (min): 17 (Z-axis), 45 (X-axis), 32 (Y-axis)
LVPS Frame
psi
psi
psi
Spider Frame
Event Frame

## Slide 23: Quasi-Static Analysis Cover von Mises Stress
Highest stress results for the Spider cover (Y-axis), EMI cover and bottom cover (Z-axis)
Spider Cover MoS (min): 43 (Z-axis), 35 (X-axis), 35 (Y-axis)
EMI Cover MoS (min): 20 (Z-axis), 46 (X-axis), 41 (Y-axis)
Bottom Cover MoS (min): 16 (Z-axis), 104 (X-axis), 92 (Y-axis)
Bottom Cover
psi
psi
psi
Spider Covers
EMI Cover

## Slide 24: Summary
Quasi-static and Modal analyses performed for the stand-alone EPI-Lo Instrument
MSC.Nastran and Femap used for analysis
  Model simplified wherever possible to aid solution time
  PWAs modeled as plate elements with uniform stiffness, thickness and density
  Instrument analyzed as hard-mounted, SwRI bracket configuration not included
  Passed all model checks; Modal free analysis and 1g static loads in all 3 directions
Modal analysis performed, 1st mode = 321 Hz (bottom cover), Instrument mode #1 = 502 Hz
Analysis environmental input levels per 7434-9039 SPP EDTRD Rev B
  Analysis performed for all three orthogonal axes relative to instrument coordinate system
  Quasi-static analysis per MAC
  Random vibration analysis to be performed for CDR
All margin of safety positive for 32 g quasi-static loading