## Slide 1: EPI-Hi LVPS Review D. Do

## Slide 2: Input Requirements
Bus Voltage: 24-35Vdc
Inrush Current: <10A <10us, <4x or 2.5A <2ms
EMI

## Slide 3: LVPS Output Requirements
 | Min Load (mA) | Max Load (mA)
+1.5V | 50 | 150
+1.8V | 20 | 60
+3.3V | 145 | 430
+6V | 79 | 500
+12V | 8 | 64
-6V | 6 | 19

## Slide 4: EPI-Hi Block Diagram

## Slide 5: EM board
Main Converter
Sync clk
EMI
Pri Shield
Secondary
Shield
Linear
Regulators
Output
Connector
Input
Con.

## Slide 6: EM with shield

## Slide 7: Regulation
Voltage | Min | Max | Min Load | Nom Load | Max Load
+1.53 | +1.51 | +1.55 | 1.531 | 1.522 | 1.514
+1.82 | +1.8 | +1.84 | 1.815 | 1.81 | 1.81
+3.41 | +3.37 | +3.45 | 3.414 | 3.41 | 3.407
+6 | 5.8 | +6.2 | 6.2 | 5.98 | 5.97
+12 | +11.52 | +12.48 | 11.93 | 12.02 | 11.68
-6 | -6.2 | -5.8 | -5.98 | -6 | -6
Pri Current |  |  | 58mA/295mV | 144mA/728mV | 233mA/1.143V
Voltage | Min | Max | +1.53 Max | +1.82 Max | +3.41 max | +6 Max | +12 Max | -6 Max
+1.53 | +1.51 | +1.55 | 1.514 | 1.53 | 1.53 | 1.53 | 1.53 | 1.53
+1.82 | +1.8 | +1.84 | 1.815 | 1.81 | 1.81 | 1.815 | 1.815 | 1.815
+3.41 | +3.37 | +3.45 | 3.414 | 3.414 | 3.407 | 3.414 | 3.414 | 3.414
+6 | 5.8 | +6.2 | 6.19 | 6.18 | 6.19 | 5.85 | 6.2 | 6.19
+12 | +11.52 | +12.48 | 11.92 | 11.94 | 11.98 | 13.47 | 11.685 | 11.92
-6 | -6.2 | -5.8 | -5.91 | -5.93 | -5.84 | -6.07 | -6.11 | -5.9
31V Input
Cross Regulation

## Slide 8: Efficiency
Current efficiency at Nom load is > 75%.

## Slide 9: Output Ripple
Ripple is low but turn on spike is high.
Additional ceramic caps and common mode filter are placed on EM board.

## Slide 10: Turn on

## Slide 11: Inrush Current

## Slide 12: Design Status
Final Part placement EPI LVPS is in progress.
Routing EPI-Hi LVPS starting next week
EM delivered and integrated with EPI-Hi instrument