## Slide 1
Matt Hill
EPI-Lo Deputy Lead Co-I (JHU/APL)
This document contains technical data that may be controlled by the International Traffic in Arms Regulations (22 CFR 120-130) and may not be provided, disclosed or transferred in any manner to any person, whether in the U.S. or abroad, who is not 1) a citizen of the United States, 2) a lawful permanent resident of the United States, or 3) a protected individual as defined by 8 USC 1324b(a)(3), without the written permission of the United States Department of State.
Pre-CDR Peer Review
(not a CDR run-through)
6 NOV 2014
EPI-Lo Sensor Review – Part 1 Matt Hill (JHU/APL) Deputy EPI-Lo Lead
Notes: introduction

## Slide 2: End-to-End: Particles-to-Data Products
1. Science requirements
2. Environment: overview of foreground and background ions, electrons, photons, and dust.
- protons and electron spectra, worst case, expected variation over the mission
- expected dust impacts on the sensor (environment, and our Boulder test results)
- light (ticker foils towards the sun, light getting through dust holes, etc.)
3. Foreground measurement: how the sensor head works to measure what we want to measure.
- how ions are measured (MCP/foils/2ndary e- for start/stop signal & pos., SSD for energy in ion & particle SSDs.
- how electrons are measured (the SSD-only detection in the particle detector & supplemental start pos. sensing)
- calibration to support these measurements
4. Background: how penetrators, solar wind e-, light, & dust interferes w/ our measurements and our mitigations.
- penetrating electrons and protons
- solar wind electrons (and protons)
- photon background rates
- internally generated secondaries
- electronics noise
- calibration/simulations to support these background estimates
5. Event Logic: Break the measurements into specific energy ranges, species, etc.
- block diagram
- event modes
- species measured during each mode
- supporting measurements: singles rates, etc.
6. Data: what products are we collecting and returning.
- main data products: species, energy, angular, temporal resolution
- subsidiary data products: event data, burst data, histogram data
7. Summary/Closure: Summary of presentation and how the data we’re getting responds to the requirements.

## Slide 3: Measurement Requirements (L3s)

## Slide 4: Key L4 Requirements: Composition

## Slide 5: Key L4 Requirements: Geometry Factor

## Slide 6: Key L4 Requirements: Count Rate

## Slide 7: Instrument Overview

## Slide 8: Instrument Overview
EPI-Lo Cross-Section View Isometric
POWER SUPPLY ASSY
EVENT PWB ASSY
ANODE PWB ASSY

## Slide 9: Instrument Overview

## Slide 10: Sensor Overview:
First
  xxxxx
  xxxxxx
Second
Third
  xxxxxx
  xxxx
Forth
  xxxxxxx
  xxxxxx
Microchannel
Plate (MCP)
Anode
Solid State
Detectors (SSDs)
Stop Foil
Start Foils
Collimators
Baffles
MCP Grid
Start Acceleration
Grid
Stop Accel. Grid
MCP Spacer
Start Foils
Collimator
Foil
Collimator Foil
start accel. grid holes need to be updated

## Slide 11: Sensor Voltages
Ground
1000 V
Equipotential
Volume
900 V
2900 V
3000 V
start e-
acceleration
region
MCP
Anode
Ground
stop e-
accel.
region
SSDs
All Foils
at Ground
100 V retarding
potential region
start accel. grid holes need to be updated

## Slide 12: Foreground Measurement: Ions
Incident ion trajectory
Start electron trajectory
Stop electron trajectory
MCP
Anode
SSDs
start accel. grid holes need to be updated

## Slide 13: Foreground Measurement: Ions
Ion Measurement Logic can toggle TOF, but no TOF  no species identification
start accel. grid holes need to be updated

## Slide 14: Foreground Measurement: Electrons
Secondary
electrons
(infrequent)
MCP
Anode
SSDs
Incident Electron
start accel. grid holes need to be updated

## Slide 15: Foreground Measurement: Electrons
Secondary Electrons from Start Foils possible, but Low Probability;
Start Electron only identifies entrance aperture
Stops from secondaries not indentifiable
start accel. grid holes need to be updated

## Slide 16: Secondary Electrons & Potentials
100 V retarding
potential region
Equipotential
Volume
2300 V
Across Plates
100 V
MCP-to-Anode
Grid
Grid
Grid
MCP
Anode
SSDs
1000 V start e-
acceleration
region
1000V
stop e-
accel.
region
start accel. grid holes need to be updated

## Slide 17: Foils
Nominal Start Foils
Mesh
50A Carbon
400A Polyimide
300A Aluminum
200A Palladium
50A Carbon
Thick Start Foils
Mesh
50A Carbon
500A Polyimide
1000A Aluminum
500A Palladium
50A Carbon
Collimator Foils
Mesh
1000Å of polyimide
50Å C flashing (inward-facing side)
Stop Foils
50A Carbon
200A Aluminum
350A Polyimide
Grid mesh
50A Carbon.

## Slide 18: Solid State Detectors
Ion SSD
700 micron
0.91 cm2 active area
50 nm dead-layer
Particle SSD
700 micron
3.2 micron Al flashing
0.81 cm2 active area
50 nm dead-layer
Anti-Coincidence SSD
700 micron
0.86 cm2 active area
50 nm dead-layer
Behind P-SSD (and part of I-SSD)

## Slide 19
Begin
End
pad connection
image of bottom (component side) of board is flipped to align with front (pad side)
pad
EPI-Lo Anode Board
2014-04-07 meh
A-5
A-7
A-9
A-8
A-6
A-4
A-0
A-1
A-2
A-3
A-10
A-11
A-12
A-13
A-15
A-17
A-19
A-18
A-16
A-14
Side A1
Side A2
Anode Board A
(example of boards A, B, C, and D)
Anode Pad Naming
L13
L12
L11
L10
L15
L14
L17
L16
L18
L19
L03
L02
L01
L00
L05
L04
L07
L06
L08
L09
A-20
A: Looking down on the board
Electrical
Science
Wedge 1
Wedge 0

## Slide 20
Start-Electron footprint mapping using a 2-D anode
Prevent Stop-Electron interference by shifting all HVs down by 1kV.
Sources in
apertures 5-9
x
y

## Slide 21
Sensor wedge mounted on EM Quadrant Anode Board
MCP Mask, Interplate spacer Mask
Readout still with lab electronics; NIM modules & LeCroy Scope.

## Slide 22: Instrument Performance

## Slide 23
Elevation 1
Elevation 2
Elevation 3
Elevation 4
Elevation 5
Initial Energy Distribution
Electron Dispersion
Hit Locations
Sample Trajectories
23
Name | Mean TOF (ns) | FWHM (ns)
Elevation 1 | 0.93 | 0.12
Elevation 2 | 2.12 | 0.08
Elevation 3 | 2.35 | 0.04
Elevation 4 | 2.32 | 0.05
Elevation 5 | 2.26 | 0.08
Stops | 5.23 | 0.09
SIMION, Allegrini Energy Distribution

## Slide 24
Elevation 1
Elevation 2
Elevation 3
Elevation 4
Elevation 5
Initial Energy Distribution
Electron Dispersion
Hit Locations
Sample Trajectories
24
Electron Dispersion
SIMION, Allegrini Energy Distribution
Name | Mean TOF (ns) | FWHM (ns)
Elevation 1 | 0.93 | 0.12
Elevation 2 | 2.12 | 0.08
Elevation 3 | 2.35 | 0.04
Elevation 4 | 2.32 | 0.05
Elevation 5 | 2.26 | 0.08
Stops | 5.23 | 0.09

## Slide 25: Microchannel Plate (MCP)
Simulation (black) versus measured centroids (red)
The misalignment in Y-direction was due to a registration offset in the setup
The offset in the X direction for the left-most data was caused by an obstruction at the edge of the MCP mount that has since been eliminated

## Slide 26: x – y positions, bin width=4ns (~0.8mm)
X 
Y 

## Slide 27: Comparison of mask and open MCP grid: X

## Slide 28: Comparison of mask and open MCP grid: Y

## Slide 29: Particles and Counting Rates

## Slide 30
Fluxes evaluated in the region from 9.5 – 30 Solar Radii (<0.14 AU)
Orbits

## Slide 31
Initial data are integral intensities of ACE/EPAM protons over the 30 keV – 4.75 MeV range (1 hr avg)
Lowest EPAM energy is 66, so low-energy slope was used to extrapolate down to the 30 – 66 keV range
The year 1998 is selected as representative of the time in the cycle analogous to the 2018 Launch date. This is an “active mission” condition because solar max conditions persist during the min perihelia.

## Slide 32
- Start at a given launch date, use the 1 AU flux and calculate the flux at the SPP position (using a power-law radial flux dependence) as it progresses in its orbits. Do this for each hour and histogram the number of occurrences (hours) in a given intensity bin.
- Do this for many launch times to account for the randomness of when particular events will occur (that is to account for the fact that a high-intensity event could take place when SPP is near the Sun or could happen when SPP is far from the Sun).

## Slide 33: Proton Intensity

## Slide 34
Protons
Proton Intensity

## Slide 35: Worst Case Protons

## Slide 36: Environment
Electron Spectra, expected, worst case, etc.

## Slide 37
Electrons
103.2 cm-2s-1sr-1MeV-1

## Slide 38: Environment
Electron Spectra, expected, worst case, etc.

## Slide 39: Anti-coincidence System: GEANT Setup
Improved setup for GEANT4 model of electron SSD anticoincidence

## Slide 40: Anti-coincidence System: GEANT Results
Assumed electron flux of j(E) ~ E– 2.65 from ~10 keV to ~5 MeV
Penetrator rejection efficiency range from 83% to 95% from 1 MeV up to 10 MeV incident electron energy
Following peer review result of S/N of ~3 for foreground electrons with anti-coincidence, higher fidelity sensor model yields S/N ~10
New GEANT model accounts for more realistic geometry and extra shielding by structure
Only ~1% of electrons below 2 MeV penetrate to detectors in this model

## Slide 41: Particle Intensities and Rates

## Slide 42: Particle Intensities and Rates

## Slide 43: Particle Intensities and Rates

## Slide 44: Particle Intensities and Rates

## Slide 45: Environment: Dust

## Slide 46: Light

## Slide 47: Field of View

## Slide 48
A1
A2
B1
B2
C1
C2
D1
D2
Cutout for connectors
Mechanical/Electrical

## Slide 49
A1
A2
B1
B2
C1
C2
D1
D2
Sun
Mechanical/Electrical

## Slide 50
TPS
Solar
Array
Limb
Sensor
Limb Sensor
EPI-Hi
WISPR
FIELDS
FIELDS
Mag Boom
3
2
1
0
7
6
5
4
0
1
2
3
4
5
6
7
Science
B2
B1
A2
A1
D2
D1
C2
C1
A1
A2
B1
B2
C1
C2
D1
D2
Engineering/Electrical
Science – Wedges/octants are named 0 to 7 counter-clockwise on sky, starting from EPI-Hi directed wedge (designed to match up with A1-D2 scheme.
Mechanical/Electrical – Quadrants are named A,B, C or D (corresponding to an anode board) with a 1 or a 2 designating which wedge/octant (which side of the board). Naming proceeds clockwise on instrument (viewed from above): A1, A2, B1, etc.
Looking at the Sky
Field of View

## Slide 51: ISIS EPI-Lo Repositioning
.060 inches below 8 degree umbra
Focal point .284 inches lower on instrument axis
Angled to minimize TPS obstruction
REPOSITIONED
ORIGINAL POSITION

## Slide 52: ISIS EPI-Lo FOV With Parker Probability
ORIGINAL FOV
REPOSITIONED FOV

## Slide 53: ISIS EPI-Lo FOV With Parker Probability
ORIGINAL FOV
REPOSITIONED FOV

## Slide 54
W0
W1
A1
A2
L13
L12
L11
L10
L15
L14
L17
L16
L18
L19
L03
L02
L01
L00
L05
L04
L07
L06
L08
L09
Mechanical / Science – Apertures are named from 0 to 9 for each wedge, counter-clockwise on sky starting on lowest elevation angle row.
For science only, all 80 holes are named from 00-79 by combining the wedge number and aperture number. Individual octants/wedges are named with a preceding W, thus there are eight octants named W0-W7. Individual holes are named with a preceding L (for look direction) so we have 80 apertures named L00-L79.
Aperture naming
Look directions associated with Anode Board A
Mechanical / Science
Electrical
Looking at the Sky

## Slide 55: Instrument Overview

## Slide 56: Particle FOV
RAM
SUN
UNOBSTRUCTED FOV
OBSTRUCTIONS TO FOV
56
FIELDS
Deployed Solar Array
TPS Leading Edge
ADCOLE Head
WISPR
EPI-Hi
ADCOLE Head
MAG Boom

## Slide 57: Ion FOV
RAM
SUN
UNOBSTRUCTED FOV
OBSTRUCTIONS TO FOV
57
FIELDS
Deployed Solar Array
TPS Leading Edge
ADCOLE Head
WISPR
EPI-Hi
ADCOLE Head
MAG Boom

## Slide 58: Particle and Ion FOV’s
RAM
SUN
PARTICLE FOV
ION FOV

## Slide 59: Particle and Ion FOV’s
SUN
PARTICLE FOV
ION FOV

## Slide 60: Start Foil FOV
RAM
SUN