## Slide 1: EPI-Lo Sensor Review – Part 2 Matt Hill (JHU/APL) Deputy EPI-Lo Lead
Matt Hill
EPI-Lo Deputy Lead Co-I (JHU/APL)
This document contains technical data that may be controlled by the International Traffic in Arms Regulations (22 CFR 120-130) and may not be provided, disclosed or transferred in any manner to any person, whether in the U.S. or abroad, who is not 1) a citizen of the United States, 2) a lawful permanent resident of the United States, or 3) a protected individual as defined by 8 USC 1324b(a)(3), without the written permission of the United States Department of State.
Pre-CDR Peer Review
(not a CDR run-through)
6 NOV 2014
Notes: introduction

## Slide 2: Composition and Energy Coverage

## Slide 3: Composition and Energy Coverage
Don’s prescription: simulate 3He by scaling alpha E -> 0.75E and population to a fraction.
S/B ~ 3
Aperture 4

## Slide 4: Energy Coverage: Fe absorber Method

## Slide 5: Energy Coverage: H, e- dE/dx vs E method

## Slide 6: Calibration

## Slide 7: EPI-Lo Calibration
EPI-Lo measurements are intended to generate the information needed to derive differential intensities (j[cm2 -sr-s-keV]-1)
The goal of EPI-Lo characterization and calibration efforts is to develop the quantitative procedures for converting the count rates (R [counts s-1]) reported by EPI-Lo into estimates of j for the various defined ranges of energies, particle species, and arrival angles
“Calibration” for a particle instrument like EPI-Lo means determining the following:
  Transfer function from counts into flux (physical units)
  Characteristic of “Rate-in” versus “Rate-out”
  Response to visible and ultraviolet light
  Response to high energetic particle backgrounds

## Slide 8: Calibration Types
Foreground
  Ions and electrons in the energy range of interest to the instrument
Background
  Electrons
  Characterize the rates from penetrating radiation
  Characterize response to Solar Wind and/or photoelectron impact
Light
  Characterize rejection of UV background, primarily H-alpha
  Characterize rejection of sunlight and glint

## Slide 9: Tests at Instrument Level
*Science requires relative/absolute accuracy: 20%/50%. Ground calibration 20% precision, reduced to 10% in flight.
30

## Slide 10: Foreground Calibration Requirements
Foreground Electrons
  40 keV to 1000 keV (Needed for understanding backgrounds)
    1 keV to 30 keV Electron Gun at APL
    30 keV to 100 keV Radioactive sources at APL
    125 keV to 1.6 MeV Accelerator at GSFC
Foreground Ions (H, He3, He4, O, Fe)
  40 keV to 15000 keV (Level 4 Requirements)
  (Goal: protons to 20 MeV)
    3 keV to 170 keV Accelerator at APL (November 2014)
    30 keV to 5 MeV Degraded alpha sources (already begun)
    125 keV to 1.6 MeV Accelerator at GSFC (16-27 Feb 2015)
    1 MeV to 20 MeV Accelerator at LBL (1 April 2015)
    ~40 MeV Fe Californium source 40 MeV 40-50 amu particles.

## Slide 11: Background Calibration Requirement
Background Electrons
  2 eV to 10 MeV (from the expected environment)
    1 eV to 100 eV Hot filament at APL
    1 keV to 50 keV Electron Gun at APL
    125 keV to 1.6 MeV Accelerator at GSFC
    1 MeV to 10 MeV Accelerator at Idaho (uncertain)
Background Ions
  3 keV to 50 MeV (from the expected environment)
    3 keV to 170 keV Accelerator at APL
    30 keV to 5 MeV Degraded alpha sources
    125 keV to 1.6 MeV Accelerator at GSFC
    1 MeV to ~100 MeV Accelerator at LBL
Photons
  UV and visible lamps at APL (need to look into this)

## Slide 12: Dust

## Slide 13: Background Measurement: Dust

## Slide 14: Background Measurement: Dust

## Slide 15: Dust: U of ColoradoTest

## Slide 16: Collimators and Start Foils
Foils Mount on Apertures (red)
    Each elevation tailored for equal geometric factors
    Second foil at intermediate baffle (vented)
Collimators screw-mount to outer cover, capture foils
    Each elevation and azimuth is unique

## Slide 17: Flight Experience with Dust: Cassini

## Slide 18: Dust: Simulating the Environment
Expect ~10 damage-inducing hits on each unprotected foil during entire mission
Reduced to ~1 hit per mission with collimator
Can lower further with pairs of pinholes
Bare Start Foil
Start Foil Behind Collimator

## Slide 19: Environment: Dust

## Slide 20: Environment: Dust
Smallest foil
106 mm2

## Slide 21: Environment: Dust
Smallest foil
106 mm2

## Slide 22: Light

## Slide 23: Light

## Slide 24: Light and Dust Mitigation (2/2)
Dust may produce pairs of pinholes in the Start and collimator foils
  Foils are designed to stop solar-wind-energy electrons
  Pinhole pairs allow will still allow access to solar-wind electrons
Solar wind electrons have an energy of ~100 eV or less
Electrons that “leak in” through apertures are indistinguishable from Start secondary electrons
Solar wind electron flux ~2 x 1012/cm2-s-sr
Estimate foil pinhole as size of a support grid element is ~4.9 x 10-5 cm2
Geometric factor of a pair of pinholes separated by ~0.5cm is ~1.3 x 10-8
  The flux through a pinhole pair can be estimated as ~2.6 x 104/s
  If every aperture had 1 grid-element pinhole, the total for a quadrant would be ~5.0 x 105/s
  This rate would be well tolerated by the electronics processing
Such a pinhole pair would result in UV induced counting rates ~10/s

## Slide 25: Status of EPI-Lo Scattered / Stray Light Analysis
Develop a stray light analysis of the EPI-Lo instrument that incorporates the reverse raytrace from the detector to object space
The reverse raytrace will result in three products:
  An antenna diagram of EPI-Lo projecting onto angular space of the sky (in progress)
  A reverse raytrace from the start foils to critical objects in the scattered FOV to model their reflectance and blackbody emission (in progress)
  A reverse raytrace from the start foils to critical objects, which scatter toward a disk representing the sun to model the scatter of the sun to the detector via s/c objects (TBD)
Assumptions:
The reverse raytrace is validated by the general radiance theorem
The reverse raytrace can yield the Geometrical Configuration Factor (GCF), which quantifies the mapping of projected area to projected solid angle
The GCF is scaled by the brightness of the source to determine the effective scatter/stray light power
The assigned scatter models, coating properties, and wavelength ranges supplied by the instrument designers represent the EPI-Lo/SPP

## Slide 26: Status of EPI-Lo Ray Tracing Model
A
B
C
D
E
F
G
H
I
J
Start Foils (A-J) are set to be source for reversed ray tracing
Projection of start foil onto external hemisphere

## Slide 27: Status of EPI-Lo Ray Tracing Model
Start foil FOV projection for a single segment

## Slide 28: Light and Dust Mitigation (1/2)
Dust may produce pinholes in the Start and collimator foils.
Foils are designed to reduce UV by ~3 orders of magnitude.
A cell-sized pinhole may account for as much as ~0.4% of a foil area.
Dust-induced holes should be 10-4% of foil area
For the 4 foils closest to the TPS edge, the suppression factor must be ~4 orders of magnitude. For these, pinholes are important to UV suppression.

## Slide 29: Event Logic and Data

## Slide 30: EPI-Lo Block Diagram

## Slide 31: Simplified Sensor & Event Board
particle
mode
ion
mode
Comparator
ADC
CFD
(start 2)
delay
delay
m
u
x
m
u
x
TDC 0
St1-Sp
TDC 2
St2-Stp
TDC 1
St1-St2
A1
A2
A1
A2
MCP
&
anode
board
Peak Detect
A1
A2
CFD
(stop)
FPGA
Quadrants A,B,C,D
Electronics for Quadrants A,B,C,D
event board
sensor
CFD
(start 1)
high
gain
low
gain
Ion SSD
particle SSD
anti-coinc. SSD
particle
mode
ion
mode
PH
anti-XEgy
PW
ion-XEgy
ea. quad has 2 wedges (octants)
event logic hard ware
&
flight soft-
ware
composite energy
PW
discriminators
Timing: TOF & position
energy measurement

## Slide 32: Event Logic: Event Modes
Event mode and event coincidence determine how TDC and Energy measurements are considered

## Slide 33: Data Flow - Ion Composition, Part 1

## Slide 34: Data Flow - Ion Composition, Part 2

## Slide 35: Data Flow - Ion Energy, Part 1

## Slide 36: Data Flow - Ion Energy, Part 2

## Slide 37: Data Flow - Part. Composition, Part 1

## Slide 38: Data Flow - Part. Composition, Part 2

## Slide 39: Data Flow - Particle Energy, Part 1

## Slide 40: Data Flow - Part Energy, Part 2

## Slide 41: Data: Main Products

## Slide 42: Data: Main Products

## Slide 43: Burst: Motivation/Importance
Large SEP events seen at 1AU are associated with strong interplanetary shock waves. The energetic-particle characteristics (spectrum, intensity vs. time) are generally consistent with the predictions of diffusive shock acceleration (DSA) theory
DSA theory predicts that the rise of SEPs seen upstream of a shock is related to the diffusion coefficient, .
In general,  is a function of position (most importantly distance from the Sun, r) and energy, E. That is  = (r,E)
Measuring (r,E) near the Sun is extremely important for understanding how the Sun accelerates particles to high energies. The intensity of very dangerous SEPs with energies > 10MeV, for example, strongly depends (r,E). See the next slide.
Solar Probe Plus ISIS/Epi-Lo can be used to measure (r,E) close to the Sun for large SEP events. It will require sufficient time cadence and energy resolution to make a meaningful determination of (r,E). The purpose of this report is to estimate the requirements.

## Slide 44: An even closer view. The total time period is about 1.5 hours. The rise time for the energies shown occurs over about 4 data points and each point is separated by 5 minutes.
55 keV
85 keV
145 keV
240 keV

## Slide 45
The exponential rise time expected for large SEP events observed at 10 solar radii as a function of energy. This is the same figure as that shown on slide 10, but with the rise time taken to be a factor of 1200 lower.

## Slide 46: Energy coverage
It is important to resolve the exponential rise just prior to the passage of strong IP shocks for large SEP events over several energy bands. This will provide information on the energy dependence of the diffusion coefficient.
Because the diffusion coefficient is much smaller closer to the Sun, the rate at which particles are accelerated by the shock is much faster than it is at 1AU. The acceleration rate (according to DSA theory) is inversely dependent on the diffusion coefficient.
Thus, the energy at which the energy spectrum will roll over (sometimes called the spectral “break” energy) will be much higher closer to the Sun than it is at 1AU. For typical large SEP events at 1AU, the break energy is of the order of an MeV or so. It will likely be closer to a GeV near the Sun for large SEP events.
Thus, we need several energy bands that cover the entire range of Epi-lo to measure the exponential rise.
Note that the rise time is shortest at low energies. I would recommend that in burst mode there be 4 energy bands between 20keV and 200 keV, and 3 more above this.

## Slide 47
Particle Count
Rate
R(t) = et/t
t = 0.1 s
t = 0.3 s
t = 1 s
t = 3 s
Assumption 1: At 1 AU the rise phase was complete w/in ~ 20 minutes. So at 10 Rs the rise phase will be completed in 1s (1200 times faster). 1 s is probably a safe minimum.
Assumption 2: The duration of the phase is (roughly) independent of energy over the 10’s keV to few MeV range
Comment: in the four examples below the different curves can be considered either different energies for the same event, or different events. They are just example profiles.
¼ second
Conclusion: If we have ion measurements every ¼ second (i.e., every other 1/8 second “slot” is in ion composition mode), then we should have enough temporal resolution to characterize the exponential rise times. This assumes we have sufficient statistics.
meh 2014-07-17

## Slide 48
Continually, once per second, a burst item is written to a circular buffer so that the oldest items are overwritten by the newest data. This allows a string of high-resolution burst-type data to be available at all times extending into the past a given amount.
When the burst trigger is activated an interval of post-trigger data is collected, then both pre and post trigger data are telemetered. The burst trigger can be internal or external to EPI-Lo.
The frequency of burst events will be limited to maintain the desired burst data volume allocation. This could be done, for example, by dividing the orbit into a number of segments each of which has one burst event (either the first triggered event, or the last buffer-full at the end of the segment).
time
Burst
Trigger
Telemeter
Burst Buffer
Pre-trigger data
post-trigger data
oldest
newest
burst data items
time
BURST BUFFER
The size of the burst buffer is estimated to be ~ 1 MiB, so can contain ~20 minutes (~1000 s) of data, assuming the 1 kiB Burst item.
The 1 kiB size of the Burst Items is notional.
ISIS/EPI-Lo Burst Data Processing (concept)
meh 2014-07-01
…
…

## Slide 49
Slot 0
1/8 s
Ancillary Data 32 bytes
(e.g., 8-slot pattern of modes)
Slot 1
1/8 s
Slot 7
1/8 s
ISIS/EPI-Lo Burst Data Item (concept) - 1 second - 1 kiB
…
Time 
There are 8 intervals (dubbed “slots”) per second. During each interval EPI-Lo is in a specified event logic mode.
We have four main modes:
Ion composition
Ion Energy
Particle composition
Particle Energy
Ion modes only measure ions, using the bottom, non Al flashed SSD, while the particle modes measure both ions and electrons using the top, Al flashed detector (formerly known as e- SSD).
The specific content of the 31 counters depends on the mode.
This provides down to 0.125 s resolution, depending on the selected mode pattern.
Burst
Data item
1 kiB, 1s
31 four-byte
counters per slot
31 four-byte
counters per slot
31 four-byte
counters per slot
…
Burst Data item 1 kiB, 1s

## Slide 50: Data: Onboard Sharing

## Slide 51: ISIS/EPI-Lo Potential Data Sharing Word
Eight Bit Word. Each bit is a flag, 0 = nominal, 1 = something exciting
0 - Hlo - low energy proton, rate flag 4 - He3 - He-3 (or other ion) rich event, composition flag
1 - Hhi - high energy proton, rate flag 5 - Hvy - heavy-ion rich event (e.g., Fe), composition flag
2 - elo - low energy electron, rate flag 6 - Han - proton anisotropy, beam flag
3 - ehi - high energy electron, rate flag 7 - ean - electron anisotropy, beam flag
[bits 0-3] Is the intensity high? Hlo, Hhi, elo, and ehi (protons and electrons, high and low energies) would all work the same way. We would specify the energy range (probably a table that specifies sets or ranges of our already defined channels: TOF vs E boxes for protons, and energy bins for e-) and specify a threshold rate value. When the total rate of all the included boxes exceeds the threshold we set the flag, otherwise we don't. It would be important to really look at the rate (or something that tracks with the rate), so we would have to account for the number of 1/8-second slots that go into the selected channels.
[bits 4-5] Is there an interesting ion composition? 3He and Hvy would work the same. We'd specify sets or ranges of channels in the numerator and denominator and a threshold ratio to define a helium or heavy (e.g., iron) -rich event.
[bits 0-5] In our parameter settings defining both types above we could have a parameter for determining directions (perhaps an eight-bit work with 1/0 = include/don't include for each octant).
[bits 6-7] Is there a particle beam? Han and ean are beam anisotropy flags. We either use the channels we've defined above for Hlo, Hhi, elo, and/or ehi or define am independent set or range or channels. Then we define numerator octants, denominator octants (8-bit set of flags), and a threshold ratio.
[bits 0-7] For any of these (particularly the last four flags) we might want to define a statistics threshold of some sort, requiring some minimum number of counts in the numerator and/or denominator.

## Slide 52: Backup
Backup

## Slide 53: Title

## Slide 54: Title

## Slide 55: Title

## Slide 56: Title

## Slide 57: Anti-coincidence System
Electron SSD is backed by an anti-coincidence SSD
Improves S/N for electrons by a factor ~25 (from ~0.4 to ~10)

## Slide 58: FPGA Block Diagram

## Slide 59: End-to-End: Particles-to-Data Products
1. Science requirements
2. Environment: foreground and background
- protons and electron
- dust
- light
3. Foreground measurement: sensor head operation
- overview
- ions
- electrons
- calibration
4. Background response: effect and mitigation
- penetrating particles
- solar wind
- photons
- internally generated secondaries
- calibration
5. Event logic: processing the measurement
- block diagram
- event modes
- supporting measurements
6. Data: data products
- main data products
- subsidiary data products
7. Summary

## Slide 60: End-to-End: Particles-to-Data Products
1. Science requirements
2. Environment: overview of foreground and background ions, electrons, photons, and dust.
- protons and electron spectra, worst case, expected variation over the mission (the stuff I’ve analyzed based mostly on Rob D’s work)
- expected dust impacts on the sensor (environment, and our Boulder test results)
- light (ticker foils towards the sun, light getting through dust holes, etc.)
3. Foreground measurement: how the instrument (sensor head) works to measure what we want to measure.
- how ions are measured (MCP/foils/2ndary e- for start/stop signal and position, SSD for energy in ion and particle detector
- how electrons are measured (primary, the SSD-only detection in the particle detector, and supplemental position sensing from starts)
- calibration to support these measurements
4. Background: how penetrators, solar wind electrons, light, and dust interferes with our measurements and what we’re doing about it.
- penetrating electrons and protons
- solar wind electrons (and protons)
- photon background rates
- internally generated secondaries
- electronics noise
- calibration/simulations to support these background estimates
5. Event Logic: how we take the measurements and break them down into specific measurements (ions vs electrons, energy ranges, composition, etc.)
- modes
- species measured during each mode
- supporting measurements: singles rates, etc.
6. Data: what products are we collecting and returning.
- main data products: species, energy, angular, temporal resolution
- subsidiary data products: event data, burst data, histogram data
7. Closure: how the data we’re getting responds to the requirements.