## Slide 1: 17 – EPI-Lo Software
John Hayes
EPI-Lo Software Engineering (JHU/APL)
Notes: introduction

## Slide 2: Overview
EPI-Lo application software
  EPI-Lo-specific software
  Common software (reused)
  SPP spacecraft interface software
EPI-Lo boot software
  Boot software (reused)
  Common software (reused)
  SPP spacecraft interface software (reused from application)

## Slide 3: Key Requirements
EPI-Lo application software
  Communicate with SPP host
  Control HV power supplies
  Configure sensor
  Integrate science data
  Operate autonomously
EPI-Lo boot software
  Communicate with SPP host
  Autonomously start application

## Slide 4: Common Software
Packet telemetry
Command handling
Macros (stored command sequences)
Memory management
Monitoring and alarm generation
Status reporting

## Slide 5: Common Software Reuse
Common software reuse estimates for EPI-Lo
  ~50% of application
  >90% of boot
Common software currently (or soon to be) in flight:
  MESSENGER: EPPS, GRS, MAG, MASCS, MDIS, NS, and XRS
  MRO: CRISM
  New Horizons: LORRI and PEPSSI
  Pucks: Juno/JEDI, RBSP/RBSPICE, MMS/EIS (2014)
  BepiColombo/Strofio (2015)
  Solar Orbiter/SIS (2017)
Automated regression test for common software (and for boot software)

## Slide 6: SPP Spacecraft Interface Software
Command and telemetry use 115200 baud UART protocol, 8 data bits plus odd parity
Virtual 1PPS, i.e. falling edge of start bit of first byte in command ITF
Redundant interface, side A vs. side B
  Command arrival determines active side; telemetry sent only to that side
  Dynamic side switching supported
Interrupt driven: per-byte interrupt for command and telemetry, and side A and B 1PPS interrupts

## Slide 7: SPP Host S/W – EPI-Lo to S/C
Telemetry ITF
  Variable length up to 8196 bytes (EPI-Lo limits to 2060 bytes)
  Multiple telemetry ITFs can be sent but cannot straddle 1PPS (EPI-Lo sends one per second)
  Frame header includes sync pattern, length, etc.; checksum at end of frame
  Frame transmission synchronized to 1PPS
CCSDS telemetry packets
  Variable length, up to 4096 bytes (including headers)
  Zero to many packets per frame
  Packets can straddle frames
  64 APIDs available
  Critical housekeeping packet

## Slide 8: SPP Host S/W – Critical Housekeeping
Critical housekeeping packet sent once per second
  May optionally be sent to the SSR
  If so, it counts against telemetry volume allocation
Contains 8 bits of TBD data to share with other instruments
Contains 8 bytes of housekeeping data
  Data is included in spacecraft-generated combined instrument critical housekeeping packet
  Data is NOT monitored by spacecraft autonomy
Contains bits to request power off or power cycle, set via EPI-Lo command:
  EPILO_SAF_OFF: Request power off
  EPILO_SAF_CYCLE: Request power cycle

## Slide 9: SPP Host S/W – S/C to EPI-Lo
Command ITF
  Variable length up to 512 bytes
  S/C sends one command ITF per second
  Frame header includes sync pattern, length, etc.; checksum at end of frame
  Frame transmission synchronized to 1PPS
CCSDS telecommand packets
  Variable length, up to 360 bytes (including headers)
  One to many packets per frame
    S/C time and status (telemetry) packet sent every second, always first
    Zero or more command packets
  Packets cannot straddle frames
  Secondary header is optional (EPI-Lo does not use)
  64 APIDs available (EPI-Lo uses one)
If command ITF is not received for a commandable number of seconds, EPI-Lo runs its safing macro

## Slide 10: SPP Host S/W – Time Keeping
Time is set by spacecraft
  32-bit MET (seconds)
  Time arrives every second (as part of time and status)
  Virtual 1PPS from S/C generates interrupt; interrupt routine sets time
Time is updated by EPI-Lo software
  1000 Hz interrupt routine updates time; continues to update on loss of virtual 1PPS
  Used in common software telemetry packet time-tags
  Science data integration synchronized to 1PPS
    Packets time-tagged at start of integration
    Time-tag accurate to less than 1 millisecond

## Slide 11: EPI-Lo Application Software
Subsystems
  MCP HV
  SSD bias
  Time-of-flight and angle/position measurement (in backup)
  Energy measurement (in backup)
  Event analysis (in backup)
Data Collection
  Integration control
  Science products
  Ancillary products
Miscellaneous
  DACs and ADCs (in backup)
  Autonomous operation

## Slide 12: EPI-Lo Application S/W – MCP HV
EPI-Lo software controls MCPs’ High Voltage (HV) common supply (bulk) and four individual HVs (opto-isolator controlled)
EPI-Lo software slowly ramps voltages to commanded levels
At least two commands are required to turn on HV
There are also commands to control current monitors implemented in hardware
Commands:
  EPILO_HV_ENB: Enable/Disable High Voltage Supply
  EPILO_HV_COM_LEVEL: Set Common High Voltage Supply Level
  EPILO_HV_COM_LIMIT: Set Common High Voltage Supply Limit
  EPILO_HV_MCP_LEVEL: Set MCP High Voltage Supply Level
  EPILO_HV_MCP_LIMIT: Set MCP High Voltage Supply Limit
  EPILO_HV_MCP_STEP: Step MCP High Voltage Supply Level
  EPILO_HV_CUR_ENB: Enable/Disable MCP HV Current Monitoring
  EPILO_HV_CUR_LIMIT: Set MCP HV Current Monitoring Limit

## Slide 13: EPI-Lo Application S/W – SSD Bias
EPI-Lo software controls SSDs’ Bias Voltage (BV) supply
EPI-Lo software slowly ramps the supply voltage to commanded level
At least two commands are required to turn on bias supply
Commands:
  EPILO_BV_ENB: Enable/Disable SSD Bias Supply
  EPILO_BV_LEVEL: Set SSD Bias Supply Level
  EPILO_BV_LIMIT: Set SSD Bias Supply Limit
  EPILO_BV_STEP: Step SSD Bias Supply Level

## Slide 14: EPI-Lo Application S/W - Integration Control
Data product integration time is commandable (T, N1, N2)
EPI-Lo data products are either fast (T), medium1 (T*N1), medium2 (T*N2), or slow (T*N1*N2)
Each data product can be individually enabled or disabled
Commands
  EPILO_DAT_ENB - Enable/Disable Data Products
  EPILO_DAT_EVT - Control Amount of Event Data
  EPILO_DAT_TIME - Control Data Integration Time

## Slide 15: EPI-Lo Application S/W - Event Modes
The EPI-Lo hardware operates in one of four event modes
  Ion composition: uses ion SSD; measures energy, TOF, and position
  Ion energy: uses ion SSD; measures energy
  Particle composition: uses “particle” SSD (i.e. ions or electrons); measures energy, TOF, and position
  Particle energy: uses particle SSD; measures energy (and some positions)
Hardware is time-multiplexed
  Each second, starting with 1PPS, is divided into 8 slots
  Each slot is assigned an event mode
Commands
  EPILO_DAT_COLLECT - Set Data Collection Pattern

## Slide 16: EPI-Lo Application S/W – Science Products
Ion composition
  High-resolution protons[80,64], slow
  High time-resolution protons[20,16], medium1
  Ions, group1[80,128], medium2
  Ions, group2[80,160], slow
  Pulse-height scan[4,3], fast
  Mass histogram[8,8,512], slow
  Ion TOF[80,64], medium2
Ion energy
  Energy histogram[8,64], slow

## Slide 17: EPI-Lo Application S/W – Science Products (cont.)
Particle composition
  Particles[80,352], slow
  Particle TOF[80,64], medium2
Particle energy
  High-resolution electrons[8,64], slow
  High time-resolution electrons[8,16], fast
  High look-resolution electrons[80,32], medium2
  High energy particles[8,48], medium2

## Slide 18: EPI-Lo Application S/W – Ancillary Products
Basic and diagnostic rates (i.e. singles) are collected
  Hardware counters, e.g. SSD LEDs, CFDs, Events queued, etc.,
    21-bit hardware counters accumulated in 32-bit software counters
    Accumulated separately per quadrant
  Software counters, e.g. Events processed
  Collected per event mode (i.e. 8 packet types):
    Ion composition: basic[27], medium1 and diagnostic[32], medium2
    Ion energy: basic[27], medium1 and diagnostic[12], medium2
    Particle composition: basic[35], medium1 and diagnostic[16], medium2
    Particle energy: basic[35], fast and diagnostic[8], medium2
Single events
  Software reads events from hardware FIFO
  A commandable number collected in raw event product
  Collected per event mode (i.e. 4 packet types)
  A subset can be sent as priority data

## Slide 19: EPI-Lo Application S/W – Autonomous Operations
Common-code macro capability support definition, execution, and save/restore of command sequences
  Macros can pause until a given MET or delay a given number of seconds
  Macros can contain do-loops, calls and “forks” to other macros
Time and status from spacecraft includes
  Startup Mode: selects manual vs. autonomous operation
  Solar Distance: current distance to the sun and in vs. outbound
If autonomous operation is selected, EPI-Lo software will:
  Automatically load macros from MRAM
  Run startup macro; this ramps up HVs, etc.
  Monitor solar distance against a set of commandable thresholds
    Different threshold crossings trigger different macros to run
    Macros configure science collection, e.g. integration times, etc.
If autonomous operation is not selected, EPI-Lo software will wait for commands

## Slide 20: EPI-Lo Boot S/W
Commands: memory load, copy, execute, dump, check, plus boot from MRAM
Telemetry: status/housekeeping, memory dump, etc.
High (>95%) code reuse:
  SPP I/F from application
  Common software (subset)
  Boot software (boot programs from MRAM)
New: wrapper, startup, etc.
  If autonomous operation is selected, EPI-Lo boot software will automatically try to boot a series of three programs from MRAM
  If autonomous operation is not selected, EPI-Lo boot software will wait for commands

## Slide 21: Software Development Environment
Flight software and development tools are on Space Department’s Unix system
  /project/spp-instr
  Backed up nightly
  Tools are C-based and have been used on Sun OS, Linux, & Mac OS X
  Only single developer can modify software
Software versions
  Numbered with integers, i.e. 1, 2, 3, etc.
  Each version is in a subdirectory; name of subdirectory includes version number
  Version number reported in telemetry
  Each delivered version includes snapshot of libraries
  Archived in Product Lifecycle Management (PLM) system
Testing
  Unit and integration testing done on Xilinx prototype board (no sensor); concocted events are in RAM
  Further testing on EM with pulsers simulating events
  Acceptance testing is done as part of Instrument Test Procedure

## Slide 22: Summary and Status
EPI-Lo application software
  EPI-Lo-specific software
    Sensor control and multiplexing done
    HV control done
    Autonomous operations done
    Science integration infrastructure in place, and ancillary data products being generated
    To do: generate main science data products
  Common software
    Reused code, ~50% of application
    Done, i.e. regression tested
  SPP spacecraft interface software
    New code, but derived from RBSP interface code
    Done but needs update based on large instantaneous data rate
EPI-Lo boot software
  >95% reused code
  Done
TBD: need resource chart; new slide?

## Slide 23: Backup

## Slide 24: Common S/W - Packet Telemetry
Provides standard API to application
  Delivers variable-length packets
  Numeric ID identifies packet type/contents
  Time tag of data collection time
API also used within common code to deliver standard products:
  Memory dump, memory checksum, etc.
  Command echo
  Alarm
  Status/housekeeping

## Slide 25: Common S/W - Commands
Standard API for “clients” to register commands:
  Numeric “opcode” and expected number of arguments
  Pointer to code that implements command
API also used within common code to register standard commands:
  EPILO_CMD_NULL: do nothing; tests uplink and downlink paths
  EPILO_STAT_CLR: reset counters
Command process executes commands
  Echoes opcode, up to ten argument bytes, and a result code
  Also executes stored command sequences, macros …

## Slide 26: Common S/W - Macros
Macros are stored sequences of commands
256 different macros can be defined
64 Kbyte of RAM is available for macro storage
Macros can nest 16 deep; up to 64 macros can execute concurrently
Real-time uplink commands take precedence over macro commands
Commands from a macro are echoed; the echo includes a flag indicating that the command is from a macro

## Slide 27: Common S/W - Macros (cont.)
Macros are “learned” by the instrument
  EPILO_MAC_DEF starts a macro definition; any command uplinked with its “macro” arg set will be appended to the macro
  EPILO_MAC_ENDDEF ends the definition
  While a macro is being compiled, any real-time command, i.e., one without a set “macro” arg will be executed.
  There is no need for macro compiler or macro memory management by ground software
Other macro commands:
  EPILO_MAC_DELAY and EPILO_MAC_PAUSE delay by a give number of seconds or until a given time, respectively
  EPILO_MAC_NEST and EPILO_MAC_RUN nest a macro and starts a concurrently executing macro, respectively
  EPILO_MAC_LOOP_BEGIN and EPILO_MAC_LOOP_END delimit a definite loop
  EPILO_MAC_HALT kills a running macro

## Slide 28: Common S/W - Memory Management
Commands:
  EPILO_MEM_LOAD: loads RAM
  EPILO_MEM_COPY: copy memory; source and/or destination can be RAM or non-volatile MRAM
  EPILO_MEM_READ: produce memory dump packets
  EPILO_MEM_READ_ABRT: stop memory dump
  EPILO_MEM_CHECK: produce a checksum packet summarizing given region
  EPILO_MEM_RUN: jump to program at given address
Note: these commands are the core of the boot software

## Slide 29: Common S/W - Monitoring and Alarms
Alarm packet is generated in response to a software problem or to a monitored value going out of limits
Alarms from monitors can be transient or persistent
  If a monitored value is out-of-limits just once, a transient alarm is reported
  If a monitored value is consecutively out-of-limits twice, a persistent alarm is reported and the software may take corrective action
  If a monitored value is consecutively out-of-limits more than twice, either corrective action is taken again, the shutdown macro is run, or nothing is done, depending on the thing being monitored
Commands:
  EPILO_MON_CNTRL enables or disables corrective action

## Slide 30: Common S/W - Monitoring Algorithm
High response (low response is similar):
high once: issue transient high alarm high twice: issue persistent high alarm if enabled (via EPILO_MON_CNTRL command) execute high response macro for this alarm high more than twice: case of monitor class current/voltage: if enabled (via EPILO_MON_CNTRL command) run shutdown macro temperature: nop count rate: if enabled (via EPILO_MON_CNTRL command) re-execute high response macro

## Slide 31: Common S/W - Status Reporting
Status packet
  Command and macro execution counters
  Analogs: voltages, currents, and temperatures
  Commanded instrument state
Commands:
  EPILO_STAT_INT: how often should status be reported

## Slide 32: EPI-Lo Application S/W – Time-Of-Flight Subsystem
Measures particle time-of-flight (TOF), look direction (i.e. position) on the sensor, and pulse height
EPI-Lo software controls discriminator thresholds
Commands:
  EPILO_TDC_CFD: Set TDC System CFD Threshold
  EPILO_TDC_PH: Set TDC System Pulse Height Threshold
  EPILO_TDC_PH_STEP: Step TDC System Pulse Height Thresholds

## Slide 33: EPI-Lo Application S/W – Energy Subsystem
Measures particle energy
EPI-Lo software time-multiplexes hardware between electron and “particle” detectors
EPI-Lo software controls thresholds, one set per detector
Commands:
  EPILO_EGY_ENERGY: Set Energy Threshold
  EPILO_EGY_EXTEND: Set Extended Energy Threshold

## Slide 34: EPI-Lo Application S/W – Event Subsystem
Analyzes data from TOF and energy subsystems to identify an “event”
EPI-Lo software configures hardware to define a valid event
Commands:
  EPILO_EVT_MULTI: Enable/Disable Multiple Hit Reject
  EPILO_EVT_TDC_CHECK: Enable/Disable TDC Consistency Check
  EPILO_EVT_TDC_MATCH: Enable/Disable TDC and SSD Match
  EPILO_EVT_TDC_ONLY: Enable/Disable TDC-Only Events
  EPILO_EVT_TDC_POS: Enable/Disable TDC Position Valid

## Slide 35: EPI-Lo Application S/W – DACs and ADCs
1 Hz activity schedule
Control QuadDACs over I2C bus
  Set power supply levels, e.g. MCP HV
  Set thresholds, e.g. MCP HV current
Read ADCs over SPI bus
  Read analogs (read three times and use median value)
  Save in housekeeping
  Monitor and report/respond to out-of-limit conditions

## Slide 36: EPI-Lo Application S/W – Test Support
EPI-Lo software provides commands to control an on-board pulser
EPI-Lo software provides commands to select internal test points to bring out on the test port
Commands:
  EPILO_TST_PUL_CFG: Configure Internal Pulser
  EPILO_TST_PUL_ENB: Enable/Disable Internal Pulser
  EPILO_TST_PUL_HGT: Set Internal Pulse Height
  EPILO_TST_POINT: Select Test Point Signal

## Slide 37: Reference Documents
7434-9066, “Solar Probe Plus (SPP) General Instrument (GI) ICD”
16105-ISIS-IRD-01, “PRELIMINARY INSTRUMENT REQUIREMENTS DOCUMENT SOLAR PROBE PLUS PROJECT ISIS INSTRUMENT”
7464-9005, “EPI-Lo Flight Software Specification”
7464-9003, “EPI-Lo Software Development Plan”

## Slide 38: Task Communications Graph

## Slide 39: Data Flow - Ion Composition, Part 1

## Slide 40: Data Flow - Ion Composition, Part 2

## Slide 41: Data Flow - Ion Energy, Part 1

## Slide 42: Data Flow - Ion Energy, Part 2

## Slide 43: Data Flow - Part. Composition, Part 1

## Slide 44: Data Flow - Part. Composition, Part 2

## Slide 45: Data Flow - Particle Energy, Part 1

## Slide 46: Data Flow - Part Energy, Part 2

## Slide 47: Software Activity Timeline