## Slide 1: 26 – ISIS Structural Analysis
Amanda Walther
ISIS Mechanical Engineering (SwRI)
Notes: introduction

## Slide 2: Suggested Outline
Introduction & overview illustrations
Driving requirements
Structural Analysis results for ISIS and its components
  FEM/Boundary Conditions
  Modal Results
  Stress Results
  Structural design margins and plans for strength verification
  Bolt analysis and torque margins
  Shock
  Circuit board analyses
Test results and model correlation
Peer review results
Remaining EM work
Major milestones
Verification plans
Summary

## Slide 3: Mechanical Packaging & Structural Design Description
Structural/Mechanical design description, including
Design description, with a complete and comprehensive definition of the entire design.
Requirements and design changes since PDR and rationale
Analyses are completed for mechanical/structural loads, stress, dynamics, fracture control, and torque margins & venting, thermal environment, including predicted performance and margins
  If applicable, finite element model demonstrating structural integrity of the housing under launch loads
  Analyses down to board level for electronics
Presentation on all analysis margins
Presentation of all required mechanical GSE design
Combined optical, thermal and mechanical budgets (specifically internal alignment plans)
Surface coating
Interface control documents (ICDs) formally released for subsystems
Final implementation plans, including engineering models, prototypes, flight units, and spares. Include any changes planned from EM to FM

## Slide 4: Mechanical Packaging & Structural Design Description (continued)
Engineering model/breadboard test results and design margins
Mechanisms qualification
Completed detailed design with bulk (~75%) of drawings signed off and ready for fabrication. (Drawings available.)
Completed (or near completion) Materials Identification List (MIL) including procured components
Brief report on fabrication plans and any items of concern for fabrication (possibly a report from an FFR, or a plan for one)
Fabrication, Assembly, Integration and Test plan/procedure at instrument level, including a detailed handling plan. Include purge requirements
Ground and in-flight calibration plans and their impact on mechanical alignments and I&T
Environmental test plans and test flow with test verification matrix
Integration and Environmental Test plans at observatory level
  Include LV operation requirements (pre fairing install, shipping, erection, and at pad)
  Purge requirements while on LV

## Slide 5: Mechanical Packaging & Structural Design Description (continued)
Mass report on margins, bottoms up mass stack-up reported
Presentation on mechanical risks (if any) to instrument delivery
Plans for shipping containers, environmental control, and transportation & logistics
Waivers sought against requirements

## Slide 6: Outline
Requirements
Finite Element Model (FEM) Overview
Analysis Results
  Modal analysis – full electronics box
  Stress analysis – electronics box
  Individual board analysis
    Modal results
    Steinberg analysis for RVL response and component fatigue life
  Bolted joint analysis – EPI-Hi mounting fasteners

## Slide 7: Requirements
Requirements taken from SPP EDTRD Rev B
Minimum first fundamental frequency: 80Hz
Random Vibration PSD Spectrum
  Applicable safety factors
    SFu = 1.4 and SFy = 1.25
    An additional factor of 1.28 is applied to account for increased Protoflight test levels
Frequency (Hz) | Qualification (G2/Hz) | Protoflight (G2/Hz) | Acceptance (G2/Hz)
20 | 0.016 | 0.016 | 0.008
50 | 0.1 | 0.1 | 0.05
600 | 0.1 | 0.1 | 0.05
2000 | 0.009 | 0.009 | 0.0045
Overall Grms | 9.93 | 9.93 | 7.0
Duration (mins) | 2 | 1 | 1
Axis Normal to the Spacecraft Deck or Panel
(Y-Axis)
Frequency (Hz) | Qualification (G2/Hz) | Protoflight (G2/Hz) | Acceptance (G2/Hz)
20 | 0.008 | 0.008 | 0.0053
50 | 0.05 | 0.05 | 0.04
600 | 0.05 | 0.05 | 0.04
2000 | 0.0045 | 0.0045 | 0.0036
Overall Grms | 7.0 | 7.0 | 6.28
Duration (mins) | 2 | 1 | 1
2 Orthogonal Axes, In-Plane of the Spacecraft Deck or Panel
(X- and Z-Axes)

## Slide 8: EPI-Hi Finite Element Model
Built in ANSYS Workbench 15.0
Used CBE (plus uncertainty mass of 4.205 kg
  Bracket geometry included
  EPI-Lo modeled as point mass
Elements:
Nodes:
Boundary conditions
  Bracket fixed at s/c mounting holes
FIGURE WILL BE UPDATED
AS ANALYSIS PROGRESSES

## Slide 9: EPI-Hi Modal Analysis
EPI-Hi Modal results go here

## Slide 10: EPI-Hi Random Vibration Analysis
PSD G acceleration applied uniaxially, all 3 major axes
  Load applied at bracket spacecraft mounting holes
Evaluated Acceptance levels, no notching applied
Constant damping ratio of 2%

## Slide 11: EPI-Hi RVL Stress Results, X-Axis
3σ maximum stress
  Location
Margin of safety

## Slide 12: EPI-Hi RVL Displacement Results, X-Axis
Maximum displacement
  location

## Slide 13: EPI-Hi RVL Stress Results, Y-Axis
3σ maximum stress
  Location
Margin of safety

## Slide 14: EPI-Hi RVL Displacement Results, Y-Axis
Maximum displacement
  Location

## Slide 15: EPI-Hi RVL Stress Results, Z-Axis
3σ maximum stress
  Location
Margin of safety

## Slide 16: EPI-Hi RVL Displacement Results, Z-Axis
Maximum displacement
  Location

## Slide 17: LVPS Modal Analysis
First mode: 373 Hz

## Slide 18: LVPS Steinberg Analysis
In progress
LVPS |  |  |  |  |  |  |  |  | 
Reference | C162 | C163 | T3 | T5/T6 | U1 | C182 | U3 | U5 | U6
Part Number |  |  |  |  |  |  |  |  | 
PSD | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05
C | 1.26 | 1.26 |  |  | 1.26 | 2.25 | 1.26 | 1.26 | 1.26
h | 0.059 | 0.059 | 0.059 | 0.059 | 0.059 | 0.059 | 0.059 | 0.059 | 0.059
r | 0.707 | 0.707 |  |  | 0.707 | 0.707 | 0.5 | 0.5 | 0.707
L | 0.425 | 0.425 |  |  | 0.614 | 0.329 | 0.614 | 0.28 | 0.28
B (Effective) | 1.378 | 1.339 |  |  | 1.378 | 1.063 | 1.221 | 1.85 | 1.161
Freq (Desired) | 237 | 243 | #DIV/0! | #DIV/0! | 275 | 419 | 230 | 120 | 230
Freq (Ansys) | 373 | 373 | 373 | 373 | 373 | 373 | 373 | 373 | 373
Margin | 136 | 130 | #DIV/0! | #DIV/0! | 98 | -46 | 143 | 253 | 143
Zdesired |  |  | #DIV/0! | #DIV/0! |  | 0.0043 |  |  | 
Zactual |  |  | 0.0050 | 0.0050 |  | 0.0050 |  |  | 
Fatigue Life (min) |  |  | #DIV/0! | #DIV/0! |  | 351 |  |  | 

## Slide 19: DPU Modal Analysis
First mode: 405 Hz

## Slide 20: DPU Steinberg Analysis
In progress
DPU |  |  |  |  | 
Reference | 1 | 2 (U2?) | 3 | 4 | 5
Part Number |  | AX250-PQ208 |  |  | 
PSD | 0.05 | 0.05 | 0.05 | 0.05 | 0.05
C | 1 | 1 | 1 | 1 | 1
h | 0.059 | 0.059 | 0.059 | 0.059 | 0.059
r | 1 | 1 | 1 | 1.26 | 1.26
L | 1.181 | 1.102 | 0.984 | 0.984 | 0.881
B (Effective) | 1.772 | 1.772 | 1.22 | 1.772 | 1.772
Freq (Desired) | 320 | 312 | 401 | 358 | 343
Freq (Ansys) | 405 | 405 | 405 | 405 | 405
Margin | 85 | 93 | 4 | 47 | 62
Zdesired |  |  |  |  | 
Zactual |  |  |  |  | 
Fatigue Life (min) |  |  |  |  | 

## Slide 21: Bias Modal Analysis
First mode: 414 Hz

## Slide 22: Bias Steinberg Analysis
In progress
BIAS |  |  |  |  |  |  |  | 
Reference | C90 | C3 | U10 | C108 | U12 | Q11 | Q2 | L8
Part Number | SRSI214X7R156M1J5 | SRSI214X7R156M1J5 | CD4069UBKMSR | SR1725X7R165K2NT95 | ISL70218 SRHMF | IRHNJ67234 | IRHNJ67234 | MIL4922-29L
PSD | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05
C |  |  | 1 |  | 1.26 | 2.25 | 2.25 | 2.25
h | 0.059 | 0.059 | 0.059 | 0.059 | 0.059 | 0.059 | 0.059 | 0.059
r | 1 | 1 | 1 | 1 | 1 | 0.707 | 0.707 | 1
L |  |  |  |  | 0.29 | 0.405 | 0.405 | 0.52
B (Effective) | 1.693 | 1.693 | 1.693 |  | 2.539 | 1.693 | 1.693 | 1.693
Freq (Desired) | 0 | 0 | 0 | #DIV/0! | 165 | 314 | 314 | 458
Freq (Ansys) | 414 | 414 | 414 | 414 | 414 | 414 | 414 | 414
Margin | 414 | 414 | 414 | #DIV/0! | 249 | 100 | 100 | -44
Zdesired |  |  |  |  |  |  |  | 0.0039
Zactual |  |  |  |  |  |  |  | 0.0044
Fatigue Life (min) |  |  |  |  |  |  |  | 360

## Slide 23: HET Modal Analysis
First mode: 468 Hz

## Slide 24: HET Steinberg Analysis
In progress
HET |  |  |  |  |  |  | 
Reference | 1 | 2 | 3 | 4 | 5 | 6 | 7
Part Number |  |  |  |  |  |  | 
PSD | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05
C | 0.707 | 1 | 0.707 | 0.707 | 1 | 1 | 0.707
h | 0.059 | 0.059 | 0.059 | 0.059 | 0.059 | 0.059 | 0.059
r | 1 | 1.26 | 1 | 1.26 | 1.26 | 1.26 | 1.26
L | 0.906 | 0.945 | 1.378 | 1.063 | 1.417 | 1.26 | 1.26
B (Effective) | 1.653 | 1.811 | 1.693 | 1.693 | 1.811 | 1.772 | 1.76
Freq (Desired) | 231 | 346 | 268 | 290 | 407 | 395 | 301
Freq (Ansys) | 468 | 468 | 468 | 468 | 468 | 468 | 468
Margin | 237 | 122 | 200 | 178 | 61 | 73 | 167

## Slide 25: LET1 Modal Analysis
First mode: 506 Hz

## Slide 26: LET1 Steinberg Analysis
In progress
LET1 |  |  |  |  |  |  | 
Reference | 1 | 2 | 3 | 4 | 5 | 6 | 7
Part Number |  |  |  |  |  |  | 
PSD | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05
C | 0.707 | 1 | 0.707 | 0.707 | 1 | 1 | 0.707
h | 0.059 | 0.059 | 0.059 | 0.059 | 0.059 | 0.059 | 0.059
r | 1 | 1.26 | 1 | 1.26 | 1.26 | 1.26 | 1.26
L | 0.906 | 0.945 | 1.378 | 1.063 | 1.417 | 1.26 | 1.26
B (Effective) | 1.653 | 1.811 | 1.693 | 1.693 | 1.811 | 1.772 | 1.76
Freq (Desired) | 231 | 346 | 268 | 290 | 407 | 395 | 301
Freq (Ansys) | 506 | 506 | 506 | 506 | 506 | 506 | 506
Margin | 275 | 160 | 238 | 216 | 99 | 111 | 205

## Slide 27: LET2 Modal Analysis
First mode: 494 Hz

## Slide 28: LET2 Steinberg Analysis
In progress
LET2 |  |  |  |  |  |  | 
Reference | 1 | 2 | 3 | 4 | 5 | 6 | 7
Part Number |  |  |  |  |  |  | 
PSD | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05
C | 0.707 | 1 | 0.707 | 0.707 | 1 | 1 | 0.707
h | 0.059 | 0.059 | 0.059 | 0.059 | 0.059 | 0.059 | 0.059
r | 1 | 1.26 | 1 | 1.26 | 1.26 | 1.26 | 1.26
L | 0.906 | 0.945 | 1.378 | 1.063 | 1.417 | 1.26 | 1.26
B (Effective) | 1.653 | 1.811 | 1.693 | 1.693 | 1.811 | 1.772 | 1.76
Freq (Desired) | 231 | 346 | 268 | 290 | 407 | 395 | 301
Freq (Ansys) | 494 | 494 | 494 | 494 | 494 | 494 | 494
Margin | 263 | 148 | 226 | 204 | 87 | 99 | 193

## Slide 29: Bolted Joint Analysis
Results of bolted joint analysis of 5 EPI-Hi mounting fasteners goes here

## Slide 30: Conclusion
Summary of analysis

## Slide 31: Steinberg Solder Joint Fatigue Analysis
Calculated desired frequency to survive 20 million stress reversal cycles using the following equation
Compared desired frequency to modal results
Calculated fatigue life of components with a negative margin (desired frequency greater than calculated frequency) using the following equation
Cumulative random vibration exposure time is estimated to be less than 20 minutes