## Slide 1: 27 – ISIS Thermal
Gregory J Dirks
ISIS Thermal Lead (SwRI)
Notes: introduction

## Slide 2: Outline
Driving Instrument Thermal Requirements
Thermal Design and Implementation
  Thermal Management
  Heaters and Sensors
  MLI Design
  Materials and Finishes
System Thermal Analysis
  Thermal Model Details
  Design Cases
  Optical Properties and Power Dissipation
  Predictions and Margins
  Resources and Requirements
EPI-Hi Circuit Board Analysis
  Component Junction Temperature Calculations
Plans for Thermal Verification

## Slide 3: Driving Requirements
Component | Hot Op. (°C) | Cold Op. (°C) | Cold Surv. (°C)
EPI-HI HET | 40 | -25 | -40
EPI-Hi LET1 | 40 | -25 | -40
EPI-Hi LET2 | 40 | -25 | -40
EPI-Hi DPU | 40 | -25 | -40
EPI-Hi Bias | 40 | -25 | -40
EPI-Hi LVPS | 40 | -25 | -40
EPI-Hi HET Tel | 30 | -25 | -40
EPI-Hi LET 1 Tel | 30 | -25 | -40
EPI-Hi LET 2 Tel | 30 | -25 | -40
Component | Hot Op. (°C) | Cold Op. (°C) | Cold Surv. (°C)
Detector | 25 | -30 | -45
Anode Board | 55 | -30 | -45
Event Board | 55 | -30 | -45
Power Board | 55 | -30 | -45
Dome | 35 | -30 | -45
Design Temperature Limits
Margin Guidelines – Includes Test and Model Uncertainty
  Hot Limits 10 C and Cold Limits 5 C (Heater Controlled)
EPI-Hi
EPI-Lo

## Slide 4: Driving Requirements
Interface Temperatures
  Operational: 0 / +45 C
  Non-Operational: 0 / +45 C
Heaters
  75% Maximum Duty Cycle
  Resistance Determined at 26 V
Environment
  1.0 AU Sun at 110 Degrees from +Z Axis for 40 Minutes
Boundary Heat Flow
  Flow from Spacecraft is No More Than 2.9 W in the Cold Case and No Less Than 0 W in the Hot Case

## Slide 5: Thermal Design
EPI-Hi
  E-box Radiator to Dissipate Internally Generated Heat
  Telescopes Conductively Isolated from E-box
  Operational Heaters on Telescopes
  Survival Heaters on Telescopes and E-box
  MLI on Surfaces Except Apertures, Radiator, and Bracket Interior Surfaces

## Slide 6: Thermal Design
EPI-Lo
  Wedge Radiators (8) to Dissipate Internally Generated Heat
  Eight Survival Heaters (One on Each Wedge)
  MLI on Surfaces Except Apertures and Radiators

## Slide 7: Thermal Design
ISIS
  EPI-Hi and EPI-Lo are Thermally Isolated from the Bracket
  Bracket is Thermally Isolated from the S/C

## Slide 8: Heaters and Sensors
EPI-Hi Heater Operations
  One S/C Thermistor on Each Telescope and Two S/C Thermistors on E-box (Primary and Redundant)
  Operational Heaters on Telescopes are All on One S/C Service, but Controlled by E-box
  Survival Heaters on Telescopes and the E-Box are All on One S/C Service and Controlled by S/C with Sense Location Currently Baselined as the E-box
  Survival Heaters Also Used to Warm Instrument to Cold Operational Temperature for Cold Turn On by using Different Set Points

## Slide 9: Heaters and Sensors
EPI-Lo Heater Operations
  Two (Primary and Redundant) S/C Thermistors on Dome for Heater Control and One More (To Be Positioned)
  All Survival Heaters are on One S/C Service (Separate from EPI-Hi) Controlled by S/C with Sense Location Currently Baselined as One of the Wedges
  Survival Heaters are Used to Warm Instrument to Cold Operational Temperature for Cold Turn On by Using Different Set Points
  Survival Heaters are Also Used to Maintain Minimum Cold Operating Temperature During Low Power Operating Conditions

## Slide 10: MLI
Coverage
  Entire Instrument Other than Apertures, Radiators
Specifications/Construction
  Each Separate Blanket Grounded with Wire to S/C
  Vented Using Edge Mesh Screens Directed away from Apertures
  Edges and Seams Sealed using GBK Tape
  Blankets Secured using G-10 Buttons and SS Snap Rings

## Slide 11: Materials and Finishes
Radiators
  Z-307 Conductive Black Paint
MLI
  Outer Layer: StaMet
Thermal Isolators
  G-10 Fiberglass
Bracket
  All Surfaces are Alodine
EPI-Hi Ebox
  All Surfaces are Alodine
EPI-Lo Electronics
  All Surfaces are Alodine

## Slide 12: Materials and Finishes
LET Apertures (3X):
  Polyimide a=0.21, e=0.20
  Aluminized a=.0.09, e=.0.02
  Polyimide Side Facing Out
  47 mm Diameter by 2 Microns Thick
  Gold Ring a=0.23, e=0.03
HET Apertures (2X)
  Black Kapton a=0.93, e=0.85
  Aluminized a=0.09, e=0.02
  Black Kapton Side Facing Out
  30 mm Diameter by 5 mils (0.005 inches) Thick
  Gold Ring a=0.23, e=0.03
EPI-Lo
  Collimators are Z93C55 White Paint and Ag-MgF2

## Slide 13: Thermal Model
EPI-Hi Modeled by Vertex Aerospace
  Rommel Zara and Santino Rosanova
EPI-Lo Modeled by APL
  Shawn Begley
Bracket Modeled by Vertex Aerospace
ISIS Model Integrated by Vertex Aerospace
All Models Created using Thermal Desktop Software
Updated Model Delivered to S/C TBD
Good Correlation between Instrument and S/C Results

## Slide 14: Design Cases
Hot Operational
  +45 C I/F Temperature
  EOL Power and BOL Optical Properties
  Low MLI e* = 0.03
Cold Operational
  0 C I/F Temperature
  BOL Power and BOL Optical Properties
  High MLI e* = 0.05
Cold Non-Operational
  0 C I/F Temperature
  BOL Optical Properties and e* = 0.05
Hot Non-Operational
  1.02 AU / 110 Degrees / 40 Minutes with +45 C I/F Temperature
  BOL Optical Properties and e* = 0.03

## Slide 15: Optical Properties
Radiator: Z-307 Black Paint
  BOL: a = 0.95, e = 0.89
MLI Exterior: StaMet
  BOL: a = 0.56, e = 0.83
EPI-Hi Apertures
  HET BOL: a = 0.93, e = 0.85
  LET BOL: a = 0.21, e = 0.20
EPI-Lo Collimators
  Z93C55 BOL: a = 0.15, e = 0.91
  Ag-MgF2 Range: a = 0.01/0.02, e = 0.07/0.09
Alodine Surfaces
  BOL: a = 0.45, e = 0.12

## Slide 16: Power Dissipation
ISIS Power Distribution
  Cold Case uses CBE, Hot Case uses CBE+Cont.

## Slide 17: Predictions
Hot Operational
Component | Hot Op Predict, °C | Hot Op Limit, °C | Margin, °C
IS_ISIS_EPI_LO_DETECTOR | 15.0 | 25.0 | 10.0
IS_ISIS_EPI_LO_EVENT | 21.3 | 55.0 | 33.7
IS_ISIS_EPI_LO_PWR_SUPPLY | 23.5 | 55.0 | 31.5
IS_ISIS_EPI_LO_MCP | 18.4 | 55.0 | 36.6
IS_ISIS_EPI_LO_ANODE | 17.3 | 55.0 | 37.7
IS_ISIS_EPI_LO_DOME | 13.1 | 55.0 | 41.9
IS_ISIS_BRACKET | 25.7 | NA | NA
Component | Hot Op Predict, °C | Hot Op Limit, °C | Margin, °C
IS_ISIS_TEL_HET | 1.8 | 30.0 | 28.2
IS_ISIS_TEL_LET1 | 7.7 | 30.0 | 22.3
IS_ISIS_TEL_LET2 | -0.8 | 30.0 | 30.8
IS_ISIS_EPI_HI_BIAS | 28.4 | 40.0 | 11.6
IS_ISIS_EPI_HI_DPU | 28.6 | 40.0 | 11.4
IS_ISIS_EPI_HI_HET | 28.4 | 40.0 | 11.6
IS_ISIS_EPI_HI_LET1 | 28.4 | 40.0 | 11.6
IS_ISIS_EPI_HI_LET2 | 27.2 | 40.0 | 12.8
IS_ISIS_EPI_HI_LVPS | 29.8 | 40.0 | 10.2
IS_ISIS_BRACKET | 25.7 | NA | NA

## Slide 18: Predictions
Cold Operational
Component | Cold Op Predict, °C | Cold Op Limit, °C | Margin, °C
IS_ISIS_EPI_LO_DETECTOR | -14.6 | -30.0 | -15.4
IS_ISIS_EPI_LO_EVENT | -10.4 | -30.0 | -19.6
IS_ISIS_EPI_LO_PWR_SUPPLY | -9.5 | -30.0 | -20.5
IS_ISIS_EPI_LO_MCP | -10.4 | -30.0 | -19.6
IS_ISIS_EPI_LO_ANODE | -12.9 | -30.0 | -17.1
IS_ISIS_EPI_LO_DOME | -15.7 | -30.0 | -14.3
IS_ISIS_BRACKET | -9.8 | NA | NA
Component | Cold Op Predict, °C | Cold Op Limit, °C | Margin, °C
IS_ISIS_TEL_HET | -20.0 | -25.0 | -5.0
IS_ISIS_TEL_LET1 | -13.7 | -25.0 | -11.3
IS_ISIS_TEL_LET2 | -19.9 | -25.0 | -5.1
IS_ISIS_EPI_HI_BIAS | 3.4 | -25.0 | -28.4
IS_ISIS_EPI_HI_DPU | 3.7 | -25.0 | -28.7
IS_ISIS_EPI_HI_HET | 3.5 | -25.0 | -28.5
IS_ISIS_EPI_HI_LET1 | 3.5 | -25.0 | -28.5
IS_ISIS_EPI_HI_LET2 | 2.6 | -25.0 | -27.6
IS_ISIS_EPI_HI_LVPS | 4.6 | -25.0 | -29.6
IS_ISIS_BRACKET | -9.8 | NA | NA

## Slide 19: Predictions
Hot Non-Operational
Component | Hot Surv Predict, °C | Hot Surv Limit, °C | Margin, °C
IS_ISIS_EPI_LO_DETECTOR | 34.7 | 55 | 20.3
IS_ISIS_EPI_LO_EVENT | 34.1 | 55 | 20.9
IS_ISIS_EPI_LO_PWR_SUPPLY | 34.1 | 55 | 20.9
IS_ISIS_EPI_LO_MCP | 34.4 | 55 | 20.6
IS_ISIS_EPI_LO_ANODE | 34.2 | 55 | 20.8
IS_ISIS_EPI_LO_DOME | 34.9 | 55 | 20.1
IS_ISIS_BRACKET | 37.4 | NA | NA
Component | Hot Surv Predict, °C | Hot Surv Limit, °C | Margin, °C
IS_ISIS_TEL_HET | 19.6 | 60 | 40.4
IS_ISIS_TEL_LET1 | 41.6 | 60 | 18.4
IS_ISIS_TEL_LET2 | 47.3 | 60 | 12.7
IS_ISIS_EPI_HI_BIAS | 36.4 | 55 | 18.6
IS_ISIS_EPI_HI_DPU | 36.4 | 55 | 18.6
IS_ISIS_EPI_HI_HET | 36.5 | 55 | 18.5
IS_ISIS_EPI_HI_LET1 | 36.5 | 55 | 18.5
IS_ISIS_EPI_HI_LET2 | 36.5 | 55 | 18.5
IS_ISIS_EPI_HI_LVPS | 36.4 | 55 | 18.6
IS_ISIS_BRACKET | 37.4 | NA | NA

## Slide 20: Predictions
Cold Non-Operational

## Slide 21: Resources
Survival Heater Power
Operational Heater Power
COLD SURVIVAL | EPI Lo | EBOX | HET | LET1 | LET2
On Time | 25034 | 23764 | 23764 | 23764 | 23764
Orbit Time | 57600 | 57600 | 57600 | 57600 | 57600
Total Energy | 125170 | 150901.4 | 16040.69 | 9980.88 | 17347.71
Duty Cycle | 43.46% | 41.26% | 41.26% | 41.26% | 41.26%
Power | 2.2 | 2.62 | 0.28 | 0.17 | 0.30
Total | 2.2 | 3.4 |  |  | 
Component | Heater Power, W | 
EPI LO | 0 | 
EPI HI Ebox | 0 | 0.07
EPI HI HET 1 | 0 | 
EPI HI LET 1 | 0 | 
EPI HI LET 2 | 0.07 | 

## Slide 22: Requirements
Heat Flow Across S/C to Bracket Interface
  Hot Operational: 1.55 W
  Cold Operational: 0.69 W
  Hot Non-Op.: 0.61
In All Cases Heat Flow is From the S/C into the Bracket

## Slide 23: Board Analysis
EPI-Hi Boards Analyzed
  HET Shown is Representative of all Telescope Boards
Components and Power
  All >50 mW were Explicitly Modeled
  Remaining Power is Evenly Distributed on the Board
Boundary Condition
  Test Limit of +50 C at Each Attachment Point
Junction Temperatures
  Derating per EEE-INST-002
Complete Results are Shown in Thermal Analysis Document 16105-TA-01

## Slide 24: Board Analysis
LVPS Board Temperature Contour Plot

## Slide 25: Board Analysis
CDH Board Temperature Contour Plot

## Slide 26: Board Analysis
Bias Board Temperature Contour Plot

## Slide 27: Board Analysis
HET Board Temperature Contour Plot

## Slide 28: Board Analysis
LVPS Component Junction Temperatures
DPU Component Junction Temperatures

## Slide 29: Board Analysis
Bias Component Junction Temperatures
HET Component Junction Temperatures

## Slide 30: Verification
ISIS Thermal Balance
  Three Cases: Hot Operational, Cold Operational, and Cold Survival
  Temperature Controlled Baseplate to S/C I/F Temperature Limits
  Radiators with View to LN2 Cooled Chamber Shroud
  Verify Heater Duty Cycle
  Verify Interface Heat Flow
  Correlate Thermal Model