## Slide 1: Solar Probe Plus Payload Requirements Document Peer Review

## Slide 2: WISPR Measurements
PAY-70: Measurement: Visible Broadband Intensity 0.046 AU to 0.07 AU | 
WISPR shall be capable of providing Full Frame Images of visible broadband intensity over solar orbital distances of 0.046 AU to 0.07 AU as follows: -- capturing the radial scene from elongations of 14 degrees to 90 degrees from sun center; -- capturing the transverse scene from 20 degrees (at 14 degrees elongation) to 44 degrees (at 90 degrees elongation); -- with image spatial resolution across the FOV of ≤ 6.4 arcmin (for elongations 14 degrees to 53 degrees) and ≤ 9.3 arcmin (for elongations 53 degrees to 90 degrees); -- with SNR for a binned pixel ≥ 20 (for elongations of 14 degrees to 20 degrees), ≥ 10 (for elongations of 20 degrees to 26 degrees) and ≥ 5 (for elongations of 26 degrees to 90 degrees); -- with nominal cadence of ≤ 10 min. | 
Description/Clarification | 
L2 Spatial resolution and photometric accuracy at the required spatial resolution and cadence are only required to be satisfied in the inner FOV of the image. L2 Cadence is an average cadence requirement over the orbit. The cadence requirement will be faster inside 0.11 AU. Since instrument cadence for the same effective aperture will vary as a function of the signal to noise ratio in the scene based on the spacecraft distance to the sun and elongation, the increase in the instrument cadence inside 0.11 AU is not driving the WISPR instrument design. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. | WISPR
Parent Traceability | Functional Allocation
MRD-95 : The Mission shall measure visible broadband intensity, as follows: -- Cadence: <= 16.5 min -- Field of view: >= 76 degrees radial x >= 20 degrees transverse at 14 degrees elongation to >= 44 degrees transverse at 90 degrees elongation -- Inner FOV boundary: <= 14 degrees -- Spatial Resolution: <= 6.4 arcmin -- Photometric sensitivity (SNR per pixel): >= 20. | 

## Slide 3: WISPR Measurements
PAY-71: Measurement: Visible Broadband Intensity 0.07 AU to 0.11 AU | 
WISPR shall be capable of providing Full Frame Images of visible broadband intensity over solar orbital distances of 0.07 AU to 0.11 AU as follows: -- capturing the radial scene from elongations of 14 degrees to 90 degrees from sun center; -- capturing the transverse scene from 20 degrees (at 14 degrees elongation) to 44 degrees (at 90 degrees elongation); -- with image spatial resolution across the FOV of ≤ 6.4 arcmin (for elongations 14 degrees to 53 degrees) and ≤ 9.3 arcmin (for elongations 53 degrees to 90 degrees); -- with SNR for a binned pixel ≥ 20 (for elongations of 14 degrees to 20 degrees), ≥ 10 (for elongations of 20 degrees to 26 degrees) and ≥ 5 (for elongations of 26 degrees to 90 degrees); -- with nominal cadence of ≤ 15 min. | 
Description/Clarification | 
L2 Spatial resolution and photometric accuracy at the required spatial resolution and cadence are only required to be satisfied in the inner FOV of the image. L2 Cadence is an average cadence requirement over the orbit. The cadence requirement will be faster inside 0.11 AU and slower outside 0.174 AU. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. | WISPR
Parent Traceability | Functional Allocation
MRD-95 : The Mission shall measure visible broadband intensity, as follows: -- Cadence: <= 16.5 min -- Field of view: >= 76 degrees radial x >= 20 degrees transverse at 14 degrees elongation to >= 44 degrees transverse at 90 degrees elongation -- Inner FOV boundary: <= 14 degrees -- Spatial Resolution: <= 6.4 arcmin -- Photometric sensitivity (SNR per pixel): >= 20. | 

## Slide 4: WISPR Measurements
PAY-72: Measurement: Visible Broadband Intensity 0.11 AU to 0.174 AU | 
WISPR shall be capable of providing Full Frame Images of visible broadband intensity over solar orbital distances of 0.11 AU to 0.174 AU as follows: -- capturing the radial scene from elongations of 14 degrees to 90 degrees from sun center; -- capturing the transverse scene from 20 degrees (at 14 degrees elongation) to 44 degrees (at 90 degrees elongation); -- with image spatial resolution across the FOV of ≤ 6.4 arcmin (for elongations 14 degrees to 53 degrees) and ≤ 9.3 arcmin (for elongations 53 degrees to 90 degrees); -- with SNR for a binned pixel ≥ 20 (for elongations of 14 degrees to 20 degrees), ≥ 10 (for elongations of 20 degrees to 26 degrees), ≥ 5 (for elongations of 26 degrees to 40 degrees), ≥ 3.33 (for elongations of 40 degrees to 53 degrees), and ≥ 5 (for elongations of 53 degrees to 90 degrees); -- with nominal cadence of ≤ 16.5 min (for elongations 14 degrees to 26 degrees) and ≤ 36 min (for elongations 26 degrees to 90 degrees). | 
Description/Clarification | 
L2 Spatial resolution and photometric accuracy at the required spatial resolution and cadence are only required to be satisfied in the inner FOV of the image. L2 Cadence is only required to be satisfied in the inner FOV of the image. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. | WISPR
Parent Traceability | Functional Allocation
MRD-95 : The Mission shall measure visible broadband intensity, as follows: -- Cadence: <= 16.5 min -- Field of view: >= 76 degrees radial x >= 20 degrees transverse at 14 degrees elongation to >= 44 degrees transverse at 90 degrees elongation -- Inner FOV boundary: <= 14 degrees -- Spatial Resolution: <= 6.4 arcmin -- Photometric sensitivity (SNR per pixel): >= 20. | 

## Slide 5: WISPR Measurements
PAY-73: Measurement: Visible Broadband Intensity 0.174 AU to 0.25 AU | 
WISPR shall be capable of providing Full Frame Images of visible broadband intensity over solar orbital distances of 0.174 AU to 0.25 AU as follows: -- capturing the radial scene from elongations of 14 degrees to 90 degrees from sun center; -- capturing the transverse scene from 20 degrees (at 14 degrees elongation) to 44 degrees (at 90 degrees elongation); -- with image spatial resolution across the FOV of ≤ 6.4 arcmin (for elongations 14 degrees to 33.5 degrees), ≤ 10.25 arcmin (for elongations 33.5 degrees to 53 degrees), ≤ 9.3 arcmin (for elongations 53 degrees to 78 degrees), and ≤ 14.2 arcmin (for elongations 78 degrees to 90 degrees); -- with SNR for a binned pixel ≥ 10 (for elongations of 14 degrees to 20 degrees), ≥ 5 (for elongations of 20 degrees to 40 degrees), ≥ 3.33 (for elongations of 40 degrees to 53 degrees), and ≥ 5 (for elongations of 53 degrees to 90 degrees); -- with nominal cadence of ≤ 24 min (for elongations 14 degrees to 26 degrees) and ≤ 45 min (for elongations 26 degrees to 90 degrees). | 
Description/Clarification | 
L2 Spatial resolution and photometric accuracy at the required spatial resolution and cadence are only required to be satisfied in the inner FOV of the image. L2 Cadence is an average cadence requirement over the orbit. The cadence requirement will be slower outside 0.174 AU across the entire FOV. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. | WISPR
Parent Traceability | Functional Allocation
MRD-95 : The Mission shall measure visible broadband intensity, as follows: -- Cadence: <= 16.5 min -- Field of view: >= 76 degrees radial x >= 20 degrees transverse at 14 degrees elongation to >= 44 degrees transverse at 90 degrees elongation -- Inner FOV boundary: <= 14 degrees -- Spatial Resolution: <= 6.4 arcmin -- Photometric sensitivity (SNR per pixel): >= 20. | 

## Slide 6: WISPR Measurements
PAY-74: Measurement: Visible Broadband Inner Field of View Subframe | 
WISPR shall be capable of providing Inner Field of View (FOV) Subframe images over solar orbital distances of 0.046 AU to 0.07 AU as follows: -- capturing the radial scene from elongations of 14 degrees to 20 degrees from sun center; -- capturing the transverse scene over 12 degrees; -- with image spatial resolution across the Inner FOV of ≤ 3.4 arcmin; -- with SNR for a binned pixel ≥ 10; -- with nominal cadence of ≤ 6 sec. | 
Description/Clarification | 
Inner FOV Subframe images do not drive the WISPR Instrument design, based on the fact that the photometric accuracy at higher cadence and smaller spatial resolution in the inner FOV where there is a high SNR is equivalent to the photometric accuracy for the low cadence and spatial resolution in PAY-70 above. | 
Rationale | Requirement Allocation
Wave Turbulance images at the inner FOV at a reduced photometric accuracy with higher spatial resolution and cadence directly address the SPP science questions, but was not included in the L2 science measurement requirements. | WISPR
Parent Traceability | Functional Allocation
MRD-95 : The Mission shall measure visible broadband intensity, as follows: -- Cadence: <= 16.5 min -- Field of view: >= 76 degrees radial x >= 20 degrees transverse at 14 degrees elongation to >= 44 degrees transverse at 90 degrees elongation -- Inner FOV boundary: <= 14 degrees -- Spatial Resolution: <= 6.4 arcmin -- Photometric sensitivity (SNR per pixel): >= 20. | 

## Slide 7: ISIS Measurements
PAY-76: Measurement: Energetic Electrons Energy Range (EPI-Lo) | 
EPI-Lo shall be capable of measuring energetic electrons over solar orbital distances of 9.86 Rs to 0.25 AU with an energy range of ≤ 0.05 MeV to 0.5 MeV (TBR). | 
Description/Clarification | 
It is presently thought that there will be no gap between the EPI-Lo and EPI-Hi energy coverages for electrons, but a factor of 2 energy gap is allowed to take into account the possibility that the energy ranges actually achieved may differ slightly from those presently planned. If there were a gap it would be located near an energy of 0.5 MeV. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. The electron energy range should extend from the suprathermal tail of the solar wind up to highly relativistic energies to allow studies of electron acceleration, to trace connectivity of the magnetic field back to structures on the Sun, and to determine release times of energetic particles from the Sun. | ISIS
Parent Traceability | Functional Allocation
MRD-96 : The Mission shall measure energetic electrons, as follows: -- Energy range1: <= 0.05 to >= 3 MeV -- Highest cadence2: <=1s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 45 degree sectors -- Composition4: n/a Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 8: ISIS Measurements
PAY-200: Measurement: Energetic Electrons Energy Range (EPI-Hi) | 
EPI-Hi shall be capable of measuring energetic electrons over solar orbital distances of 9.86 Rs to 0.25 AU with an energy range of 0.5 MeV (TBR) to ≥ 3 MeV. | 
Description/Clarification | 
It is presently thought that there will be no gap between the EPI-Lo and EPI-Hi energy coverages for electrons, but a factor of 2 energy gap is allowed to take into account the possibility that the energy ranges actually achieved may differ slightly from those presently planned. If there were a gap it would be located near an energy of 0.5 MeV. The lower bound on the EPI-Hi energy range might be changed later to maybe as high as 1.0 MeV (?), but the intent is to be as close to 0.5 MeV as possible]. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. The electron energy range should extend from the suprathermal tail of the solar wind up to highly relativistic energies to allow studies of electron acceleration, to trace connectivity of the magnetic field back to structures on the Sun, and to determine release times of energetic particles from the Sun. | ISIS
Parent Traceability | Functional Allocation
MRD-96 : The Mission shall measure energetic electrons, as follows: -- Energy range1: <= 0.05 to >= 3 MeV -- Highest cadence2: <=1s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 45 degree sectors -- Composition4: n/a Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 9: ISIS Measurements
PAY-77: Measurement: Energetic Electrons Bins (EPI-Lo) | 
EPI-Lo shall be capable of measuring electron intensities with at least 6 energy bins per decade. | 
Rationale | Requirement Allocation
The energy binning should be fine enough to investigate spectral features (e.g., high-energy cutoffs) that occur over an energy width smaller than a decade. | ISIS
Parent Traceability | Functional Allocation
MRD-96 : The Mission shall measure energetic electrons, as follows: -- Energy range1: <= 0.05 to >= 3 MeV -- Highest cadence2: <=1s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 45 degree sectors -- Composition4: n/a Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 10: ISIS Measurements
PAY-201: Measurement: Energetic Electrons Bins (EPI-Hi) | 
EPI-Hi shall be capable of measuring electron intensities with at least 6 energy bins per decade. | 
Rationale | Requirement Allocation
The energy binning should be fine enough to investigate spectral features (e.g., high-energy cutoffs) that occur over an energy width smaller than a decade. | ISIS
Parent Traceability | Functional Allocation
MRD-96 : The Mission shall measure energetic electrons, as follows: -- Energy range1: <= 0.05 to >= 3 MeV -- Highest cadence2: <=1s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 45 degree sectors -- Composition4: n/a Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 11: ISIS Measurements
PAY-78: Measurement: Energetic Electrons Cadence (EPI-Lo) | 
EPI-Lo shall be capable of measuring electron count rate in at least one energy range over solar orbital distances of 9.86 Rs to 0.25 AU below 0.5 MeV (TBR) with a time resolution of 1 s or faster. | 
Description/Clarification | 
Electrons from a broad range of energies and incidence angles can be combined in order to increase statistical accuracy. Additional electron rates, subdivided according to energy and incidence angle, will be measurable at various time cadences, ≤ 1 s to ≥ 1 hr, as appropriate to expected counting statistics. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Electron rates at high cadence are needed to look for fast time structure in the energetic particle intensities as might be caused, for example, by rapid changes in the magnetic field direction. Electron rates with good statistical accuracy at slower cadences but higher energy and angular resolution are needed to measure energy spectra, to use velocity dispersion for timing studies, and to investigate the time evolution of energetic electron flows over the course of an event. | ISIS
Parent Traceability | Functional Allocation
MRD-96 : The Mission shall measure energetic electrons, as follows: -- Energy range1: <= 0.05 to >= 3 MeV -- Highest cadence2: <=1s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 45 degree sectors -- Composition4: n/a Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 12: ISIS Measurements
PAY-202: Measurement: Energetic Electrons Cadence (EPI-Hi) | 
EPI-Hi shall be capable of measuring electron count rate in at least one energy range over solar orbital distances of 9.86 Rs to 0.25 AU above 0.5 MeV (TBR) with a time resolution of 1 s or faster. | 
Description/Clarification | 
Electrons from a broad range of energies and incidence angles can be combined in order to increase statistical accuracy. Additional electron rates, subdivided according to energy and incidence angle, will be measurable at various time cadences, ≤ 1 s to ≥ 1 hr, as appropriate to expected counting statistics. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Electron rates at high cadence are needed to look for fast time structure in the energetic particle intensities as might be caused, for example, by rapid changes in the magnetic field direction. Electron rates with good statistical accuracy at slower cadences but higher energy and angular resolution are needed to measure energy spectra, to use velocity dispersion for timing studies, and to investigate the time evolution of energetic electron flows over the course of an event. | ISIS
Parent Traceability | Functional Allocation
MRD-96 : The Mission shall measure energetic electrons, as follows: -- Energy range1: <= 0.05 to >= 3 MeV -- Highest cadence2: <=1s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 45 degree sectors -- Composition4: n/a Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 13: ISIS Measurements
PAY-79: Measurement: Energetic Electrons Angular Sectoring (EPI-Lo) | 
EPI-Lo shall be capable of measuring energetic electron angular distributions over solar orbital distances of 9.86 Rs to 0.25 AU using sectors of width ≤ 45°. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Sectoring of electron intensity measurements is required for deriving pitch angle distributions (in conjunction with measurements of the magnetic field direction), for observing the time evolution of these distributions, and for estimating the fractions of the distributions that are unmeasured due to field of view limitations. | ISIS
Parent Traceability | Functional Allocation
MRD-96 : The Mission shall measure energetic electrons, as follows: -- Energy range1: <= 0.05 to >= 3 MeV -- Highest cadence2: <=1s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 45 degree sectors -- Composition4: n/a Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 14: ISIS Measurements
PAY-266: Measurement: Energetic Electrons Angular Sectoring (EPI-Hi) | 
EPI-Hi shall be capable of measuring energetic electron angular distributions over solar orbital distances of 9.86 Rs to 0.25 AU using sectors of width ≤ 45° over at least 1 steradian in both the sunward and anti-sunward hemisphere. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Sectoring of electron intensity measurements is required for deriving pitch angle distributions (in conjunction with measurements of the magnetic field direction), for observing the time evolution of these distributions, and for estimating the fractions of the distributions that are unmeasured due to field of view limitations. | ISIS
Parent Traceability | Functional Allocation
MRD-96 : The Mission shall measure energetic electrons, as follows: -- Energy range1: <= 0.05 to >= 3 MeV -- Highest cadence2: <=1s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 45 degree sectors -- Composition4: n/a Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 15: ISIS Measurements
PAY-80: Measurement: Protons/Heavy Ions Energy Range (EPI-Lo) | 
EPI-Lo shall be capable of measuring protons and heavy ions (Z ≥ 2) over solar orbital distances of 9.86 Rs to 0.25 AU with an energy range of ≤ 0.05 MeV/nuc to 1 MeV/nuc (TBR). | 
Description/Clarification | 
Minimizing the gap in energy coverage between EPI-Lo and EPI-Hi is important for a good intercalibration of the two instruments and for investigating spectral features (e.g., high energy spectral cutoffs) when they occur near the boundary between the energy coverage of the two instruments. Because of the different techniques used for species identification (ToF vs E for EPI-Lo, dE/dx vs E for EPI-Hi), the size of the gap increases with increasing atomic number. A gap may exist near 1 MeV/nuc where the EPI-Lo and EPI-Hi energy ranges do not converge. This gap will not exceed a factor of 10 (TBR) in energy per nucleon for any given element between H and Si. For Fe the gap may be up to a factor of 20. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. The energy range needs to go from the suprathermal tail of the solar wind at low energies up to the high energies of importance for space weather studies. | ISIS
Parent Traceability | Functional Allocation
MRD-97 : The Mission shall measure energetic protons and heavy ions, as follows: -- Energy range1: <= 0.05 to >= 50 MeV/nucleon -- Highest cadence2: <= 5s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 30 degree sectors -- Composition4: at least H, He, 3He, C, O, Ne, Mg, Si, Fe Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 16: ISIS Measurements
PAY-203: Measurement: Protons/Heavy Ions Energy Range (EPI-Hi) | 
EPI-Hi shall be capable of measuring protons and heavy ions (Z ≥ 2) over solar orbital distances of 9.86 Rs to 0.25 AU with an energy range of 1 MeV/nuc (TBR) to ≥ 50 MeV/nuc. | 
Description/Clarification | 
Minimizing the gap in energy coverage between EPI-Lo and EPI-Hi is important for a good intercalibration of the two instruments and for investigating spectral features (e.g., high energy spectral cutoffs) when they occur near the boundary between the energy coverage of the two instruments. Because of the different techniques used for species identification (ToF vs E for EPI-Lo, dE/dx vs E for EPI-Hi), the size of the gap increases with increasing atomic number. A gap may exist near 1 MeV/nuc where the EPI-Lo and EPI-Hi energy ranges do not converge. This gap will not exceed a factor of 10 (TBR) in energy per nucleon for any given element between H and Si. For Fe the gap may be up to a factor of 20. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. The energy range needs to go from the suprathermal tail of the solar wind at low energies up to the high energies of importance for space weather studies. | ISIS
Parent Traceability | Functional Allocation
MRD-97 : The Mission shall measure energetic protons and heavy ions, as follows: -- Energy range1: <= 0.05 to >= 50 MeV/nucleon -- Highest cadence2: <= 5s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 30 degree sectors -- Composition4: at least H, He, 3He, C, O, Ne, Mg, Si, Fe Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 17: ISIS Measurements
PAY-81: Measurement: Protons/Heavy Ions Bins (EPI-Lo) | 
EPI-Lo shall be capable of measuring proton and heavy ion intensities with at least 6 energy bins per decade. | 
Rationale | Requirement Allocation
The energy binning should be fine enough to investigate spectral features (e.g., high-energy cutoffs) that occur over an energy width smaller than a decade. | ISIS
Parent Traceability | Functional Allocation
MRD-97 : The Mission shall measure energetic protons and heavy ions, as follows: -- Energy range1: <= 0.05 to >= 50 MeV/nucleon -- Highest cadence2: <= 5s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 30 degree sectors -- Composition4: at least H, He, 3He, C, O, Ne, Mg, Si, Fe Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 18: ISIS Measurements
PAY-205: Measurement: Protons/Heavy Ions Bins (EPI-Hi) | 
EPI-Hi shall be capable of measuring proton and heavy ion intensities with at least 6 energy bins per decade. | 
Rationale | Requirement Allocation
The energy binning should be fine enough to investigate spectral features (e.g., high-energy cutoffs) that occur over an energy width smaller than a decade. | ISIS
Parent Traceability | Functional Allocation
MRD-97 : The Mission shall measure energetic protons and heavy ions, as follows: -- Energy range1: <= 0.05 to >= 50 MeV/nucleon -- Highest cadence2: <= 5s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 30 degree sectors -- Composition4: at least H, He, 3He, C, O, Ne, Mg, Si, Fe Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 19: ISIS Measurements
PAY-82: Measurement: Protons/Heavy Ions Cadence (EPI-Lo) | 
EPI-Lo shall be capable of measuring proton count rate in at least one energy range over solar orbital distances of 9.86 Rs to 0.25 AU below 1 MeV with a time resolution of 5 s or faster. | 
Description/Clarification | 
Electrons from a broad range of energies and incidence angles can be combined in order to increase statistical accuracy. Additional proton and heavy-ion rates, subdivided according to species, energy, and incidence angle, will be measurable at various time cadences, ≤ 5 s to ≥ 1 hr, as appropriate to expected counting statistics. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Proton rates at high cadence are needed to look for fast time structure in the energetic particle intensities as might be caused, for example, by a rapid changes in the magnetic field direction or by the passage of a shock. Proton and heavy-ion rates with good statistical accuracy at slower cadences but higher energy and angular resolution are needed to measure energy spectra and angular distributions and to trace their evolution over the course of an event. | ISIS
Parent Traceability | Functional Allocation
MRD-97 : The Mission shall measure energetic protons and heavy ions, as follows: -- Energy range1: <= 0.05 to >= 50 MeV/nucleon -- Highest cadence2: <= 5s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 30 degree sectors -- Composition4: at least H, He, 3He, C, O, Ne, Mg, Si, Fe Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 20: ISIS Measurements
PAY-267: Measurement: Protons/Heavy Ions Cadence (EPI-Hi) | 
EPI-Hi shall be capable of measuring proton count rate in at least one energy range over solar orbital distances of 9.86 Rs to 0.25 AU above 1 MeV with a time resolution of 5 s or faster. | 
Description/Clarification | 
Electrons from a broad range of energies and incidence angles can be combined in order to increase statistical accuracy. Additional proton and heavy-ion rates, subdivided according to species, energy, and incidence angle, will be measurable at various time cadences, ≤ 5 s to ≥ 1 hr, as appropriate to expected counting statistics. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Proton rates at high cadence are needed to look for fast time structure in the energetic particle intensities as might be caused, for example, by a rapid changes in the magnetic field direction or by the passage of a shock. Proton and heavy-ion rates with good statistical accuracy at slower cadences but higher energy and angular resolution are needed to measure energy spectra and angular distributions and to trace their evolution over the course of an event. | ISIS
Parent Traceability | Functional Allocation
MRD-97 : The Mission shall measure energetic protons and heavy ions, as follows: -- Energy range1: <= 0.05 to >= 50 MeV/nucleon -- Highest cadence2: <= 5s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 30 degree sectors -- Composition4: at least H, He, 3He, C, O, Ne, Mg, Si, Fe Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 21: ISIS Measurements
PAY-83: Measurement: Protons/Heavy Ions Angular Sectoring (EPI-Lo) | 
EPI-Lo shall be capable of measuring proton and heavy ion angular distributions over solar orbital distances of 9.86 Rs to 0.25 AU using sectors of width ≤ 30° (TBR). | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Sectoring of proton and heavy-ion intensity measurements is required for deriving pitch angle distributions (in conjunction with measurements of the magnetic field direction), for observing the time evolution of these distributions, and for estimating the fractions of the distributions that are unmeasured due to field-of-view limitations. | ISIS
Parent Traceability | Functional Allocation
MRD-97 : The Mission shall measure energetic protons and heavy ions, as follows: -- Energy range1: <= 0.05 to >= 50 MeV/nucleon -- Highest cadence2: <= 5s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 30 degree sectors -- Composition4: at least H, He, 3He, C, O, Ne, Mg, Si, Fe Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 22: ISIS Measurements
PAY-206: Measurement: Protons/Heavy Ions Angular Sectoring (EPI-Hi) | 
EPI-Hi shall be capable of measuring proton and heavy ion angular distributions over solar orbital distances of 9.86 Rs to 0.25 AU using sectors of width ≤ 30° (TBR). | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Sectoring of proton and heavy-ion intensity measurements is required for deriving pitch angle distributions (in conjunction with measurements of the magnetic field direction), for observing the time evolution of these distributions, and for estimating the fractions of the distributions that are unmeasured due to field-of-view limitations. | ISIS
Parent Traceability | Functional Allocation
MRD-97 : The Mission shall measure energetic protons and heavy ions, as follows: -- Energy range1: <= 0.05 to >= 50 MeV/nucleon -- Highest cadence2: <= 5s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 30 degree sectors -- Composition4: at least H, He, 3He, C, O, Ne, Mg, Si, Fe Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 23: ISIS Measurements
PAY-84: Measurement: Protons/Heavy Ions Composition (EPI-Lo) | 
EPI-Lo shall be capable of resolving at least the elements H, He, C, O, Ne, Mg, Si, and Fe, each with a FWHM charge (Z) resolution ≤ 0.5 times the charge separation from the nearest neighbor element in the list. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. These elements, which are the most abundant in solar energetic particle events, can sample a wide range in the ratio M/Q (mass to ionic charge) and provide important diagnostics of the acceleration mechanism. A FWHM resolution of half the spacing to the nearest adjacent major element (or isotope in the case of He isotope studies) will allow measurements of abundances ratios up to at least as great as 10:1. | ISIS
Parent Traceability | Functional Allocation
MRD-97 : The Mission shall measure energetic protons and heavy ions, as follows: -- Energy range1: <= 0.05 to >= 50 MeV/nucleon -- Highest cadence2: <= 5s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 30 degree sectors -- Composition4: at least H, He, 3He, C, O, Ne, Mg, Si, Fe Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 24: ISIS Measurements
PAY-268: Measurement: Protons/Heavy Ions Composition (EPI-Hi) | 
EPI-Hi shall be capable of resolving at least the elements H, He, C, O, Ne, Mg, Si, and Fe, each with a FWHM charge (Z) resolution ≤ 0.5 times the charge separation from the nearest neighbor element in the list. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. These elements, which are the most abundant in solar energetic particle events, can sample a wide range in the ratio M/Q (mass to ionic charge) and provide important diagnostics of the acceleration mechanism. A FWHM resolution of half the spacing to the nearest adjacent major element (or isotope in the case of He isotope studies) will allow measurements of abundances ratios up to at least as great as 10:1. | ISIS
Parent Traceability | Functional Allocation
MRD-97 : The Mission shall measure energetic protons and heavy ions, as follows: -- Energy range1: <= 0.05 to >= 50 MeV/nucleon -- Highest cadence2: <= 5s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 30 degree sectors -- Composition4: at least H, He, 3He, C, O, Ne, Mg, Si, Fe Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 25: ISIS Measurements
PAY-223: Measurement: Protons/Heavy Ions Element Ratio & mass resolution (EPI-Lo) | 
EPI-Lo shall be capable of measuring the 3He/4He ratio over at least TBD decades in energy below 1 MeV/nuc and resolving 4He with a FWHM mass resolution ≤ 0.5 AMU (TBR). | 
Rationale | Requirement Allocation
This requirement supports Level 2 Mission Science Requirements. | ISIS
Parent Traceability | Functional Allocation
MRD-97 : The Mission shall measure energetic protons and heavy ions, as follows: -- Energy range1: <= 0.05 to >= 50 MeV/nucleon -- Highest cadence2: <= 5s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 30 degree sectors -- Composition4: at least H, He, 3He, C, O, Ne, Mg, Si, Fe Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 26: ISIS Measurements
PAY-224: Measurement: Protons/Heavy Ions Element Ratio & mass resolution (EPI-Hi) | 
EPI-Hi shall be capable of measuring the 3He/4He ratio over at least one decade in energy above 1 MeV/nuc (TBR) and resolving 4He with a FWHM mass resolution ≤ 0.5 AMU (TBR). | 
Rationale | Requirement Allocation
This requirement supports Level 2 Mission Science Requirements. | ISIS
Parent Traceability | Functional Allocation
MRD-97 : The Mission shall measure energetic protons and heavy ions, as follows: -- Energy range1: <= 0.05 to >= 50 MeV/nucleon -- Highest cadence2: <= 5s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 30 degree sectors -- Composition4: at least H, He, 3He, C, O, Ne, Mg, Si, Fe Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 27: ISIS Measurements
PAY-85: Measurement: SEP Event Energetic Electrons (EPI-Lo) | 
EPI-Lo shall be capable of measuring energy spectra and angular distributions for energetic electrons from 0.05 MeV to 0.5 MeV (TBR) for solar energetic particle event intensities up to at least 10^6 particles/cm2-sr-s (TBR). | 
Rationale | Requirement Allocation
Capability for making good measurements, without excessive saturation or background, during times of high particle intensity is important for assuring that high quality data can be obtained even in solar energetic particle events that occur when the spacecraft is close to the Sun. Intensities are expected to increase at least as fast as 1/r2 going in toward the Sun. | ISIS
Parent Traceability | Functional Allocation
MRD-96 : The Mission shall measure energetic electrons, as follows: -- Energy range1: <= 0.05 to >= 3 MeV -- Highest cadence2: <=1s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 45 degree sectors -- Composition4: n/a Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 28: ISIS Measurements
PAY-226: Measurement: SEP Event Ions (EPI-Lo) | 
EPI-Lo shall be capable of measuring energy spectra, composition, and angular distributions for ions from ≤ 0.05 MeV/nuc to ≥ 5 MeV/nuc to a maximum energy of 15 MeV for solar energetic particle event intensities up to at least 10^6 particles/cm2-sr-s. | 
Rationale | Requirement Allocation
Capability for making good measurements, without excessive saturation or background, during times of high particle intensity is important for assuring that high quality data can be obtained even in solar energetic particle events that occur when the spacecraft is close to the Sun. Intensities are expected to increase at least as fast as 1/r2 going in toward the Sun. | ISIS
Parent Traceability | Functional Allocation
MRD-97 : The Mission shall measure energetic protons and heavy ions, as follows: -- Energy range1: <= 0.05 to >= 50 MeV/nucleon -- Highest cadence2: <= 5s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 30 degree sectors -- Composition4: at least H, He, 3He, C, O, Ne, Mg, Si, Fe Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 29: ISIS Measurements
PAY-228: Measurement: SEP Event Energetic Electrons (EPI-Hi) | 
EPI-Hi shall be capable of measuring energy spectra and angular distributions for energetic electrons from 0.5 MeV (TBR) to ≥3 MeV up to 10% (TBR) of an upper-limit spectrum of electron intensities specified in the SPP Environmental Design and Test Requirements Document, 7434-9039. | 
Rationale | Requirement Allocation
n the case of the rare occurrence of an extreme solar energetic particle event close to perihelion, some saturation of the instrument is likely to occur when operated in its normal mode. The instrument will be designed to allow a graceful degradation of performance as intensities increase above the specified levels and maximize the achievable scientific return up to the full level given by the upper-limit spectrum. | ISIS
Parent Traceability | Functional Allocation
MRD-96 : The Mission shall measure energetic electrons, as follows: -- Energy range1: <= 0.05 to >= 3 MeV -- Highest cadence2: <=1s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 45 degree sectors -- Composition4: n/a Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 30: ISIS Measurements
PAY-230: Measurement: SEP Event Ions (EPI-Hi) | 
EPI-Hi shall be capable of measuring energy spectra, composition, and angular distributions for energetic ions from 1 MeV/nuc (TBR) to ≥ 50 MeV/nuc up to 10% (TBR) of an upper-limit spectrum of proton intensities specified in the SPP Environmental Design and Test Requirements Document, 7434-9039. | 
Rationale | Requirement Allocation
In the case of the rare occurrence of an extreme solar energetic particle event close to perihelion, some saturation of the instrument is likely to occur when operated in its normal mode. The instrument will be designed to allow a graceful degradation of performance as intensities increase above the specified levels and maximize the achievable scientific return up to the full level given by the upper-limit spectrum. | ISIS
Parent Traceability | Functional Allocation
MRD-97 : The Mission shall measure energetic protons and heavy ions, as follows: -- Energy range1: <= 0.05 to >= 50 MeV/nucleon -- Highest cadence2: <= 5s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 30 degree sectors -- Composition4: at least H, He, 3He, C, O, Ne, Mg, Si, Fe Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 31: ISIS Measurements
PAY-87: Measurement: Energetic Electrons Field-of-View (EPI-Lo) | 
EPI-Lo shall be capable of measuring energetic electrons over solar orbital distances of 9.86 Rs to 0.25 AU with a ≥ π/2 steradians FOV in the sunward hemisphere and a ≥ π/2 steradians FOV in the anti-sunward hemisphere including coverage within 10° of the Spacecraft-Sun line, subject to the constraints and FOV obstructions defined in the ISIS-to-Spacecraft ICD (7434-9058). | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. The FOV should cover as much as the sky as possible in order to allow accurate particle intensity measurements even when the angular distribution is highly anisotropic or the magnetic field deviates strongly from the nominal Parker spiral. The minimum FOV requirement allows measurement of particles with pitch angles out to ~40° from the nominal field direction in both the forward and backward directions and enables good determinations of first order anisotropies. Additional measurements closer to 90° pitch angle are important for investigating the time evolution of particle pitch angle distributions and for measuring higher order anisotropies. | ISIS
Parent Traceability | Functional Allocation
MRD-96 : The Mission shall measure energetic electrons, as follows: -- Energy range1: <= 0.05 to >= 3 MeV -- Highest cadence2: <=1s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 45 degree sectors -- Composition4: n/a Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 32: ISIS Measurements
PAY-208: Measurement: Energetic Electrons Field-of-View (EPI-Hi) | 
EPI-Hi shall be capable of measuring energetic electrons over solar orbital distances of 9.86 Rs to 0.25 AU with a ≥ π/2 steradians FOV in the sunward hemisphere and a ≥ π/2 steradians FOV in the anti-sunward hemisphere including coverage within 10° of the Spacecraft-Sun line, subject to the constraints and FOV obstructions defined in the ISIS-to-Spacecraft ICD (7434-9058). | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. The FOV should cover as much as the sky as possible in order to allow accurate particle intensity measurements even when the angular distribution is highly anisotropic or the magnetic field deviates strongly from the nominal Parker spiral. The minimum FOV requirement allows measurement of particles with pitch angles out to ~40° from the nominal field direction in both the forward and backward directions and enables good determinations of first order anisotropies. Additional measurements closer to 90° pitch angle are important for investigating the time evolution of particle pitch angle distributions and for measuring higher order anisotropies. | ISIS
Parent Traceability | Functional Allocation
MRD-96 : The Mission shall measure energetic electrons, as follows: -- Energy range1: <= 0.05 to >= 3 MeV -- Highest cadence2: <=1s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 45 degree sectors -- Composition4: n/a Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 33: ISIS Measurements
PAY-270: Measurement: Energetic Protons/Heavy Ions Field-of-View (EPI-Lo) | 
EPI-Lo shall be capable of measuring protons and heavy ions over solar orbital distances of 9.86 Rs to 0.25 AU with a ≥ π/2 steradians FOV in the sunward hemisphere and a ≥ π/2 steradians FOV in the anti-sunward hemisphere including coverage within 10° of the Spacecraft-Sun line, subject to the constraints and FOV obstructions defined in the ISIS-to-Spacecraft ICD (7434-9058). | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. The FOV should cover as much as the sky as possible in order to allow accurate particle intensity measurements even when the angular distribution is highly anisotropic or the magnetic field deviates strongly from the nominal Parker spiral. The minimum FOV requirement allows measurement of particles with pitch angles out to ~40° from the nominal field direction in both the forward and backward directions and enables good determinations of first order anisotropies. Additional measurements closer to 90° pitch angle are important for investigating the time evolution of particle pitch angle distributions and for measuring higher order anisotropies. | ISIS
Parent Traceability | Functional Allocation
MRD-97 : The Mission shall measure energetic protons and heavy ions, as follows: -- Energy range1: <= 0.05 to >= 50 MeV/nucleon -- Highest cadence2: <= 5s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 30 degree sectors -- Composition4: at least H, He, 3He, C, O, Ne, Mg, Si, Fe Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 34: ISIS Measurements
PAY-271: Measurement: Energetic Protons/Heavy Ions Field-of-View (EPI-Hi) | 
EPI-Hi shall be capable of measuring protons and heavy ions over solar orbital distances of 9.86 Rs to 0.25 AU with a ≥ π/2 steradians FOV in the sunward hemisphere and a ≥ π/2 steradians FOV in the anti-sunward hemisphere including coverage within 10° of the Spacecraft-Sun line, subject to the constraints and FOV obstructions defined in the ISIS-to-Spacecraft ICD (7434-9058). | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. The FOV should cover as much as the sky as possible in order to allow accurate particle intensity measurements even when the angular distribution is highly anisotropic or the magnetic field deviates strongly from the nominal Parker spiral. The minimum FOV requirement allows measurement of particles with pitch angles out to ~40° from the nominal field direction in both the forward and backward directions and enables good determinations of first order anisotropies. Additional measurements closer to 90° pitch angle are important for investigating the time evolution of particle pitch angle distributions and for measuring higher order anisotropies. | ISIS
Parent Traceability | Functional Allocation
MRD-97 : The Mission shall measure energetic protons and heavy ions, as follows: -- Energy range1: <= 0.05 to >= 50 MeV/nucleon -- Highest cadence2: <= 5s for selected rates -- Field of view3: >= π/2 sr in sunward and anti-sunward hemispheres -- Angular sectoring: <= 30 degree sectors -- Composition4: at least H, He, 3He, C, O, Ne, Mg, Si, Fe Notes: 1 Combined energy range of all sensors; small gaps in energy coverage are acceptable 2 Additional rates at lower cadences, as appropriate, for expected statistics and bit rate allocation 3 Combined sky coverage of all sensors, some regions densely sampled rather than 100% covered 4 Measured species; not all measured under all conditions | 

## Slide 35: SWEAP Measurements
PAY-56: Measurement: Thermal Ions Field-of-View (nadir-direction) | 
SPC shall be capable of measuring thermal ions in the nadir direction over solar orbital distances of 9.86 Rs to 0.25 AU with a ≥ 28 degree half-angle (≥ 56 degree full-angle) cone FOV oriented within 10 degrees of the Spacecraft z-axis, subject to the FOV obstructions defined in the SWEAP to Spacecraft ICD 7434-9056. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. SWEAP must be able to determine certain bulk properties of the solar wind, such as the p core and e- strahl. This implies i+ and e- fields of view that cover a large fraction of the sky. | SWEAP
Parent Traceability | Functional Allocation
MRD-93 : The Mission shall measure thermal ions, as follows: -- Energy range1: 10 eV – 20 keV -- Energy resolution: < 20% -- FOV: nadir and ram directions -- Angular resolution2: 10 deg x 25 deg -- VDF cadence: 1 Hz -- Mass resolution3: d(m/q)/(m/q) < 25% Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 36: SWEAP Measurements
PAY-182: Measurement: Thermal Ions Field-of-View (ram-direction) | 
SPAN-A+ shall be capable of measuring thermal ions in the ram direction over solar orbital distances of 9.86 Rs to 0.25 AU with a FOV of ≥ 180 degrees about the Spacecraft y-axis and ≥ 30 degrees out of the Spacecraft X-Z plane for ions with energy/charge ≤ 4 keV/q, subject to the FOV obstructions defined in the SWEAP to Spacecraft ICD 7434-9056. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. SWEAP must be able to determine certain bulk properties of the solar wind, such as the p core and e- strahl. This implies i+ and e- fields of view that cover a large fraction of the sky. | SWEAP
Parent Traceability | Functional Allocation
MRD-93 : The Mission shall measure thermal ions, as follows: -- Energy range1: 10 eV – 20 keV -- Energy resolution: < 20% -- FOV: nadir and ram directions -- Angular resolution2: 10 deg x 25 deg -- VDF cadence: 1 Hz -- Mass resolution3: d(m/q)/(m/q) < 25% Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 37: SWEAP Measurements
PAY-57: Measurement: Thermal Ions Minimum Ion Energy (nadir-direction) | 
SPC shall be capable of measuring thermal ions in the nadir direction over solar orbital distances of 9.86 Rs to 0.25 AU with a minimum energy/charge of ≤ 150 eV/q, except when the Spacecraft potential is > + TBD V. | 
Description/Clarification | 
SWEAP is not required to meet L2 minimum energy requirement in all directions. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. | SWEAP
Parent Traceability | Functional Allocation
MRD-93 : The Mission shall measure thermal ions, as follows: -- Energy range1: 10 eV – 20 keV -- Energy resolution: < 20% -- FOV: nadir and ram directions -- Angular resolution2: 10 deg x 25 deg -- VDF cadence: 1 Hz -- Mass resolution3: d(m/q)/(m/q) < 25% Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 38: SWEAP Measurements
PAY-183: Measurement: Thermal Ions Minimum Ion Energy (ram-direction) | 
SPAN-A+ shall be capable of measuring thermal ions in the ram direction over solar orbital distances of 9.86 Rs to 0.25 AU with a minimum energy/charge of ≤ 10 eV/q, except when the Spacecraft potential is > + TBD V. | 
Description/Clarification | 
SWEAP is not required to meet L2 minimum energy requirement in all directions. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. | SWEAP
Parent Traceability | Functional Allocation
MRD-93 : The Mission shall measure thermal ions, as follows: -- Energy range1: 10 eV – 20 keV -- Energy resolution: < 20% -- FOV: nadir and ram directions -- Angular resolution2: 10 deg x 25 deg -- VDF cadence: 1 Hz -- Mass resolution3: d(m/q)/(m/q) < 25% Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 39: SWEAP Measurements
PAY-58: Measurement: Thermal Ions Maximum Ion Energy (nadir-direction, close range) | 
SPC shall be capable of measuring thermal ions in the nadir direction over solar orbital distances of 9.86 Rs to 20 Rs with a maximum energy/charge of > 4 keV/q. | 
Description/Clarification | 
SWEAP is not required to meet L2 maximum energy requirement in all directions and distances. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. | SWEAP
Parent Traceability | Functional Allocation
MRD-93 : The Mission shall measure thermal ions, as follows: -- Energy range1: 10 eV – 20 keV -- Energy resolution: < 20% -- FOV: nadir and ram directions -- Angular resolution2: 10 deg x 25 deg -- VDF cadence: 1 Hz -- Mass resolution3: d(m/q)/(m/q) < 25% Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 40: SWEAP Measurements
PAY-269: Measurement: Thermal Ions Maximum Ion Energy (nadir-direction, far range) | 
SPC shall be capable of measuring thermal ions in the nadir direction over solar orbital distances of 20 Rs to 0.25 AU with a maximum energy/charge of > 6 keV/q. | 
Description/Clarification | 
SWEAP is not required to meet L2 maximum energy requirement in all directions and distances. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. | SWEAP
Parent Traceability | Functional Allocation
MRD-93 : The Mission shall measure thermal ions, as follows: -- Energy range1: 10 eV – 20 keV -- Energy resolution: < 20% -- FOV: nadir and ram directions -- Angular resolution2: 10 deg x 25 deg -- VDF cadence: 1 Hz -- Mass resolution3: d(m/q)/(m/q) < 25% Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 41: SWEAP Measurements
PAY-184: Measurement: Thermal Ions Maximum Ion Energy (ram-direction) | 
SPAN-A+ shall be capable of measuring thermal ions in the ram direction over solar orbital distances of 9.86 Rs to 0.25 AU with a maximum energy/charge of > 20 keV/q (TBR). | 
Description/Clarification | 
SWEAP is not required to meet L2 maximum energy requirement in all directions and distances. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. | SWEAP
Parent Traceability | Functional Allocation
MRD-93 : The Mission shall measure thermal ions, as follows: -- Energy range1: 10 eV – 20 keV -- Energy resolution: < 20% -- FOV: nadir and ram directions -- Angular resolution2: 10 deg x 25 deg -- VDF cadence: 1 Hz -- Mass resolution3: d(m/q)/(m/q) < 25% Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 42: SWEAP Measurements
PAY-59: Measurement: Thermal Ions Energy Resolution (nadir-facing) | 
SPC shall be capable of measuring thermal ions in the nadir direction over solar orbital distances of 9.86 Rs to 0.25 AU with an energy/charge (E/q) resolution of d(E/q)/(E/q) ≤ 20%. | 
Description/Clarification | 
Energy resolution is needed to determine ion temperatures. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. | SWEAP
Parent Traceability | Functional Allocation
MRD-93 : The Mission shall measure thermal ions, as follows: -- Energy range1: 10 eV – 20 keV -- Energy resolution: < 20% -- FOV: nadir and ram directions -- Angular resolution2: 10 deg x 25 deg -- VDF cadence: 1 Hz -- Mass resolution3: d(m/q)/(m/q) < 25% Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 43: SWEAP Measurements
PAY-185: Measurement: Thermal Ions Energy Resolution (ram-facing) | 
SPAN-A+ shall be capable of measuring thermal ions in the ram direction over solar orbital distances of 9.86 Rs to 0.25 AU with an energy/charge (E/q) resolution of d(E/q)/(E/q) ≤ 20%. | 
Description/Clarification | 
Energy resolution is needed to determine ion temperatures. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. | SWEAP
Parent Traceability | Functional Allocation
MRD-93 : The Mission shall measure thermal ions, as follows: -- Energy range1: 10 eV – 20 keV -- Energy resolution: < 20% -- FOV: nadir and ram directions -- Angular resolution2: 10 deg x 25 deg -- VDF cadence: 1 Hz -- Mass resolution3: d(m/q)/(m/q) < 25% Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 44: SWEAP Measurements
PAY-60: Measurement: Thermal Ions Angular Resolution (nadir-facing) | 
SPC shall be capable of measuring thermal ion flow angles in the nadir direction over solar orbital distances of 9.86 Rs to 0.25 AU with an angular resolution of ≤ 10 degrees, except when Spacecraft potential is > + TBD V. | 
Description/Clarification | 
SWEAP is not required to meet L2 angular resolution requirement in all directions. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. | SWEAP
Parent Traceability | Functional Allocation
MRD-93 : The Mission shall measure thermal ions, as follows: -- Energy range1: 10 eV – 20 keV -- Energy resolution: < 20% -- FOV: nadir and ram directions -- Angular resolution2: 10 deg x 25 deg -- VDF cadence: 1 Hz -- Mass resolution3: d(m/q)/(m/q) < 25% Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 45: SWEAP Measurements
PAY-186: Measurement: Thermal Ions Angular Resolution (ram-facing) | 
SPAN-A+ shall be capable of measuring thermal ions in the ram direction over solar orbital distances of 9.86 Rs to 0.25 AU with an angular resolution of ≤ 25 degrees about the Spacecraft y-axis and ≤ 10 degrees in the Spacecraft X-Z plane, except when Spacecraft potential is > + TBD V. | 
Description/Clarification | 
SWEAP is not required to meet L2 angular resolution requirement in all directions. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. | SWEAP
Parent Traceability | Functional Allocation
MRD-93 : The Mission shall measure thermal ions, as follows: -- Energy range1: 10 eV – 20 keV -- Energy resolution: < 20% -- FOV: nadir and ram directions -- Angular resolution2: 10 deg x 25 deg -- VDF cadence: 1 Hz -- Mass resolution3: d(m/q)/(m/q) < 25% Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 46: SWEAP Measurements
PAY-61: Measurement: Thermal Ions Velocity Distribution Function (nadir-facing) | 
SPC shall be capable of measuring thermal ions in the nadir direction over solar orbital distances of 9.86 Rs to 0.25 AU with a VDF measurement cadence of ≥ 1 Hz. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. | SWEAP
Parent Traceability | Functional Allocation
MRD-93 : The Mission shall measure thermal ions, as follows: -- Energy range1: 10 eV – 20 keV -- Energy resolution: < 20% -- FOV: nadir and ram directions -- Angular resolution2: 10 deg x 25 deg -- VDF cadence: 1 Hz -- Mass resolution3: d(m/q)/(m/q) < 25% Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 47: SWEAP Measurements
PAY-187: Measurement: Thermal Ions Velocity Distribution Function (ram-facing) | 
SPAN-A+ shall be capable of measuring thermal ions in the ram direction over solar orbital distances of 9.86 Rs to 0.25 AU with a VDF measurement cadence of ≥ 1 Hz. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. | SWEAP
Parent Traceability | Functional Allocation
MRD-93 : The Mission shall measure thermal ions, as follows: -- Energy range1: 10 eV – 20 keV -- Energy resolution: < 20% -- FOV: nadir and ram directions -- Angular resolution2: 10 deg x 25 deg -- VDF cadence: 1 Hz -- Mass resolution3: d(m/q)/(m/q) < 25% Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 48: SWEAP Measurements
PAY-62: Measurement: Thermal Ions Mass Resolution | 
SPAN-A+ shall be capable of measuring thermal ions in the ram direction over solar orbital distances of 9.86 Rs to 0.25 AU with a mass/charge resolution d(m/q)/(m/q) of ≤ 25%. | 
Description/Clarification | 
Distinguish between proton & alpha particles with the same energy per charge by also measuring their mass/charge ratio. SWEAP is not required to meet L2 mass resolution in all directions. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. | SWEAP
Parent Traceability | Functional Allocation
MRD-93 : The Mission shall measure thermal ions, as follows: -- Energy range1: 10 eV – 20 keV -- Energy resolution: < 20% -- FOV: nadir and ram directions -- Angular resolution2: 10 deg x 25 deg -- VDF cadence: 1 Hz -- Mass resolution3: d(m/q)/(m/q) < 25% Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 49: SWEAP Measurements
PAY-63: Measurement: Thermal Electrons Field-of-View (nadir-facing) | 
SPC shall be capable of measuring thermal electrons in the nadir direction over solar orbital distances of 9.86 Rs to 0.25 AU with a ≥ 28 degree half-angle (≥ 56 degree full-angle) cone FOV oriented within 10 degrees of the Spacecraft z-axis, subject to the FOV obstructions defined in the SWEAP to Spacecraft ICD 7434-9056. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Electron flux is needed to determine electron properties because the thermal electron distribution is subsonic, and needed to detect bi-directional electron flow along magnetic fields. | SWEAP
Parent Traceability | Functional Allocation
MRD-94 : The Mission shall measure thermal electrons, as follows: -- Energy range1: 5 eV – 20 keV -- Energy resolution: < 20% -- FOV: > 75% of the sky -- Angular resolution2: 10 deg x 10 deg -- VDF cadence: 1 Hz -- Mass resolution3: n/a Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 50: SWEAP Measurements
PAY-188: Measurement: Thermal Electrons Field-of-View (ram-facing) | 
SPAN-A+ shall be capable of measuring thermal electrons in the ram direction over solar orbital distances of 9.86 Rs to 0.25 AU with a FOV of ≥ 180 degrees about the Spacecraft y-axis (TBR) and ≥ 30 degrees out of Spacecraft X-Z plane (TBR) for electrons with energy ≤ 4 keV, subject to the FOV obstructions defined in the SWEAP to Spacecraft ICD 7434-9056. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Electron flux is needed to determine electron properties because the thermal electron distribution is subsonic, and needed to detect bi-directional electron flow along magnetic fields. | SWEAP
Parent Traceability | Functional Allocation
MRD-94 : The Mission shall measure thermal electrons, as follows: -- Energy range1: 5 eV – 20 keV -- Energy resolution: < 20% -- FOV: > 75% of the sky -- Angular resolution2: 10 deg x 10 deg -- VDF cadence: 1 Hz -- Mass resolution3: n/a Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 51: SWEAP Measurements
PAY-189: Measurement: Thermal Electrons Field-of-View (anti-ram-facing) | 
SPAN-B shall be capable of measuring thermal electrons in the anti-ram direction over solar orbital distances of 9.86 Rs to 0.25 AU with a FOV of ≥ 180 degrees about the Spacecraft z-axis (TBR) and ≥ 30 degrees out of Spacecraft X-Y plane (TBR) for electrons with energy ≤ 4 keV, subject to the FOV obstructions defined in the SWEAP to Spacecraft ICD 7434-9056. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Electron flux is needed to determine electron properties because the thermal electron distribution is subsonic, and needed to detect bi-directional electron flow along magnetic fields. | SWEAP
Parent Traceability | Functional Allocation
MRD-94 : The Mission shall measure thermal electrons, as follows: -- Energy range1: 5 eV – 20 keV -- Energy resolution: < 20% -- FOV: > 75% of the sky -- Angular resolution2: 10 deg x 10 deg -- VDF cadence: 1 Hz -- Mass resolution3: n/a Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 52: SWEAP Measurements
PAY-64: Measurement: Thermal Electrons Minimum Electron Energy (nadir-facing) | 
SPC shall be capable of measuring thermal electrons in the nadir direction over solar orbital distances of 9.86 Rs to 0.25 AU with a minimum energy of ≤ 100 eV (TBR), except when the Spacecraft potential is ≤ - TBD V. | 
Description/Clarification | 
SWEAP is not required to meet L2 minimum energy requirement in all directions. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. This energy range is needed to observe the thermal electron population & the suprathermal electron population that dominates the heat flux of the solar wind. | SWEAP
Parent Traceability | Functional Allocation
MRD-94 : The Mission shall measure thermal electrons, as follows: -- Energy range1: 5 eV – 20 keV -- Energy resolution: < 20% -- FOV: > 75% of the sky -- Angular resolution2: 10 deg x 10 deg -- VDF cadence: 1 Hz -- Mass resolution3: n/a Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 53: SWEAP Measurements
PAY-190: Measurement: Thermal Electrons Minimum Electron Energy (ram-facing) | 
SPAN-A+ shall be capable of measuring thermal electrons in the ram direction over solar orbital distances of 9.86 Rs to 0.25 AU with a minimum energy of ≤ 5 eV, except when the Spacecraft potential is ≤ - TBD V. | 
Description/Clarification | 
SWEAP is not required to meet L2 minimum energy requirement in all directions. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. This energy range is needed to observe the thermal electron population & the suprathermal electron population that dominates the heat flux of the solar wind. | SWEAP
Parent Traceability | Functional Allocation
MRD-94 : The Mission shall measure thermal electrons, as follows: -- Energy range1: 5 eV – 20 keV -- Energy resolution: < 20% -- FOV: > 75% of the sky -- Angular resolution2: 10 deg x 10 deg -- VDF cadence: 1 Hz -- Mass resolution3: n/a Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 54: SWEAP Measurements
PAY-191: Measurement: Thermal Electrons Minimum Electron Energy (anti-ram-facing) | 
SPAN-B shall be capable of measuring thermal electrons in the anti-ram direction over solar orbital distances of 9.86 Rs to 0.25 AU with a minimum energy of ≤ 5 eV, except when the Spacecraft potential is ≤ - TBD V. | 
Description/Clarification | 
SWEAP is not required to meet L2 minimum energy requirement in all directions. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. This energy range is needed to observe the thermal electron population & the suprathermal electron population that dominates the heat flux of the solar wind. | SWEAP
Parent Traceability | Functional Allocation
MRD-94 : The Mission shall measure thermal electrons, as follows: -- Energy range1: 5 eV – 20 keV -- Energy resolution: < 20% -- FOV: > 75% of the sky -- Angular resolution2: 10 deg x 10 deg -- VDF cadence: 1 Hz -- Mass resolution3: n/a Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 55: SWEAP Measurements
PAY-65: Measurement: Thermal Electrons Maximum Electron Energy (nadir-facing) | 
SPC shall be capable of measuring thermal electrons in the nadir direction over solar orbital distances of 9.86 Rs to 0.25 AU with a maximum energy of ≥ 1.5 keV. | 
Description/Clarification | 
SWEAP is not required to meet L2 maximum energy requirement in all directions. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. This energy range is needed to observe the thermal electron population & the suprathermal electron population that dominates the heat flux of the solar wind. | SWEAP
Parent Traceability | Functional Allocation
MRD-94 : The Mission shall measure thermal electrons, as follows: -- Energy range1: 5 eV – 20 keV -- Energy resolution: < 20% -- FOV: > 75% of the sky -- Angular resolution2: 10 deg x 10 deg -- VDF cadence: 1 Hz -- Mass resolution3: n/a Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 56: SWEAP Measurements
PAY-192: Measurement: Thermal Electrons Maximum Electron Energy (ram-facing) | 
SPAN-A+ shall be capable of measuring thermal electrons in the ram direction over solar orbital distances of 9.86 Rs to 0.25 AU with a maximum energy of ≥ 20 keV. | 
Description/Clarification | 
SWEAP is not required to meet L2 maximum energy requirement in all directions. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. This energy range is needed to observe the thermal electron population & the suprathermal electron population that dominates the heat flux of the solar wind. | SWEAP
Parent Traceability | Functional Allocation
MRD-94 : The Mission shall measure thermal electrons, as follows: -- Energy range1: 5 eV – 20 keV -- Energy resolution: < 20% -- FOV: > 75% of the sky -- Angular resolution2: 10 deg x 10 deg -- VDF cadence: 1 Hz -- Mass resolution3: n/a Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 57: SWEAP Measurements
PAY-196: Measurement: Thermal Electrons Maximum Electron Energy (anti-ram-facing) | 
SPAN-B shall be capable of measuring thermal electrons in the anti-ram direction over solar orbital distances of 9.86 Rs to 0.25 AU with a maximum energy of ≥ 20 keV. | 
Description/Clarification | 
SWEAP is not required to meet L2 maximum energy requirement in all directions. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. This energy range is needed to observe the thermal electron population & the suprathermal electron population that dominates the heat flux of the solar wind. | SWEAP
Parent Traceability | Functional Allocation
MRD-94 : The Mission shall measure thermal electrons, as follows: -- Energy range1: 5 eV – 20 keV -- Energy resolution: < 20% -- FOV: > 75% of the sky -- Angular resolution2: 10 deg x 10 deg -- VDF cadence: 1 Hz -- Mass resolution3: n/a Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 58: SWEAP Measurements
PAY-66: Measurement: Thermal Electrons Energy Resolution (nadir-facing) | 
SPC shall be capable of measuring thermal electrons in the nadir direction over solar orbital distances of 9.86 Rs to 0.25 AU with an energy resolution dE/E of < 20%. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Energy resolution is needed to determine electron temperature. | SWEAP
Parent Traceability | Functional Allocation
MRD-94 : The Mission shall measure thermal electrons, as follows: -- Energy range1: 5 eV – 20 keV -- Energy resolution: < 20% -- FOV: > 75% of the sky -- Angular resolution2: 10 deg x 10 deg -- VDF cadence: 1 Hz -- Mass resolution3: n/a Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 59: SWEAP Measurements
PAY-193: Measurement: Thermal Electrons Energy Resolution (ram-facing) | 
SPAN-A+ shall be capable of measuring thermal electrons in the ram direction over solar orbital distances of 9.86 Rs to 0.25 AU with an energy resolution dE/E of < 20%. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Energy resolution is needed to determine electron temperature. | SWEAP
Parent Traceability | Functional Allocation
MRD-94 : The Mission shall measure thermal electrons, as follows: -- Energy range1: 5 eV – 20 keV -- Energy resolution: < 20% -- FOV: > 75% of the sky -- Angular resolution2: 10 deg x 10 deg -- VDF cadence: 1 Hz -- Mass resolution3: n/a Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 60: SWEAP Measurements
PAY-197: Measurement: Thermal Electrons Energy Resolution (anti-ram-facing) | 
SPAN-B shall be capable of measuring thermal electrons in the anti-ram direction over solar orbital distances of 9.86 Rs to 0.25 AU with an energy resolution dE/E of < 20%. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Energy resolution is needed to determine electron temperature. | SWEAP
Parent Traceability | Functional Allocation
MRD-94 : The Mission shall measure thermal electrons, as follows: -- Energy range1: 5 eV – 20 keV -- Energy resolution: < 20% -- FOV: > 75% of the sky -- Angular resolution2: 10 deg x 10 deg -- VDF cadence: 1 Hz -- Mass resolution3: n/a Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 61: SWEAP Measurements
PAY-194: Measurement: Thermal Electrons Angular Resolution (ram-facing) | 
SPAN-A+ shall be capable of measuring thermal electrons in the ram direction over solar orbital distances of 9.86 Rs to 0.25 AU with an angular resolution of ≤ 25 degrees about the Spacecraft y-axis and ≤ 10 degrees about the Spacecraft X-Z plane, except when Spacecraft potential is ≤ - TBD V. | 
Description/Clarification | 
SWEAP is not required to meet L2 angular resolution requirement in all directions. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Angular resolution is needed to determine electron temperature anisotropy and to characterize electron beams. | SWEAP
Parent Traceability | Functional Allocation
MRD-94 : The Mission shall measure thermal electrons, as follows: -- Energy range1: 5 eV – 20 keV -- Energy resolution: < 20% -- FOV: > 75% of the sky -- Angular resolution2: 10 deg x 10 deg -- VDF cadence: 1 Hz -- Mass resolution3: n/a Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 62: SWEAP Measurements
PAY-198: Measurement: Thermal Electrons Angular Resolution (anti-ram-facing) | 
SPAN-B shall be capable of measuring thermal electrons in the anti-ram direction over solar orbital distances of 9.86 Rs to 0.25 AU with an angular resolution of ≤ 25 degrees about the Spacecraft y-axis and ≤ 10 degrees about the Spacecraft X-Z plane, except when Spacecraft potential is ≤ - TBD V. | 
Description/Clarification | 
SWEAP is not required to meet L2 angular resolution requirement in all directions. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Angular resolution is needed to determine electron temperature anisotropy and to characterize electron beams. | SWEAP
Parent Traceability | Functional Allocation
MRD-94 : The Mission shall measure thermal electrons, as follows: -- Energy range1: 5 eV – 20 keV -- Energy resolution: < 20% -- FOV: > 75% of the sky -- Angular resolution2: 10 deg x 10 deg -- VDF cadence: 1 Hz -- Mass resolution3: n/a Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 63: SWEAP Measurements
PAY-68: Measurement: Thermal Electrons Velocity Distribution Function (nadir-facing) | 
SPC shall be capable of measuring thermal electrons in the nadir direction over solar orbital distances of 9.86 Rs to 0.25 AU with a VDF measurement cadence of ≥ 1 Hz. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Velocity Distribution Function is needed to resolve structures. | SWEAP
Parent Traceability | Functional Allocation
MRD-94 : The Mission shall measure thermal electrons, as follows: -- Energy range1: 5 eV – 20 keV -- Energy resolution: < 20% -- FOV: > 75% of the sky -- Angular resolution2: 10 deg x 10 deg -- VDF cadence: 1 Hz -- Mass resolution3: n/a Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 64: SWEAP Measurements
PAY-195: Measurement: Thermal Electrons Velocity Distribution Function (ram-facing) | 
SPAN-A+ shall be capable of measuring thermal electrons in the ram direction over solar orbital distances of 9.86 Rs to 0.25 AU with a VDF measurement cadence of ≥ 1 Hz. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Velocity Distribution Function is needed to resolve structures. | SWEAP
Parent Traceability | Functional Allocation
MRD-94 : The Mission shall measure thermal electrons, as follows: -- Energy range1: 5 eV – 20 keV -- Energy resolution: < 20% -- FOV: > 75% of the sky -- Angular resolution2: 10 deg x 10 deg -- VDF cadence: 1 Hz -- Mass resolution3: n/a Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 65: SWEAP Measurements
PAY-199: Measurement: Thermal Electrons Velocity Distribution Function (anti-ram-facing) | 
SPAN-B shall be capable of measuring thermal electrons in the anti-ram direction over solar orbital distances of 9.86 Rs to 0.25 AU with a VDF measurement cadence of ≥ 1 Hz. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Velocity Distribution Function is needed to resolve structures. | SWEAP
Parent Traceability | Functional Allocation
MRD-94 : The Mission shall measure thermal electrons, as follows: -- Energy range1: 5 eV – 20 keV -- Energy resolution: < 20% -- FOV: > 75% of the sky -- Angular resolution2: 10 deg x 10 deg -- VDF cadence: 1 Hz -- Mass resolution3: n/a Notes: 1 Energy range not required in all directions 2 Angular resolution not required in all directions 3 Mass resolution not required in all directions | 

## Slide 66: FIELDS Measurements
PAY-37: Measurement: Magnetic Field MAG | 
MAG shall be capable of measuring 3D vector magnetic fields over solar orbital distances of 9.86 Rs to 0.25 AU as follows: -- frequency range: DC to greater than 100 Hz; -- maximum field intensity: -65000 to +65000 nT; -- cadence: up to 2x the highest frequency in vectors/sec; -- minimum sensitivity (excluding external noise sources) better than: 4 nT in 65000 nT range; 0.1 nT in 1000 nT range; -- accuracy: 5 nT; -- in three orthogonal components. | 
Description/Clarification | 
Maximum field intensity is the maximum expected value, based on HELIOS data, and extrapolating inward for solar orbital distances of 10Rs to 0.25AU. MAG will have multiple ranges to accommodate the dynamic range of expected measurements. Highest sensitivity is available in the lowest range. Sensitivity at higher ranges is limited by 16-bit ADC performance. Cadence is expressed as a peak value, average cadence in data stream will be lower. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Frequency range must include DC, and provide at least a decade overlap with SCM. | FIELDS
Parent Traceability | Functional Allocation
MRD-89 : The Mission shall measure the magnetic field, as follows: -- dynamic range: 140 dB, -- cadence: 100k vectors/sec, -- bandwidth: DC – 50 kHz | 

## Slide 67: FIELDS Measurements
PAY-38: Measurement: Magnetic Field SCM | 
SCM shall be capable of measuring 3D vector magnetic fields over solar orbital distances of 9.86 Rs to 0.25 AU as follows: -- frequency range: 10 Hz to greater than 50 KHz; -- maximum field intensity: 3000nT above noise floor at 3.5kHz; -- cadence: up to 2x the highst frequency in vectors/sec; -- minimum sensitivity (excluding external noise sources) better than: 1 x 10^(-3) nT/sqrt(Hz) at 100 Hz; 1 x 10^(-4) nT/sqrt(Hz) at 3.5 kHz; -- in three orthogonal components. | 
Description/Clarification | 
This is one of two identical requirements that address different Level 2 Mission Science Requirements. This requirement addresses the DC Magnetic Field measurement requirement. Maximum field intensity is the maximum expected value, based on HELIOS data, and extrapolating inward for solar orbital distances of 10Rs to 0.25AU. Minimum sensitivity is 10x the expected noise floor of the sensor, and provides margin for signal processing. Cadence is expressed as a peak value, average cadence in data stream will be lower. Dynamic range, across the spectrum of magnetic field measurements, is greater than 140dB, as required by MRD-89, and demonstrated by this example: SCM rms noise, Ns = sqrt(3500)*1E-4nT = 5.9E-3nT. MAG peak signal, Sm = 2*65000nT Dynamic range = 20*log(Sm/Ns) ≥ 140dB | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. The frequency range spans a decade in common with MAG, and extends up to 50kHz as required in Level 2. | FIELDS
Parent Traceability | Functional Allocation
MRD-89 : The Mission shall measure the magnetic field, as follows: -- dynamic range: 140 dB, -- cadence: 100k vectors/sec, -- bandwidth: DC – 50 kHz | 

## Slide 68: FIELDS Measurements
PAY-170: Measurement: Electric Field | 
EFI shall be capable of measuring 3D vector electric fields over solar orbital distances of 9.86 Rs to 0.25 AU as follows: -- frequency range: DC to 1 MHz; -- maximum field intensity: ±10V/m at DC; ±5V/m at 20kHz; ±1V/m at 1MHz; -- cadence: up to 2x the highest frequency in vectors/sec; -- sensitivity (excluding power converter frequencies and external noise sources) better than: 300 μV/m (TBR) in 10V/m range at DC; 30 μV/m (TBR) in 1V/m range at DC; 1x10^(-7) V/m/sqrt(Hz) at 100kHz; 6x10^(-8) V/m/sqrt(Hz) (TBR) at 1MHz; -- in three orthogonal components in the frequency range 100 kHz – 500 kHz. | 
Description/Clarification | 
This is one of two identical requirements that address different Level 2 Mission Science Requirements. This requirement addresses the DC Electric Field measurement requirement. Maximum field intensity is the maximum expected value, based on extrapolation of HELIOS and 1AU measurements to solar orbital distances of 10Rs to 0.25AU. EFI will have multiple ranges to accommodate the dynamic range of expected measurements. Sensitivity at the higher frequencies is set by requirement to observe shot noise of antennas and galactic thermal noise background. Sensitivity at lower frequencies limited by 16-bit ADC performance. Cadence is expressed as a peak value, average cadence in data stream will be lower. Dynamic range, across the spectrum of electric field measurements, is greater than 140dB, as required in MRD-99, and demonstrated by this example: EFI rms noise in 1kHz measurement BW, Ne = sqrt(1000)*6E-8V/m = 1.9E-6V/m EFI peak signal, Se = 2*10V/m Dynamic range = 20*log(Se/Ne) ≥ 140dB | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Frequency range derives directly from Level 2 requirement. | FIELDS
Parent Traceability | Functional Allocation
MRD-99 : The Mission shall measure the electric field, as follows: -- dynamic range: 140 dB, -- cadence: 2M vectors/sec, -- bandwidth: DC – 1 MHz | 

## Slide 69: FIELDS Measurements
PAY-171: Measurement: Plasma Waves (Magnetic Field SCM) | 
SCM shall be capable of measuring 3D vector magnetic fields over solar orbital distances of 9.86 Rs to 0.25 AU as follows: -- frequency range: 10 Hz to greater than 50 KHz; -- maximum field intensity: 3000nT above noise floor at 3.5kHz; -- cadence: up to 2x the highest frequency in vectors/sec; -- minimum sensitivity (excluding external noise sources) better than : 1 x 10^(-3) nT/sqrt(Hz) at 100 Hz; 1 x 10^(-4) nT/sqrt(Hz) at 3.5 kHz; -- in three orthogonal components. | 
Description/Clarification | 
This is one of two identical requirements that address different Level 2 Mission Science Requirements. This requirement addresses the Plasma Waves requirement. Cadence is expressed as a peak value, average cadence in data stream will be lower. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. | FIELDS
Parent Traceability | Functional Allocation
MRD-103 : The Mission shall measure the plasma waves, as follows: -- dynamic range: 140 dB, -- cadence: 1 spectrum/sec, -- bandwidth: 5 Hz – 1 MHz | 

## Slide 70: FIELDS Measurements
PAY-172: Measurement: Plasma Waves (AC Magnetic Field) | 
SCM shall be capable of measuring AC magnetic field amplitude over solar orbital distances of 9.86 Rs to 0.25 AU as follows: -- frequency range: 1 kHz – 1 MHz; -- maximum field intensity: 6 nT above noise floor at 100 kHz; -- cadence: up to 2M vectors/second; -- sensitivity (excluding power converter frequencies and external noise sources) better than: 1 x 10^(-4) nT/sqrt(Hz) at 10 kHz; 3 x 10^(-5) nT/sqrt(Hz) at 100 kHz; -- one component aligned with one axis of SCM-LF. | 
Description/Clarification | 
The frequency range covers the span of plasma frequencies expected for solar orbital distances of 10Rs to 0.25AU. Cadence is expressed as a peak value, average cadence in data stream will be lower. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. For plasma wave observation, at least one axis of AC magnetic field measurement is necessary to distinguish waves as electrostatic or electromagnetic. | FIELDS
Parent Traceability | Functional Allocation
MRD-103 : The Mission shall measure the plasma waves, as follows: -- dynamic range: 140 dB, -- cadence: 1 spectrum/sec, -- bandwidth: 5 Hz – 1 MHz | 

## Slide 71: FIELDS Measurements
PAY-173: Measurement: Plasma Waves (Electric Field) | 
EFI shall be capable of measuring 3D vector electric fields over solar orbital distances of 9.86 Rs to 0.25 AU as follows: -- frequency range: DC to 1 MHz; -- maximum field intensity: ±10V/m at DC; ±5V/m at 20kHz; ±1V/m at 1MHz; -- cadence: up to 2x the highest frequency in vectors/sec; -- sensitivity (excluding power converter frequencies an dexternal noise sources) better than: 300 μV/m (TBR) in 10V/m range at DC; 30 μV/m (TBR) in 1V/m range at DC; 1x10^(-7) V/m/sqrt(Hz) at 100kHz; 6x10^(-8) V/m/sqrt(Hz) (TBR) at 1MHz; -- in three orthogonal components in the frequency range 100 kHz – 500 kHz. | 
Description/Clarification | 
This is one of two identical requirements that address different Level 2 Mission Science Requirements. This requirement addresses the Plasma Waves requirement. Cadence is expressed as a peak value, average cadence in data stream will be lower. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. | FIELDS
Parent Traceability | Functional Allocation
MRD-103 : The Mission shall measure the plasma waves, as follows: -- dynamic range: 140 dB, -- cadence: 1 spectrum/sec, -- bandwidth: 5 Hz – 1 MHz | 

## Slide 72: FIELDS Measurements
PAY-174: Measurement: Plasma Waves (Magnetic Field Power Spectra) | 
SCM shall be capable of measuring power spectra of AC magnetic fields over solar orbital distances of 9.86 Rs to 0.25 AU as follows: -- frequency range: 10 Hz – 1 MHz; -- cadence: up to 1 spectrum/second. | 
Description/Clarification | 
Cadence is expressed as a peak value, average cadence in data stream will be lower. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Frequency range derives directly from Level 2 requirement. At frequencies above 50kHz, the spectra can be limited to one axis. | FIELDS
Parent Traceability | Functional Allocation
MRD-103 : The Mission shall measure the plasma waves, as follows: -- dynamic range: 140 dB, -- cadence: 1 spectrum/sec, -- bandwidth: 5 Hz – 1 MHz | 

## Slide 73: FIELDS Measurements
PAY-272: Measurement: Plasma Waves (Electric Field Power Spectra) | 
EFI shall be capable of measuring power spectra of AC electric fields from SPP over solar orbital distances of 9.86 Rs to 0.25 AU as follows: -- frequency range: 5 Hz – 1 MHz; -- cadence: up to 1 spectrum/second. | 
Description/Clarification | 
Cadence is expressed as a peak value, average cadence in data stream will be lower. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Frequency range derives directly from Level 2 requirement. | FIELDS
Parent Traceability | Functional Allocation
MRD-103 : The Mission shall measure the plasma waves, as follows: -- dynamic range: 140 dB, -- cadence: 1 spectrum/sec, -- bandwidth: 5 Hz – 1 MHz | 

## Slide 74: FIELDS Measurements
PAY-175: Measurement: Electric Field QTN Spectroscopy | 
EFI shall be capable of measuring QTN Spectroscopy (TNR/HFR Survey Mode) over solar orbital distances of 9.86 Rs to 0.25 AU as follows: -- frequency range: 10 kHz - 2500 kHz; -- dynamic range: 100 dB; -- maximum field intensity: ±200mV/m at 100kHz -- cadence: up to 1 spectrum / 4 seconds; -- sensitivity (excluding power converter frequencies and external noise sources) better than: 1 x 10^(-7) V/m/sqrt(Hz) at 100 kHz; 2 x 10^(-8) V/m/sqrt(Hz) at 2 MHz; -- in one direction. | 
Description/Clarification | 
Maximum field is derived from scaling Type III radio burst intensity inward to SPP solar orbital distances. Sensitivity is derived from requirement to observe shot noise of antennas and galactic thermal noise background. Cadence is expressed as a peak value, average cadence in data stream will be lower. Dynamic range, across the spectrum of QTN measurements, is greater than 100dB, as required in MRD-107, and demonstrated by this example: EFI rms noise in 2kHz measurement BW, Ne = sqrt(2000)*2E-8V/m = 9E-7V/m EFI peak signal, Se = 2*0.2V/m Dynamic range = 20*log(Se/Ne) ≥ 100dB | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Frequency range is derived from expected variation of plasma density for solar orbital distances of 10Rs to 0.25 AU. | FIELDS
Parent Traceability | Functional Allocation
MRD-107 : The Mission shall measure the quasi-thermal noise, as follows: -- dynamic range: 100 dB, -- cadence: 1 spectrum / 4 sec, -- bandwidth: 10 - 2500 kHz | 

## Slide 75: FIELDS Measurements
PAY-176: Measurement: Electric Field Radio Emissions | 
EFI shall be capable of measuring Radio Emissions over solar orbital distances of 9.86 Rs to 0.25 AU as follows: -- frequency range: 1 MHz - 16 MHz; -- dynamic range: 80 dB; -- maximum field intensity: ±100mV/m at 2 MHz -- cadence: up to 1 spectrum/16 sec; -- sensitivity (excluding power converter frequencies and external noise sources) better than: 2 x 10^(-8) V/m/sqrt(Hz) at 2 MHz and above; -- in two orthogonal components. | 
Description/Clarification | 
Maximum field is derived from scaling Type III radio burst intensity for solar orbital distances of 10Rs to 0.25AU. Sensitivity is derived from requirement to observe shot noise of antennas and galactic thermal noise background. Cadence is expressed as a peak value, average cadence in data stream will be lower. Dynamic range, across the spectrum of Radio Emissions measurement, is greater than 80dB, as required in MRD-108, and demonstrated by this example: EFI rms noise in 20kHz BW, Ne = sqrt(20000)*2E-8V/m = 2.8E-6V/m EFI peak signal, Se = 2*0.1V/m Dynamic range = 20*log(Se/Ne) ≥ 100dB | 
Rationale | Requirement Allocation
This requirement meets Level 2 Mission Science Requirements. Frequency range is derived directly from Level 2 requirement. | FIELDS
Parent Traceability | Functional Allocation
MRD-108 : The Mission shall measure radio emissions, as follows: -- dynamic range: 80 dB, -- cadence: 1 spectrum / 16 sec, -- bandwidth: 1 – 16 MHz | 

## Slide 76: System Operability
PAY-99: Payload: Minimum Perihelion | 
All instruments shall be designed to provide science measurements over at least three solar encounter periods with perihelion distance of 9.86 Rs +TBD/-0 Rs from the center of the Sun. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation
MRD-20 : The Mission shall complete at least three orbits with perihelion distance of 9.5 Rs +TBD/-0 Rs from the center of the Sun. | 

## Slide 77: System Operability
PAY-100: Payload: Minimum Perihelion Hours | 
All instruments shall be designed to provide science measurements for at least 920 hours below 20 Rs, with at least 14 hours below 10 Rs. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements, which meets baseline science requirements. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation
MRD-134 : The Mission shall spend 920 hours below 20 Rs, with no less than 14 hours below 10 Rs. | 

## Slide 78: System Operability
PAY-101: Payload: Mission Length | 
All instruments shall be designed to acheive an operational lifetime of at least 7 years after launch. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. The mission is being designed for a lifetime of 7 years for spacecraft, payload, and ground system longevity purposes. This requirement meets a design decision. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation
MRD-22 : The Mission shall achieve minimum perihelion passes within 7 years of launch. | 

## Slide 79: System Operability
PAY-102: Payload: Launch Readiness Calibration | 
All instruments shall be calibrated to meet instrument performance requirements prior to launch. | 
Rationale | Requirement Allocation
This requirement meets a Level 2 Launch Readiness Date Requirement. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation
MRD-23 : The Mission shall be ready to launch in July, 2018. | 

## Slide 80: System Operability
PAY-231: Payload: In-Flight Calibration | 
All instruments shall be designed to accommodate instrument check-out/in-flight calibration. | 
Description/Clarification | 
The term "calibration" is used to refer to in-flight operations so instruments may best prepare for measurement modes during the science campaign. | 
Rationale | Requirement Allocation
Instruments require check-out and in-flight calibration to acheive baseline science requirements. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation

## Slide 81: System Operability
PAY-104: Payload: Risk Category | 
FIELDS shall be single fault tolerant. | 
Rationale | Requirement Allocation
 | FIELDS
Parent Traceability | Functional Allocation
MRD-28 : The Mission shall be designed as a Mission Category 1, per NPR 7120.5D, and Risk Category B mission, as defined in NPR 8705.4 | 

## Slide 82: System Operability
PAY-109: Payload: Burst Mode Management | 
FIELDS shall be responsible for management of its internal burst data buffer. | 
Rationale | Requirement Allocation
This requirement supports Level 2 Burst Mode Requirements. Internal burst data buffer management meets a design desision. | FIELDS
Parent Traceability | Functional Allocation
MRD-29 : The Mission shall be capable of sharing a limited amount of instrument messaging information sufficient for the purposes of coordinating concentrated or focused measurement (burst mode) periods. | 

## Slide 83: System Operability
PAY-110: Payload: Burst Mode Management | 
SWEAP shall be responsible for management of its internal burst data buffer. | 
Rationale | Requirement Allocation
This requirement supports Level 2 Burst Mode Requirements. Internal burst data buffer management meets a design desision. | SWEAP
Parent Traceability | Functional Allocation
MRD-29 : The Mission shall be capable of sharing a limited amount of instrument messaging information sufficient for the purposes of coordinating concentrated or focused measurement (burst mode) periods. | 

## Slide 84: System Operability
PAY-112: Payload: Flight Software Modification | 
All instruments shall be capable of modifying operational flight software and/or change calibration coefficients or tables in response to respective SOC instrument commands. | 
Rationale | Requirement Allocation
This capability is required for anomaly investigations. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation

## Slide 85: Timekeeping
PAY-113: Timekeeping: FIELDS Time Knowledge Accuracy | 
FIELDS shall limit internal instrument timing uncertainty to +/- 2 msec (3-sigma) (TBR) relative to the most recently received Spacecraft time reference. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. | FIELDS
Parent Traceability | Functional Allocation
MRD-34 : The Mission shall ensure that the absolute time knowledge accuracy for measurements made by the FIELDS instruments is to within +/- 1 second (3-sigma) after post-processing on the ground when the spacecraft is within 0.25 AU of the Sun. | 

## Slide 86: Timekeeping
PAY-115: Timekeeping: SWEAP Time Knowledge Accuracy | 
SWEAP shall limit internal instrument timing uncertainty to +/- 2 msec (3-sigma) (TBR) relative to the most recently received Spacecraft time reference. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. | SWEAP
Parent Traceability | Functional Allocation
MRD-36 : The Mission shall ensure that the absolute time knowledge accuracy for measurements made by the SWEAP instruments is to within +/- 1 second (3-sigma) after post-processing on the ground when the spacecraft is within 0.25 AU of the Sun. | 

## Slide 87: Timekeeping
PAY-116: Timekeeping: WISPR Time Knowledge Accuracy | 
WISPR shall limit internal instrument timing uncertainty to +/- 2 msec (3-sigma) (TBR) relative to the most recently received Spacecraft time reference. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. | WISPR
Parent Traceability | Functional Allocation
MRD-37 : The Mission shall ensure that the absolute time knowledge accuracy for measurements made by the WISPR instruments is to within +/- 1 second (3-sigma) after post-processing on the ground when the spacecraft is within 0.25 AU of the Sun. | 

## Slide 88: Timekeeping
PAY-114: Timekeeping: ISIS Time Knowledge Accuracy | 
ISIS shall limit internal instrument timing uncertainty to +/- 2 msec (3-sigma) (TBR) relative to the most recently received Spacecraft time reference. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. | ISIS
Parent Traceability | Functional Allocation
MRD-35 : The Mission shall ensure that the absolute time knowledge accuracy for measurements made by the ISIS instruments is to within +/- 1 second (3-sigma) after post-processing on the ground when the spacecraft is within 0.25 AU of the Sun. | 

## Slide 89: Timekeeping
PAY-117: Timekeeping: Support for Accuracy Verification | 
All instruments shall include provisions to support verification during Observatory I&T that the absolute time accuracy requirements are satisfied. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation
MRD-157 : The Mission shall include provisions to support verification during Observatory I&T that the absolute time accuracy requirements are satisfied. | 

## Slide 90: Data Post-Processing & Delivery
PAY-132: CDH Data Delivery: SDMP | 
All Science Operations Centers shall provide inputs to a NASA Headquarters-approved Science Data Management Plan, as defined in [each instrument's CDRL's, TBR]. | 
Description/Clarification | 
This information is further detailed in the Science Data Management Plan. The verifiable requirement is carried in this document. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation
MRD-66 : The Mission shall create, update and adhere to a NASA Headquarters-approved Science Data Management Plan that specifies file contents, metadata, formats, standards, schedule and pathways for public data access, and the destination of the data upon mission termination. | 

## Slide 91: Data Post-Processing & Delivery
PAY-133: CDH Data Delivery: Quick-Look Data | 
All Science Operations Centers shall provide for public dissemination a quick-look processed version of science data (e.g. thumbnails) within 6 months (TBR) of downlink for the first three orbits after launch and 60 days (TBR) of downlink thereafter. | 
Description/Clarification | 
This information is further detailed in the Science Data Management Plan. The verifiable requirement is carried in this document. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation
MRD-58 : The Mission shall ensure that each SOC provides for public dissemination a quick-look processed version of science data (e.g. thumbnails) within 60 days (TBR) of downlink. | 

## Slide 92: Data Post-Processing & Delivery
PAY-134: CDH Data: Data Sharing | 
All Science Operations Centers shall be capable of sharing data with other SPP instrument teams to support data analysis as specified in the Science Data Management Plan (7434-9101). | 
Description/Clarification | 
This information is further detailed in the Science Data Management Plan. The verifiable requirement is carried in this document. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation
MRD-59 : The Mission shall be capable of sharing data between instrument teams to support data analysis as specified in the Science Data Management Plan (7434-9101). | 

## Slide 93: Data Post-Processing & Delivery
PAY-135: CDH Data: Engineering Data Sharing | 
All Science Operations Centers shall be capable of sharing ancillary engineering information necessary to validate and calibrate science data sets with all investigation teams prior to depositing them in a NASA approved data repository. | 
Description/Clarification | 
This information is further detailed in the Science Data Management Plan. The verifiable requirement is carried in this document. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation
MRD-60 : The Mission shall be capable of sharing ancillary engineering information necessary to validate and calibrate science data sets to all investigation teams prior to depositing them in a NASA approved data repository. | 

## Slide 94: Data Post-Processing & Delivery
PAY-136: CDH Data: Public Dissemination | 
All Science Operations Centers shall provide processed science data obtained as part of the SPP mission to the public no later than 6 months (TBR) from downlink of all a given encounter's data. | 
Description/Clarification | 
This information is further detailed in the Science Data Management Plan. The verifiable requirement is carried in this document. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation
MRD-61 : The Mission shall ensure that each SPP science investigation provides processed science data obtained as part of the SPP mission to the public no later than 6 months (TBR) from downlink of all a given encounter's data. | 

## Slide 95: Data Post-Processing & Delivery
PAY-137: CDH Data Delivery: Data Retention at MOC | 
All Science Operations Centers shall maintain all instrument telemetry & all associated data products throughout the duration of the operational phase of the mission plus one year (TBR). | 
Description/Clarification | 
This information is further detailed in the Science Data Management Plan. The verifiable requirement is carried in this document. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation
MRD-63 : The Mission shall ensure that all instrument telemetry received by the MOC, all associated ancillary data products generated by the ground system, and any processed science data products received by the MOC at any point in the mission life cycle are retained at the MOC throughout the duration of the operational phase of the mission plus one year (TBR). | 

## Slide 96: Data Post-Processing & Delivery
PAY-138: CDH Data Delivery: Data Retention at SOCs | 
All Science Operations Centers shall maintain a data archive of its instrument science, documentation, software and science data products for the life of the mission plus one year (TBR). | 
Description/Clarification | 
This information is further detailed in the Science Data Management Plan. The verifiable requirement is carried in this document. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation
MRD-64 : The Mission shall ensure that each SOC maintains a data archive of its instrument science, documentation, software and science data products for the life of the mission plus one year (TBR). | 

## Slide 97: Data Post-Processing & Delivery
PAY-139: CDH Data Delivery: Data Delivery to NASA | 
All Science Operations Centers shall deliver its data archive from the operational phase of the mission to a NASA-designated location for a deep data archive within 12 months (TBR) of completion of the operational phase of the mission. | 
Description/Clarification | 
This information is further detailed in the Science Data Management Plan. The verifiable requirement is carried in this document. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation
MRD-65 : The Mission shall ensure that each science investigation team delivers their respective data archive from the operational phase of the mission to a NASA-designated location for a deep data archive within 12 months (TBR) of completion of the operational phase of the mission. | 

## Slide 98: Environment
PAY-142: TSA: SPC Thermal Load | 
SPC shall be designed such that the thermal load to the TSA is no more than 25 W and no less than 0 W, including 30% margin. | 
Rationale | Requirement Allocation
This requirement meets thermal constraints on the Spacecraft subsystems. | SWEAP
Parent Traceability | Functional Allocation

## Slide 99: Environment
PAY-143: Cooling System: SPC Thermal Load | 
SPC shall be designed such that the thermal load to the Cooling System is no more than 65 W, including 30% margin. | 
Rationale | Requirement Allocation
This requirement meets thermal constraints on the Spacecraft subsystems. | SWEAP
Parent Traceability | Functional Allocation

## Slide 100: Environment
PAY-144: Spacecraft: SPC Thermal Load | 
SPC shall be designed such that the thermal load to the Spacecraft bus is no more than 0W and no less than 0 W, ±1 W. | 
Rationale | Requirement Allocation
This requirement meets thermal constraints on the Spacecraft subsystems. | SWEAP
Parent Traceability | Functional Allocation

## Slide 101: Environment
PAY-145: TSA: Antennas Thermal Load | 
FIELDS shall be designed such that the thermal load from the antennas to the TSA is no more than 25 W and no less than 0W, including 30% margin (total for all 4 instruments). | 
Rationale | Requirement Allocation
This requirement meets thermal constraints on the Spacecraft subsystems. | FIELDS
Parent Traceability | Functional Allocation

## Slide 102: Environment
PAY-146: Cooling System: Antennas Thermal Load | 
FIELDS shall be designed such that the thermal load from the antennas to the Cooling System is no more than 35 W, including 30% margin (total for all 4 instruments). | 
Rationale | Requirement Allocation
This requirement meets thermal constraints on the Spacecraft subsystems. | FIELDS
Parent Traceability | Functional Allocation

## Slide 103: Environment
PAY-147: Spacecraft: Antennas Thermal Load | 
FIELDS shall be designed such that the thermal load from the antennas to the Spacecraft bus is no more than 6W and no less than 1W, including 30% margin (total for all 4 instruments). | 
Rationale | Requirement Allocation
This requirement meets thermal constraints on the Spacecraft subsystems. | FIELDS
Parent Traceability | Functional Allocation

## Slide 104: Environment
PAY-292: Solar Storm Event Operability | 
All instruments shall be capable of continuing to acquire science data during solar storm events, as defined by Cases TBR in Sections TBR of the EDTRD. | 
Description/Clarification | 
It is understood that the instrument may lose the ability to function during the solar storm, depending on storm intensity, saturation, etc. It is not required that instruments always continue to meet performance requirements (such as signal-to-noise ratio) during these larger storm events. The expected verification activity is Analysis. | 
Rationale | Requirement Allocation
 | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation

## Slide 105: Compliance
PAY-274: Compliance: SPP Instrument Shared Data Document | 
All instruments shall comply with the requirements and constraints imposed by the SPP Instrument Shared Data Document 7434-XXXX. | 
Description/Clarification | 
The SPP Project Office and the science investigations will collaborate to define these requirements. The requirements will be approved per SCS-SPP-005. This requirement will only be verified once relevant requirements in the referenced document are verified. Relevant requirements include (but are not limited to): the capability to share instrument messaging information; the capability to generate and send Instrument Status Packets to the Spacecraft. | 
Rationale | Requirement Allocation
The referenced document contains verifiable requirements that are relevant to instruments. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation
MRD-29 : The Mission shall be capable of sharing a limited amount of instrument messaging information sufficient for the purposes of coordinating concentrated or focused measurement (burst mode) periods. | 

## Slide 106: Compliance
PAY-276: Compliance: General Instrument Specification | 
All instruments shall comply with the requirements and constraints imposed by the General Instrument ICD 7434-XXXX. | 
Description/Clarification | 
The SPP Project Office and the science investigations will collaborate to define these requirements. The requirements will be approved per SCS-SPP-005. This requirement will only be verified once relevant requirements in the referenced document are verified. Relevant requirements include (but are not limited to): a design in accordance with the Spacecraft coordinate system; the capability to receive and react to Spacecraft time & status packets; a design that accommodates real-time communications during instrument commissioning. | 
Rationale | Requirement Allocation
The referenced document contains verifiable requirements that are relevant to instruments. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation
MRD-53 : The Mission shall provide real-time communication during instrument commissioning. MRD-75 : The Mission shall provide a means to recover to an operational state from critical faults. MRD-115 : The Mission shall provide an indicator to instruments prior to firing a thruster. | 

## Slide 107: Compliance
PAY-277: Compliance: FIELDS to SWEAP ICD (FIELDS) | 
FIELDS shall comply with the requirements and constraints imposed by the FIELDS to SWEAP ICD #XXXX. | 
Description/Clarification | 
This requirement will only be verified once relevant requirements in the referenced document are verified. Relevant requirements include (but are not limited to): responsibility for the exchange of synchronized real time data with the SWEAP instrument. | 
Rationale | Requirement Allocation
The referenced document contains verifiable requirements that are relevant to instruments. | FIELDS
Parent Traceability | Functional Allocation
MRD-29 : The Mission shall be capable of sharing a limited amount of instrument messaging information sufficient for the purposes of coordinating concentrated or focused measurement (burst mode) periods. | 

## Slide 108: Compliance
PAY-278: Compliance: FIELDS to SWEAP ICD (SWEAP) | 
SWEAP shall comply with the requirements and constraints imposed by the FIELDS to SWEAP ICD #XXXX. | 
Description/Clarification | 
This requirement will only be verified once relevant requirements in the referenced document are verified. Relevant requirements include (but are not limited to): responsibility for the exchange of synchronized real time data with the FIELDS instrument. | 
Rationale | Requirement Allocation
The referenced document contains verifiable requirements that are relevant to instruments. | SWEAP
Parent Traceability | Functional Allocation
MRD-29 : The Mission shall be capable of sharing a limited amount of instrument messaging information sufficient for the purposes of coordinating concentrated or focused measurement (burst mode) periods. | 

## Slide 109: Compliance
PAY-279: Compliance: FIELDS to Spacecraft ICD | 
FIELDS shall comply with the requirements and constraints imposed by the FIELDS to Spacecraft ICD 7434-9055. | 
Description/Clarification | 
The SPP Project Office and the science investigations will collaborate to define these requirements. The requirements will be approved per SCS-SPP-005. This requirement will only be verified once relevant requirements in the referenced document are verified. Relevant requirements include (but are not limited to): a design with a total internal alignment error as described; the capability to provide real-time instrument health and status data in telemetry formats as described; the capability to provide data to the Spacecraft for downlink in volumes as described; the capability to provide data to the Spacecraft in CCSDS-compliant packets; compliance with maximum mass and power constraints; a design that imparts a torque as described; a design that accommodates FOV obstructions as described; a design that compensates for possible shifts of the Spacecraft TPS prior to launch. | 
Rationale | Requirement Allocation
The referenced document contains verifiable requirements that are relevant to instruments. | FIELDS
Parent Traceability | Functional Allocation
MRD-49 : The Mission shall be capable of supporting real-time commands. MRD-52 : The Mission shall provide an average of 85 (TBR) Gbits of science data per orbit to the ground. MRD-112 : The Mission shall be capable of pointing the spacecraft +z axis to within 3 degrees (TBR) (3-sigma) to the Sun, for FIELDS accuracy, during science measurements, within solar distances less than 0.25 AU. MRD-158 : The Mission shall be capable of determining spacecraft pointing knowledge relative to the Sun center to within 1 degree (TBR) (3-sigma) during FIELDS science data collection, within solar distances less than 0.25 AU. | 

## Slide 110: Compliance
PAY-280: Compliance: SWEAP to Spacecraft ICD | 
SWEAP shall comply with the requirements and constraints imposed by the SWEAP to Spacecraft ICD 7434-9056. | 
Description/Clarification | 
The SPP Project Office and the science investigations will collaborate to define these requirements. The requirements will be approved per SCS-SPP-005. This requirement will only be verified once relevant requirements in the referenced document are verified. Relevant requirements include (but are not limited to): a design with a total internal alignment error as described; the capability to provide real-time instrument health and status data in telemetry formats as described; the capability to provide data to the Spacecraft for downlink in volumes as described; the capability to provide data to the Spacecraft in CCSDS-compliant packets; compliance with maximum mass and power constraints; a design that imparts a torque as described; a design that accommodates FOV obstructions as described; a design that compensates for possible shifts of the Spacecraft TPS prior to launch. | 
Rationale | Requirement Allocation
The referenced document contains verifiable requirements that are relevant to instruments. | SWEAP
Parent Traceability | Functional Allocation
MRD-49 : The Mission shall be capable of supporting real-time commands. MRD-52 : The Mission shall provide an average of 85 (TBR) Gbits of science data per orbit to the ground. MRD-114 : The Mission shall be capable of determining spacecraft pointing knowledge relative to the Sun center to within 1 degree (TBR) (3-sigma) during SWEAP science data collection, within solar distances less than 0.25 AU. | 

## Slide 111: Compliance
PAY-281: Compliance: WISPR to Spacecraft ICD | 
WISPR shall comply with the requirements and constraints imposed by the WISPR to Spacecraft ICD 7434-9057. | 
Description/Clarification | 
The SPP Project Office and the science investigations will collaborate to define these requirements. The requirements will be approved per SCS-SPP-005. This requirement will only be verified once relevant requirements in the referenced document are verified. Relevant requirements include (but are not limited to): a design with a total internal alignment error as described; the capability to provide real-time instrument health and status data in telemetry formats as described; the capability to provide data to the Spacecraft for downlink in volumes as described; the capability to provide data to the Spacecraft in CCSDS-compliant packets; a design that accommodates FOV obstructions as described; compliance with maximum mass and power constraints. | 
Rationale | Requirement Allocation
The referenced document contains verifiable requirements that are relevant to instruments. | WISPR
Parent Traceability | Functional Allocation
MRD-43 : The Mission shall be capable of pointing the WISPR instrument to an accuracy of 6 arcmin (TBR) (3-sigma) relative to WISPR optical z axis and 60 arcmin (TBR) (3-sigma) about the WISPR optical z axis for a spacecraft solar distance <= 0.25 AU. MRD-49 : The Mission shall be capable of supporting real-time commands. MRD-52 : The Mission shall provide an average of 85 (TBR) Gbits of science data per orbit to the ground. MRD-140 : The Mission shall be capable of determining spacecraft pointing knowledge relative to the Sun center to within 1.2 arcmin (TBR) (3-sigma) relative to the WISPR optical z axis and 3.4 arcmin (TBR) (3-sigma) about the WISPR optical z axis. The following image displays the WISPR instrument as defined in Document 7434-XXXX (TBD). In the case of a conflict, Document 7434-XXXX shall take precedence. | 

## Slide 112: Compliance
PAY-282: Compliance: ISIS to Spacecraft ICD | 
ISIS shall comply with the requirements and constraints imposed by the ISIS to Spacecraft ICD 7434-9058. | 
Description/Clarification | 
The SPP Project Office and the science investigations will collaborate to define these requirements. The requirements will be approved per SCS-SPP-005. This requirement will only be verified once relevant requirements in the referenced document are verified. Relevant requirements include (but are not limited to): a design with a total internal alignment error as described; the capability to provide real-time instrument health and status data in telemetry formats as described; the capability to provide data to the Spacecraft for downlink in volumes as described; the capability to provide data to the Spacecraft in CCSDS-compliant packets; a design that accommodates FOV obstructions as described; compliance with maximum mass and power constraints. | 
Rationale | Requirement Allocation
The referenced document contains verifiable requirements that are relevant to instruments. | ISIS
Parent Traceability | Functional Allocation
MRD-49 : The Mission shall be capable of supporting real-time commands. MRD-52 : The Mission shall provide an average of 85 (TBR) Gbits of science data per orbit to the ground. MRD-113 : The Mission shall be capable of pointing the spacecraft +z axis to within 2 degrees (TBR) (3-sigma) to the Sun, for ISIS accuracy, during science measurements, within solar distances less than 0.25 AU. MRD-159 : The Mission shall be capable of determining spacecraft pointing knowledge relative to the Sun center to within 1 degree (TBR) (3-sigma) during ISIS science data collection, within solar distances less than 0.25 AU. | 

## Slide 113: Compliance
PAY-283: Compliance: MOC to SOC ICD | 
All instruments shall comply with the requirements and constraints imposed by the MOC to SOC ICD 7434-9078. | 
Description/Clarification | 
The SPP Project Office and the science investigations will collaborate to define these requirements. The requirements will be approved per SCS-SPP-005. This requirement will only be verified once relevant requirements in the referenced document are verified. Relevant requirements include (but are not limited to): the capability to implement real-time commands via CCSDS packets in files uplinked via CFDP; operations in accordance with described procedures for science operations. | 
Rationale | Requirement Allocation
The referenced document contains verifiable requirements that are relevant to instruments. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation
MRD-49 : The Mission shall be capable of supporting real-time commands. | 

## Slide 114: Compliance
PAY-140: Compliance: EMECP | 
All instruments shall comply with the requirements and constraints imposed by the SPP Electromagnetic Environment Control Plan, 7434-9040. | 
Description/Clarification | 
The SPP Project Office and the science investigations will collaborate to define these requirements. The requirements will be approved per SCS-SPP-005. | 
Rationale | Requirement Allocation
The referenced document contains verifiable requirements that are relevant to instruments. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation
MRD-67 : The Mission shall comply with the requirements and constraints imposed by the SPP Electromagnetic Environment Control Plan, 7434-9040. | 

## Slide 115: Compliance
PAY-141: Compliance: EDTRD | 
All instruments shall comply with the requirements and constraints imposed by the SPP Environmental Design and Test Requirements Document, 7434-9039. | 
Description/Clarification | 
The SPP Project Office and the science investigations will collaborate to define these requirements. The requirements will be approved per SCS-SPP-005. This requirement will only be verified once relevant requirements in the referenced document are verified. Relevant requirements include (but are not limited to): tolerance to Spacecraft reorientation; compliance with solar environment conditions; | 
Rationale | Requirement Allocation
The referenced document contains verifiable requirements that are relevant to instruments. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation
MRD-47 : The Mission shall be capable of supporting instrument and spacecraft component calibration and commissioning activities within sun safety and other operational constraints (TBD). MRD-68 : The Mission shall comply with the requirements and constraints imposed by the SPP Environmental Design and Test Requirements Document, 7434-9039. | 

## Slide 116: Compliance
PAY-148: Compliance: CCP | 
All instruments shall comply with the requirements and constraints imposed by the SPP Contamination Control Plan, 7434-9011. | 
Description/Clarification | 
The SPP Project Office and the science investigations will collaborate to define these requirements. The requirements will be approved per SCS-SPP-005. | 
Rationale | Requirement Allocation
The referenced document contains verifiable requirements that are relevant to instruments. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation
MRD-69 : The Mission shall comply with the requirements and constraints imposed by the SPP Contamination Control Plan, 7434-9011. | 

## Slide 117: Backup

## Slide 118: Instrument Data Sharing
PAY-105: Payload: FIELDS Burst Mode | 
FIELDS shall be capable of sharing a limited amount of instrument messaging information sufficient for the purposes of coordinating concentrated or focused measurement (burst mode) periods, as defined in the SPP Instrument Shared Data Document 7434-XXXX (TBR). | 
Description/Clarification | 
This is a placeholder requirement. It will likely be kept in the SPP Instrument Shared Data Plan. It is being held here currently. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. FIELDS will be participating in Burst Mode data sharing. | FIELDS
Parent Traceability | Functional Allocation

## Slide 119: Instrument Data Sharing
PAY-211: Payload: SWEAP Burst Mode | 
SWEAP shall be capable of sharing a limited amount of instrument messaging information sufficient for the purposes of coordinating concentrated or focused measurement (burst mode) periods, as defined in the SPP Instrument Shared Data Document 7434-XXXX (TBR). | 
Description/Clarification | 
This is a placeholder requirement. It will likely be kept in the SPP Instrument Shared Data Plan. It is being held here currently. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. SWEAP will be participating in Burst Mode data sharing. | SWEAP
Parent Traceability | Functional Allocation

## Slide 120: Instrument Data Sharing
PAY-215: Payload: ISIS Burst Mode | 
ISIS shall be capable of sharing a limited amount of instrument messaging information sufficient for the purposes of coordinating concentrated or focused measurement (burst mode) periods, as defined in the SPP Instrument Shared Data Document 7434-XXXX (TBR). | 
Description/Clarification | 
This is a placeholder requirement. It will likely be kept in the SPP Instrument Shared Data Plan. It is being held here currently. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. ISIS will be participating in Burst Mode data sharing. | ISIS
Parent Traceability | Functional Allocation

## Slide 121: Instrument Data Sharing
PAY-106: Payload: FIELDS Status Packets | 
FIELDS shall be capable of generating and sending CCSDS Instrument Status Packets to the Spacecraft at a rate of 1 packet per second that includes instrument status and shared burst data, as defined in the SPP Instrument Shared Data Document 7434-XXXX (TBR). | 
Description/Clarification | 
This is a placeholder requirement. It will likely be kept in the SPP Instrument Shared Data Plan. It is being held here currently. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. CCSDS is the protocol by which status packets are sent. | FIELDS
Parent Traceability | Functional Allocation

## Slide 122: Instrument Data Sharing
PAY-213: Payload: SWEAP Status Packets | 
SWEAP shall be capable of generating and sending CCSDS Instrument Status Packets to the Spacecraft at a rate of 1 packet per second that includes instrument status and shared burst data, as defined in the SPP Instrument Shared Data Document 7434-XXXX (TBR). | 
Description/Clarification | 
This is a placeholder requirement. It will likely be kept in the SPP Instrument Shared Data Plan. It is being held here currently. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. CCSDS is the protocol by which status packets are sent. | SWEAP
Parent Traceability | Functional Allocation

## Slide 123: Instrument Data Sharing
PAY-216: Payload: ISIS Status Packets | 
ISIS shall be capable of generating and sending CCSDS Instrument Status Packets to the Spacecraft at a rate of 1 packet per second that includes instrument status and shared burst data, as defined in the SPP Instrument Shared Data Document 7434-XXXX (TBR). | 
Description/Clarification | 
This is a placeholder requirement. It will likely be kept in the SPP Instrument Shared Data Plan. It is being held here currently. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. CCSDS is the protocol by which status packets are sent. | ISIS
Parent Traceability | Functional Allocation

## Slide 124: System Operability
PAY-153: Payload: Maximum Mass & Power | 
All instruments shall comply with maximum mass and power constraints as defined in each individual instrument to spacecraft ICD. | 
Description/Clarification | 
This is a placeholder requirement. It will likely be kept in each specific Instrument to Spacecraft ICD. It is being held here currently. | 
Rationale | Requirement Allocation
Compliance with the mass and power NTEs will allow the Spacecraft to acheive launch wet mass capability. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation

## Slide 125: Alignment & Pointing
PAY-118: ADC: Spacecraft Coordinate Frame Definition | 
All instruments shall be designed in accordance with the spacecraft coordinate system as defined in the Solar Probe Plus Spacecraft ICD 7434-0011. The following images display the spacecraft coordinate system as defined in Document 7434-0011. In the case of a conflict, Document 7434-0011 will take precedence. | 
Description/Clarification | 
This is a placeholder requirement. It will likely be kept in each specific Instrument to Spacecraft ICD or in the General Instrument ICD. It is being held here currently until the best reference source is determined. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation
MRD-138 : The Mission shall be designed such that the observatory has a spacecraft coordinate system as defined in Document 7434-0011 Solar Probe Plus Spacecraft ICD. The following images display the spacecraft coordinate system as defined in Document 7434-0011. In the case of a conflict, Document 7434-0011 will take precedence. | 

## Slide 126: Alignment & Pointing
PAY-121: ADC: FIELDS Alignment | 
FIELDS shall be designed such that its total internal alignment error (including contributions for static & dynamic errors) is ≤ TBR, as described in the FIELDS to Spacecraft ICD 7434-9055. | 
Description/Clarification | 
This is a placeholder requirement. It will likely be kept in the specific Instrument to Spacecraft ICD. It is being held here currently. | 
Rationale | Requirement Allocation
 | FIELDS
Parent Traceability | Functional Allocation

## Slide 127: Alignment & Pointing
PAY-125: ADC: SWEAP Alignment | 
SWEAP shall be designed such that its total internal alignment error (including contributions for static & dynamic errors) is ≤ TBR, as described in the SWEAP to Spacecraft ICD 7434-9056. | 
Description/Clarification | 
This is a placeholder requirement. It will likely be kept in the specific Instrument to Spacecraft ICD. It is being held here currently. | 
Rationale | Requirement Allocation
 | SWEAP
Parent Traceability | Functional Allocation

## Slide 128: Alignment & Pointing
PAY-120: ADC: WISPR Alignment | 
WISPR shall be designed such that its total internal alignment error (including contributions for static & dynamic errors) is ≤ TBR, as described in the WISPR to Spacecraft ICD 7434-9057. | 
Description/Clarification | 
This is a placeholder requirement. It will likely be kept in the specific Instrument to Spacecraft ICD. It is being held here currently. | 
Rationale | Requirement Allocation
 | WISPR
Parent Traceability | Functional Allocation

## Slide 129: Alignment & Pointing
PAY-123: ADC: ISIS Alignment | 
ISIS shall be designed such that its total internal alignment error (including contributions for static & dynamic errors) is ≤ TBR, as described in the ISIS to Spacecraft ICD 7434-9058. | 
Description/Clarification | 
This is a placeholder requirement. It will likely be kept in the specific Instrument to Spacecraft ICD. It is being held here currently. | 
Rationale | Requirement Allocation
 | ISIS
Parent Traceability | Functional Allocation

## Slide 130: Alignment & Pointing
PAY-156: ADC: FIELDS torque | 
FIELDS shall impart antenna-derived torques to the Spacecraft associated with antenna geometry and optical properties of TBD +/- TBD, 3-sigma (TBR) to support control of spacecraft Cp-Cg balance, assuming nominal antenna deployments. | 
Description/Clarification | 
This is a placeholder requirement. It will likely be kept in the specific Instrument to Spacecraft ICD. It is being held here currently. | 
Rationale | Requirement Allocation
 | FIELDS
Parent Traceability | Functional Allocation

## Slide 131: Alignment & Pointing
PAY-154: ADC: SPC torque | 
SPC shall impart a torque to the spacecraft associated with SPC geometry and optical properties of TBD +/- TBD, 3-sigma (TBR) to support control of spacecraft Cp-Cg balance. | 
Description/Clarification | 
This is a placeholder requirement. It will likely be kept in the specific Instrument to Spacecraft ICD. It is being held here currently. | 
Rationale | Requirement Allocation
 | SWEAP
Parent Traceability | Functional Allocation

## Slide 132: Alignment & Pointing
PAY-155: ADC: SPC compensation of TPS shift | 
SPC shall include design features (including adjustable bracket length) to compensate for possible shifts of the spacecraft TPS prior to launch, as defined in the SWEAP to Spacecraft ICD. | 
Description/Clarification | 
This is a placeholder requirement. It will likely be kept in the specific Instrument to Spacecraft ICD. It is being held here currently. | 
Rationale | Requirement Allocation
 | SWEAP
Parent Traceability | Functional Allocation

## Slide 133: Commanding & Uplink
PAY-127: CDH: Real-time Commands | 
All instruments shall be capable of implementing real-time commands via CCSDS packets in files uplinked via CFDP, as defined in the MOC-to-SOC ICD 7434-9078. | 
Description/Clarification | 
This is a placeholder requirement. It will likely be kept in the MOC-to-SOC ICD. It is being held here currently. | 
Rationale | Requirement Allocation
This requirement supports the capability to utilize real-time commands during instrument commissioning and off-nominal situations where necessary. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation

## Slide 134: Commanding & Uplink
PAY-128: CDH: MOC Interface | 
All instruments shall operate in accordance with procedures for science operations described in the MOC-to-SOC ICD 7434-9078. | 
Description/Clarification | 
This is a placeholder requirement. It will likely be kept in the MOC-to-SOC ICD. It is being held here currently. | 
Rationale | Requirement Allocation
 | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation

## Slide 135: Data Return & Downlink
PAY-129: CDH: Data Return | 
All instruments shall provide data to the spacecraft for downlink in volumes that are defined by TBD and at transfer rates defined by each individual payload ICD. | 
Description/Clarification | 
This is a placeholder requirement. It will likely be kept in the specific Instrument to Spacecraft ICD. It is being held here currently. | 
Rationale | Requirement Allocation
 | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation

## Slide 136: Data Return & Downlink
PAY-131: CDH: Housekeeping | 
All instruments shall be capable of providing real-time instrument health and status data in telemetry formats specified by each individual payload to spacecraft ICD, when required by mission operations for routine monitoring of housekeeping data and status. | 
Description/Clarification | 
This is a placeholder requirement. It will likely be kept in the specific Instrument to Spacecraft ICD. It is being held here currently. | 
Rationale | Requirement Allocation
 | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation

## Slide 137: Fault Management
PAY-149: FP: Instrument Fault Protection | 
All instruments shall provide data to support instrument fault protection (including ground system monitoring of selected instrument health data, remote SOC notifications of critical fault conditions, and autonomous onboard instrument power-downs in response to instrument request, detection of stale instrument heartbeat, or overcurrent). | 
Description/Clarification | 
This is a placeholder requirement. It will likely be kept in each specific Instrument to Spacecraft ICD or in the General Instrument ICD. It is being held here currently. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation
MRD-72 : The Mission shall provide instrument fault protection to include ground system monitoring of selected instrument health data, remote SOC notifications of critical fault conditions, and autonomous onboard instrument power-downs in response to instrument request and critical telemetry. | 

## Slide 138: Fault Management
PAY-150: FP: Instrument Power-Down Safe State | 
All instruments shall be capable of entering a safe state of powering down upon receipt of a spacecraft-provided bit in the spacecraft status message to request an instrument put itself in a safe state for power down. | 
Description/Clarification | 
This is a placeholder requirement. It will likely be kept in each specific Instrument to Spacecraft ICD or in the General Instrument ICD. It is being held here currently. | 
Rationale | Requirement Allocation
 | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation
MRD-72 : The Mission shall provide instrument fault protection to include ground system monitoring of selected instrument health data, remote SOC notifications of critical fault conditions, and autonomous onboard instrument power-downs in response to instrument request and critical telemetry. | 

## Slide 139: Fault Management
PAY-151: FP: Instrument Power-Down Time | 
All instruments shall be capable of safely powering down within TBD s upon receipt of a status message with a bit indicating power-down command. | 
Description/Clarification | 
This is a placeholder requirement. It will likely be kept in each specific Instrument to Spacecraft ICD or in the General Instrument ICD. It is being held here currently. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation
MRD-72 : The Mission shall provide instrument fault protection to include ground system monitoring of selected instrument health data, remote SOC notifications of critical fault conditions, and autonomous onboard instrument power-downs in response to instrument request and critical telemetry. | 

## Slide 140: Fault Management
PAY-152: FP: Instrument Power-Down Preparedness | 
All instruments shall be designed to accommodate immediate loss of power (without warning) without damage to the instrument. | 
Description/Clarification | 
This is a placeholder requirement. It will likely be kept in each specific Instrument to Spacecraft ICD or in the General Instrument ICD. It is being held here currently. | 
Rationale | Requirement Allocation
This requirement meets Level 2 Requirements. | FIELDS SWEAP WISPR ISIS
Parent Traceability | Functional Allocation
MRD-72 : The Mission shall provide instrument fault protection to include ground system monitoring of selected instrument health data, remote SOC notifications of critical fault conditions, and autonomous onboard instrument power-downs in response to instrument request and critical telemetry. |